## Slide 1: Way Forward on simplified TDL channel model
Huawei, HiSilicon, Spirent, Rohde&Schwarz, Keysight, Ericsson, Intel
3GPP TSG-RAN WG4 Meeting #88-bis R1-1813735
Chengdu, China, 8 – 12 October 2018
Agenda item: 7.13.1.5

## Slide 2: Background
During the online meeting on UE demodulation on Wednesday morning 10th October, it was agreed to make a joint way forward on TDL model simplification procedure and the proposed final models.

## Slide 3: Procedure (1/2)
Step 1: Use the original TDL model from TR38.901.
Step 2: Re-order the taps in ascending delays
Step 3: Perform delay scaling according to the procedure described in section 7.7.3 in TR38.901.
Step 4: Apply the quantization to the agreed delay resolution (5 ns for Rel-15). This is done simply by rounding the tap delays to the nearest multiple of the delay resolution.
Step 5: If multiple taps are rounded to the same delay bin, merge them by calculating their linear power sum.

## Slide 4: Procedure (2/2)
Step 6: If there are more than 12 taps in the quantized model, merge the taps as follows
  Keep first tap [and the last tap*] as such
  Merge two parallel taps with different delays (average delay, sum power) starting from the weakest ones. If the average delay is not in the sampling grid, round up/down it towards the direction of the higher power original tap (e.g. 10 ns & 20 ns  15 ns, 10 ns & 25 ns  20 ns, if 25 ns had higher or equal power; 15 ns, if 10 ns had higher power)
  Continue as long as the final number of taps is 12.
Step 7: round the amplitudes of taps to one decimal (e.g. -8.78 dB  -8.8 dB) Note that the delay spread may have slightly changed due to the tap merge. Adjust the final delay spread by increasing or decreasing the power of the last tap so that the delay spread is corrected.
Step 8: Round the amplitudes of taps to one decimal (e.g. -8.78 dB  -8.8 dB)
Step 9: Re-normalize the highest tap to 0 dB.
*keeping the last tap would ensure that maximum excess delay
is similar to the original model.

## Slide 5: Example
keep
merge (same delay)
merge (same delay)
merge (same delay)
merge (same delay)
merge (same delay)
merge (different delay)
merge (different delay)
merge (same delay)
merge (different delay)
merge (different delay)
50

## Slide 6: Model Tables (1/3)
TDLA30 (editable version in R4-1812328)

## Slide 7: Model Tables (2/3)
TDLB100 (editable version in R4-1812328)

## Slide 8: Model Tables (3/3)
TDLC300 (editable version in R4-1812328)

## Slide 9: Proposals
Proposal #1: The procedure described in this WF is agreed.
Proposal #2: The tables are updated according to the agreed procedure during this meeting.