## Slide 1: A-MPR for intra-band EN-DC
Source: Ericsson
Agenda item: 7.6.4.3.3
Document for: Approval
TSG-RAN Working Group 4 (Radio) meeting #89 R4-1814716
Spokane, WA, USA, 12 – 16 November 2018

## Slide 2: Proposed method
The LTE timeline is kept, the LTE power completely determined by the LTE (MCG) alone
Power back-off is applied on the total transmitted signal relative to PEN-DC,total
Intended for both contiguous and non-contiguous intra-band EN-DC
The A-MPR on the MCG, A-MPRE-UTRA, is determined by the PRB allocation on the MCG alone and the UE determines the Pcmax,c,E-UTRA and the PHRE-UTRA accordingly
The A-MPR of the total transmission power PEN-DC,total, A-MPRtotal, is determined by the PRB allocations on both CGs and the UE determines the resulting PEN-DC,total used for determining if the SCG power should be reduced/dropped
The A-MPR on the SCG, A-MPRNR is set to A-MPRtotal (similar to UL CA for LTE) and the UE determines the Pcmax,c,NR and the PHRNR accordingly
On the SCG: given the PEN-DC,total, the actual UE powers PMCG (known) and PSCG and, the UE reduces the PSCG or drops the SCG

## Slide 3: Timing diagram (same numerology)
PDCCH
PDCCH
PUSCH
PUSCH
n-4
n-1
A-MPR calcuation (MSG and SCG UL SG)
SCG PHR determination
SCG scaling (if needed) based on computed PEN-DC,total
A-MPR calcuation (MSG UL SG)
MCG PHR determination
MCG
SCG
Applies for both intra-band and inter-band EN-DC

## Slide 4: Examples, intra-band contiguous, DC_(n)71AA
Ppowerclass,EN-DC = 23 dBm, DFTS-OFDM, 10 + 10 MHz
Suppose PL estimate the same on both and both PC loops work out required UL power 0 dBm/PRB
10 PRB on LTE and 20 PRB on NR => A-MPRtotal = 7 dB (MPR = 0 dB)
  A-MPRLTE = 1 dB (by 36.101 for B71), A-MPRNR = A-MPRtotal = 7 dB
  PEN-DC, total = Ppowerclass,EN-DC - A-MPRtotal = 16dBm, PMCG = 10 dBm, PSCG = 13 dBm
  No scaling since PMCG + PSCG = 14.7 dBm < PEN-DC, total
10 PRB on LTE and 50 PRB on NR => A-MPRtotal = 5 dB
  A-MPRLTE = 1 dB (by 36.101 for B71), A-MPRNR = A-MPRtotal = 5 dB
  PEN-DC, total = 18 dBm, PMCG = 10 dBm, PSCG = 17 dBm
  No scaling since PMCG + PSCG = 17,8 dBm < PEN-DC, total
10 PRB on LTE and 50 PRB on NR but with 3 dBm/PRB on NR => A-MPRtotal = 5 dB
  A-MPRLTE = 1 dB (by 36.101 for B71), A-MPRNR = A-MPRtotal = 5 dB
  PEN-DC, total = 18 dBm, PMCG = 10 dBm, PSCG = 18 dBm (23 - A-MPRNR reduced from 20 dBm = 3 dBm/PRB + 17)
  NR reduction since PMCG + PSCG = 18.5 dBm > PEN-DC, total , NR reduced to PSCG = PEN-DC, total - PMCG = 17.2 dBm
All computations above internally in the UE
A-MPRtotal table

## Slide 5
Comparison to a proposal by Skyworks made at RAN4#88bis

## Slide 6: Skyworks’ proposal: comparison
The present (”Ericsson”) proposal represented by changes in yellow highlight

## Slide 7: Comparison between proposals
Ppowerclass,EN-DC = 23 dBm, DFTS-OFDM, 10 + 10 MHz
Suppose PL estimate the same on both, PC loops work out required UL power 3 dBm/PRB
Ericsson proposal
10 PRB on LTE and 50 PRB on NR => A-MPRtotal = 5 dB
A-MPRLTE = 1 dB (by 36.101 for B71), A-MPRNR = A-MPRtotal = 5 dB
PEN-DC, total = 18 dBm, PMCG = 13 dBm, computed PSCG = 18 dBm (23 - A-MPRNR reduced from 20 dBm = 3 dBm/PRB + 17 dB)
NR reduction since PMCG + PSCG = 19.2 dBm > PEN-DC, total , NR reduced to PSCG = PEN-DC, total - PMCG = 16.3 dBm
Total power = PMCG + PSCG = PEN-DC, total = 18 dBm,
Skyworks proposal
10 PRB on LTE and 50 PRB on NR => BOeq = A-MPRtotal = 5 dB (PEN-DC, total = 23 dBm in this proposal)
PMCG = PLTE_act = 13 dBm, DBOLTE = 5 - (22-13) = -4 dB. If IMD3 then BONR = 3 dB. PNR_req = 20 dBm (3 dBm/PRB + 17 dB), Pmax_NRampr = 22 – 3 = 19 dBm, Pmax_NRscale = 23 dBm, PSCG = dropped since PNR_req > Pmax_NR = 19 dBm,
Reducing NR to Pmax_NR then PSCG = 19 dBm (modified proposal), total power = PMCG + PSCG = 20 dBm, 2 dB higher than in the Ericsson proposal
  Unwanted emissions may still be met for the power difference between LTE and NR is large (6 dB)

## Slide 8: Comparison: case of dropping
Ppowerclass,EN-DC = 23 dBm, DFTS-OFDM, 10 + 10 MHz
Suppose PL estimate the same on both, PC loops work out required UL power 3 dBm/PRB
Ericsson proposal
30 PRB on LTE and 50 PRB on NR => A-MPRtotal = 5 dB
A-MPRLTE = 1 dB (by 36.101 for B71), A-MPRNR = A-MPRtotal = 5 dB
PEN-DC, total = 18 dBm, PMCG = 18 dBm, computed PSCG = 18 dBm (23 - A-MPRNR reduced from 20 dBm = 3 dBm/PRB + 17 dB)
NR dropped since PMCG = PEN-DC, total
Total power = PMCG = PEN-DC, total = 18 dBm (LTE allocated the required power)
Skyworks proposal
30 PRB on LTE and 50 PRB on NR => BOeq = A-MPRtotal = 5 dB (PEN-DC, total = 23 dBm in this proposal)
PMCG = PLTE_act = 18 dBm, DBOLTE = 5 - (22-18) = 1 dB. If IMD3 then BONR = 5 + 1 dB. PNR_req = 20 dBm (3 dBm/PRB + 17 dB), Pmax_NRampr = 22 – 6 = 16 dBm, Pmax_NRscale = 21.4 dBm
NR dropped since PNR_req > Pmax_NR = 16 dBm,
Reducing NR to Pmax_NR then PSCG = 16 dBm (modified proposal), total power = PMCG + PSCG = 20,1 dBm
  Unwanted emissions met with total back-off around 3 dB? (cf. BOeq = 5 dB)

## Slide 9: Comparison: ”conformance test”
Ppowerclass,EN-DC = 23 dBm, DFTS-OFDM, 10 + 10 MHz
Suppose the UE uses the maximum A-MPR when operated standalone, UP commands sent on both CGs
Ericsson proposal
20 PRB on LTE and 50 PRB on NR => A-MPRtotal = 5 dB
A-MPRLTE = 1 dB (by 36.101 for B71), A-MPRNR = A-MPRtotal = 5 dB
PEN-DC, total = 18 dBm, PMCG = 22 dBm (23 dBm – A-MPRLTE), PSCG dropped, nothing left for power reduction
NR dropped since PMCG > PEN-DC, total
Skyworks proposal
20 PRB on LTE and 50 PRB on NR => BOeq = A-MPRtotal = 5 dB (PEN-DC, total 23 dBm in this proposal)
PMCG = PLTE_act = 22 dBm, DBOLTE = 5 + (22-22) = 0 dB. If IMD3 then BONR = BOeq = 5 dB. PNR_req = 22 dBm, Pmax_NRampr = (22 dBm - BONR) = 17 dBm, PSCG dropped if not scaled (Pmax_NR = Pmax_NRscale = 16 dBm)
NR dropped since PNR_req > Pmax_NR
Reducing NR to Pmax_NR then PSCG = 16 dBm (modified proposal), total power = PMCG + PSCG = 23 dBm
  Unwanted emissions met with no back-off of total signal (cf. BOeq = 5 dB)?

## Slide 10: Skyworks proposal: unwanted emissions
Allows 20 PRB on LTE at 22 dBm and 50 PRB on NR at 16 dBm (previous page)
Simulation1 indicate the B29 limit is violated for DC_(n)71AA, back-off insufficent
NOTE 1: simulation mistakenly with 30 PRB on LTE but would also be allowed at 22 dBm
The ”equal A-MPR” BOeq is based on equal PSD but can allow very different CG power levels: same backoff of total signal for e.g. 1 PRB (LTE) + 50 RRB (NR) and 25 PRB (LTE) + 25 RRB (NR)
Application of DBOLTE (compensation for actual LTE power level) then leads to insufficient power back-off?

## Slide 11: Skyworks and Ericsson proposals
Ericsson proposal more conservative, only based on PRB allocations
Skyworks’ based on actual CG power level, can allow smaller A-MPR and higher NR power
  good for performance, but are the unwanted emissions requirements met?
NR dropping/scaling criterion different:
  Ericsson based on PEN-DC,total with A-MPR (BOeq) applied to the total signal thus reducing PEN-DC,total
  Skyworks dropping if
    the resulting A-MPR (BO) of the NR signal (max power of NR signal)
    or there is not enough remaining NR power after LTE allocation with the total power limited by PEN-DC,total = Ppowerclass, EN-DC
  Modify the Skyworks proposal to allow scaling when the above occurs (Xscale)

## Slide 12: Proposal
Adopt the method on p.2 for both contiguous and non-contiguous intra-band EN-DC
  a general method, A-MPR values can be modified later if beneficial
Use back-off of the total signal for Rel-15
  consider modification of the A-MPR according to the Skyworks proposal as a ”modification of the NR” behaviour in the next release
  can lead to reduced A-MPR for dual (simultaneous) UL