## Slide 1: Motivation for Power Class 2 UE for EN-DC (1 LTE band +1 NR band) CMCC
3GPP TSG-RAN4 #89 R4-1814749
Spokane, WA, USA, 12 - 16 Nov, 2018

## Slide 2: Justification
In order to reduce the big imbalance between 5G NR uplink and downlink coverage, RAN4 has completed PC2 HPUE feature to improve the uplink coverage for 5G SA deployments on NR bands n41, n77, n78 and n79 in Rel-15 NR WI, including PC2 UL MIMO (2Tx 23+23dBm) and PC2 1Tx (26dBm) UE. The following NR bands were approved to support PC2 HPUE for 5G NR SA in Rel-15
Band n41 (2496 – 2690 MHz)：
UL-MIMO (2Tx 23+23dBm) and 1Tx (26dBm) are supported for NR Band n41
Band n77 (3.3 - 4.2 GHz)：
UL-MIMO (2Tx 23+23dBm) and 1Tx (26dBm) are supported for NR Band n77
Band n78 (3.3 - 3.8 GHz)：
UL-MIMO (2Tx 23+23dBm) and 1Tx (26dBm) are supported for NR Band n78
Band n79 (4.4 - 5 GHz)：
UL-MIMO (2Tx 23+23dBm) and 1Tx (26dBm) are supported for NR Band n79
For 5G NR NSA deployment, the imbalance between UL and DL coverage still exists, and the uplink coverage for EN-DC is also need to be improved. Considering the technical status of the industry chain, the Power Class 2 (+26dBm) EN-DC UE should be the most practical and suitable choice to improve the UL coverage for 5G NR NSA deployment
Notes: 600，550

## Slide 3: Justification
It is proposed to specify Power Class 2 UE for EN-DC supporting +26 dBm. This Work Item is to develop a new feature to enable Power Class 2 EN-DC (1 LTE band +1 NR band with 1Tx) UE with +26 dBm maximum output power
For PC2 EN-DC (1 LTE band + 1 NR band), the following PC2 EN-DC for TDD-TDD band combinations are proposed in this Work Item
EN-DC configuration | REL-indep. from | contact name, company | contact email | other supporting companies (min. 3) | status (new, ongoing, completed, stopped)
DC_39A-n41A | Rel-15 | Shao Zhe, CMCC | shaozhe@chinamobile.com | CATT, ZTE, Huawei | New
DC_(n)41AA | Rel-15 | Shao Zhe, CMCC | shaozhe@chinamobile.com | CATT, ZTE, Huawei | New
DC_41A-n41A | Rel-15 | Shao Zhe, CMCC | shaozhe@chinamobile.com | CATT, ZTE, Huawei | New
DC_39A-n79A | Rel-15 | Shao Zhe, CMCC | shaozhe@chinamobile.com | CATT, ZTE, Huawei | New
DC_41A-n79A | Rel-15 | Shao Zhe, CMCC | shaozhe@chinamobile.com | CATT, ZTE, Huawei | New

## Slide 4: Objective
Specify the band combination specific RF requirements for all listed PC2 EN-DC configurations consisting of 2 different bands DL with 2 different bands UL (1 LTE band and 1 NR band) including at least
  Applicable frequencies if necessary
  Applicable bandwidths and bandwidth sets if necessary
  UE requirements, including UE maximum output power, Tx power tolerance, MPR, A-MPR, IBE and ACLR for Power Class 2 EN-DC
  UE Tx duty cycle requirements sufficient to prevent exceeding local regulatory limits such as SAR
  Regulatory issues related to the use of PC2 EN-DC capable devices when roaming and/or p-max absence shall be addressed
  Simultaneous RxTx UE capability for PC2 EN-DC is in scope
The Core Part requirements:

## Slide 5: Objective
Analyse band combinations that have self-desensitization due to following reasons:
  TX Harmonic and/or intermodulation overlap of receive band
  TX signal overlap of receiver harmonic frequency
  TX frequency being in close proximity of one of the receive bands
  Any other identified reasons
For the combination where self-desensitization exists:
  ∆TIB, c and ∆RIB, c
  Reference sensitivity exceptions including MSD test cases
Release independent issue is to be considered for PC2 EN-DC
If needed, the signaling impact due to support of PC2 EN-DC should be discussed in RAN2
Required changes are to be added to release independence TS 38.307
The Perf. Part requirements:

## Slide 6
Thanks