## Slide 1: 3GPP TSG-RAN WG4 Meeting #89 Spokane, US, 12th – 16th November 2018
Huawei, HiSilicon
Way forward on FR2 RRM test
R4-1815183

## Slide 2: Background
Three AoA setups were considered for FR2 RRM test cases
  Setup #1: Single AoA setup with signal arriving in the peak direction of Rx antenna beam
  Setup #2: Single AoA setup with signal arriving not in the peak direction of Rx antenna beam
  Setup #3: Dual AoA setup
In RAN4#88bis, the AoA setup for some RRM test cases are agreed to be setup#1, but AoA setup for other test cases are TBD.
In the agreed Testability WF R4-1814313, two types of RRM test cases are supported
  Type 1 RRM test cases: RRM test cases are designed under assumption that UE is using “fine” UE RX beams
  Type 2 RRM test cases: RRM test case are designed under assumption that UE is using “rough” UE RX beams
  Note: It is up to RRM room to identify which test cases are Type 1 or 2
How to select the tested direction for Setup 2 and 3 is FFS

## Slide 3: AoA setup and fine/rough beam assumption for Phase 1 test cases
TC | Test purpose | AoA setup | Rough/fine beam
1 | EN-DC cell search and L1 measurement period | Setup#3 if two cells are on FR2, otherwise Setup#1 | Rough
2 | SA cell search and L1 measurement period | Setup#3 if two cells are on FR2, otherwise Setup#1 | Rough
3 | EN-DC Timing accuracy and adjustment | Setup#1 | Fine
4 | SA Timing accuracy and adjustment | Setup#1 | Fine
5 | EN-DC TA accuracy | Setup#1 | Fine
6 | SA TA accuracy | Setup#1 | Fine
7 | EN-DC SSB RLM for PSCell IS and OOS | Setup#3 | Fine
9 | SA SSB RLM for PCell IS and OOS | Setup#3 | Fine
10 | Random access | Setup#1 | Rough
11 | Intra-frequency RSRP accuracy for FR1 and FR2 | Setup#1 | Rough
12 | EN-DC SCell activation/deactivation delay | Setup#1 | Rough
13A | EN-DC CSI RLM for PSCell | Setup#3 | Fine
13B | SA CSI RLM for PCell | Setup#3 | Fine
14A | EN-DC interruptions due to DRX transition | Setup#1 | Fine
14B | EN-DC interruptions due to deactivated SCell operations | Setup#1 | Fine
17A | Serving NR PSCell and target E-UTRA inter-frequency measurement with LTE PCell | Setup#1 | Fine
17B | NR Pcell with target inter-RAT E-UTRA measurement | Setup#1 | N/A
18A | EN-DC NR inter-frequency measurement | Setup#3 if two cells are on FR2, otherwise Setup#1 | Rough
18B | SA NR inter-frequency measurement | Setup#3 if two cells are on FR2, otherwise Setup#1 | Rough
19 | Inter-frequency RSRP accuracy for FR1 and FR2 | Setup#1 | Rough
20A | EN-DC interruptions at UL carrier RRC reconfiguration | Setup#1 | Fine
20B | EN-DC interruptions due to active BWP switching | Setup#1 | Fine

## Slide 4: AoA setup and fine/rough beam assumption for Phase 2 test cases
TC | Test purpose | AoA setup | Rough/fine beam
21A | SA interruptions at SCell addition/release/activation/deactivation | Setup#1 | Fine
21B | SA interruptions at UL carrier RRC reconfiguration | Setup#1 | Fine
21C | SA interruptions due to Active BWP switching | Setup#1 | Fine
26A | NR-NR Handovers | Setup#3 if two cells are on FR2, otherwise Setup#1 | Rough
26B | NR handovers to other RATs | Setup#1 | Fine
29A | Beam management: L1-RSRP reporting | Setup#3 | FFS
29B | Beam management: Beam failure detection and link recovery procedure | Setup#3 | BFD fine BFR FFS
31 | Intra-freq RSRQ accuracy for FR1 and FR2 | Setup#1 | Rough
32 | Inter-freq RSRQ accuracy for FR1 and FR2 | Setup#1 | Rough
34 | BWP switching interruptions on E-UTRA serving cells in EN-DC | Setup#1 | Fine
35 | BWP switching delay | Setup#1 | Fine
36 | NR PSCell addition and release in EN-DC | Setup#1 | Rough
37 | UL carrier RRC reconfiguration delay | N/A | N/A
38 | SA RRC_Idle/inactive cell reselection NR to NR (FR1) | N/A | N/A
39 | SA RRC Idle/inactive cell reselection NR to E-UTRAN (FR1) | N/A | N/A

## Slide 5: Test directions
A separate spherical coverage map for rough beams is defined, and for test cases where UE is assumed to use rough beams, the test directions are selected based on this map.
As a starting point, the spherical coverage for rough beam could be defined in a similar way as EIS spherical coverage but based on RSRP instead of throughput.
RAN4 should discuss how to account for the Rx beam gain difference in the two AoA directions in AoA setup #3.
RAN4 should discuss how to account for the difference in the Rx beam gain and direction between fine beam peak and rough beam in AoA setup #1.

## Slide 6: Test mode
Use test mode 1 (TE emulates target SNR conditions) for all RRM test cases.