## Slide 1: Updated simulation assumptions for Rel-15 MTC WUS
Ericsson
3GPP TSG-RAN WG4 Meeting #89 R4-1815444
Spokane, USA, 12 – 16 November 2018
Agenda Item: 6.5.4.1

## Slide 2: WUS simulation assumptions for Rel-15 MTC (1/2)
Parameter | Value
BS TX antenna configuration | 1 Tx, 2 Tx with transmit diversity Note: Tx diversity scheme will depend on RAN1 agreements
UE Rx antenna configuration | 1 Rx
WUS BW | 2 PRBs
Channel model | EPA 1Hz, ETU 1 Hz, EPA 5 Hz, ETU 30 Hz,
SNR | -6 dB, -15 dB
False alarm rate | 1%
Detection probability | 99%
Combining: | Option 1: No combining; Option 2: Coherent combining of 2 consecutive WUS subframes

## Slide 3: WUS simulation assumptions for Rel-15 MTC (2/2)
DRX cycle (s) | Frequency drift [Hz] | Timing drift [us]
0.32 | 44.4 | 4.69006
0.64 | 58.8 | 4.69774
1.28 | 87.6 | 4.72846
2.56 | 145.2 | 4.85134