## Slide 1: Updated simulation assumptions for Rel-15 NB-IoT WUS
Ericsson
3GPP TSG-RAN WG4 Meeting #89 R4-1815446
Spokane, US, 12 – 16 November 2018
Agenda Item: 6.4.4.1

## Slide 2: WUS simulation assumptions for Rel-15 NB-IoT (1/2)
Parameter | Value
BS TX antenna configuration | 1 Tx, 2 Tx with transmit diversity, Note: Tx diversity scheme will depend on RAN1 agreements
UE Rx antenna configuration | 1 Rx
WUS BW | 180 kHz
Channel model | EPA 1Hz, ETU 1 Hz
SNR | -6 dB, -15 dB
False alarm rate | 1%
Detection probability | 99%
Combining | Option 1: No combining; Option 2: Coherent combining of 2 consecutive WUS subframes

## Slide 3: WUS simulation assumptions for Rel-15 NB-IoT (2/2)
DRX cycle (s) | Frequency drift [Hz] | Timing drift [us]
1.28 | 57.6 | 4.0960e-08
2.56 | 115.2 | 1.6384e-07
5.12 | 230.4 | 6.5536e-07
10.24 | 460.8 | 2.6214e-06