## Slide 1: A-MPR Tradeoff of Intra-Band EN-DC
Sprint
R4-1815858
3GPP TSG RAN4 #89
Spokane, WA, USA, November 12-16, 2018
Agenda Item 9.10.2

## Slide 2: Tradeoff Rules Background
Current EN-DC A-MPR definitions for B41/n41 and B71/n71 EN-DC apply backoff to both LTE and NR
Due to legacy LTE scheduling timelines, NR-aware A-MPR applied to LTE is not always possible
To allow adaption of the approved A-MPR to NR-only application, rules for LTE<->NR power trading are needed.
Theory predicts that IMD3 powers from two transmissions are influenced by the following rules:
1 dB change in near transmission power results in 2 dB change in IMD3 power
1 dB change in far transmission power results in 1 dB change in IMD3 power
Empirical measurements from some companies have suggested that real implementation may have closer to 1:1 trade ratios for both sides.
All data suggests that tradeoff ratio is in the range between 2:1 and 1:1, dB for dB.

## Slide 3: Current Definition – Equal A-MPR
LTE
NR
IM3
IM3
Current definition is based on equal A-MPR (equal power) on LTE and NR, and is sufficient to keep IMD3s below the specified limits.
Equal A-MPR
-25 dBm/MHz
-25 dBm/MHz

## Slide 4: NR Side IM3 when LTE power is unused
LTE
NR
IM3
IM3
NR-side IM3 power can be maintained with 1:2 tradeoff rule.
2 dB of unused power on LTE allows 1 dB of extra NR power.
Even if implementation factors mean tradeoff is really closer to 1:1, conservative assumption would still be:
2 dB of unused power on LTE allows 1 dB of extra NR power.
+1 dB
-2 dB
-3 dB
+0 dB
Equal A-MPR
-25 dBm/MHz
-25 dBm/MHz
(-2) + 2 x (+1) = 0
(+1) + 2 x (-2) = -3

## Slide 5: NR Side IM3 when LTE power is excessive
LTE
NR
IM3
IM3
NR-side IM3 power can be maintained with 1:2 tradeoff rule.
2 dB of excess power on LTE requires 1 dB of additional NR backoff.
Care must be taken since LTE-side IM3 will increase by 3 dB
Must still comply with -13 dBm/MHz limit
Therefore, LTE can safely exceed equal limit by only (2/3) * (25-13) = 8 dB.
If LTE exceeds equal limit by more than 8dB, NR should be dropped.
If implementation factors mean tradeoff is really closer to 1:1, conservative assumption would be:
1 dB of excess power on LTE requires 1 dB of extra NR backoff.
-1 dB
+2 dB
+3 dB
+0 dB
Equal A-MPR
-25 dBm/MHz
-25 dBm/MHz
(+2) + 2 x (-1) = 0
(-1) + 2 x (+2) = +3

## Slide 6: LTE Side IM3 when LTE power is unused
LTE
NR
Equal A-MPR
IM3
IM3
-25 dBm/MHz
+2 dB
-1 dB
+3 dB
+0 dB
LTE-side IM3 power can be maintained with 2:1 tradeoff rule.
1 dB of unused power on LTE allows 2 dB of extra NR power.
Care must be taken since NR-side IM3 will increase by 3 dB
Must still comply with -13 dBm/MHz limit
Therefore, NR can safely increase power by only (2/3) * (25-13) = 8 dB.
If implementation factors mean tradeoff is really closer to 1:1, conservative assumption would be:
1 dB of excess power on LTE requires 1 dB of extra NR backoff.
-25 dBm/MHz
(-1) + 2 x (+2) = +3
(+2) + 2 x (-1) = 0

## Slide 7: LTE Side IM3 when LTE power is excessive
LTE
NR
Equal A-MPR
IM3
IM3
-25 dBm/MHz
-2 dB
+1 dB
-3 dB
+0 dB
LTE-side IM3 power can be maintained with 2:1 tradeoff rule.
1 dB of excess power on LTE requires 2 dB of extra NR backoff.
Even if implementation factors mean tradeoff is really closer to 1:1, conservative assumption would still be:
1 dB of excess power on LTE requires 2 dB of extra NR backoff.
-25 dBm/MHz
(+1) + 2 x (-2) = -3
(-2) + 2 x (+1) = 0

## Slide 8: Tradeoff Rules Summary
IM3 of Concern | LTE Power | NR Power Limit 2:1 Trade (Theory) | NR Power Limit 1:1 Trade | Worst Case (Conservative)
NR-side | 1 dB Unused | +0.5 dB | +1 dB | +0.5 dB
 | 1 dB Excessive | -0.5 dB | -1 dB | -1 dB
LTE-side | 1dB Unused | +2 dB | +1 dB | +1 dB
 | 1 dB Excessive | -2 dB | -1 dB | -2 dB

## Slide 9: Potential Benefits of Frequency Awareness
Case | Contig/Non | Curve | Criteria for Case | Potential Tradeoff Optimization
A | Contiguous | -13 dBm/MHz | All IM3s clear of NS_04 | Symmetrical. Must use worst case 1:2 tradeoff
B |  | -25 dBm/MHz | Lower IM3 impacted by NS_04 | NR on lower channel must use 1:2 NR on higher channel could use 1:1
C | Non-Contiguous | -13 dBm/MHz | All IM3s in filter rejection | Difficult – would require further assumptions on filter curve. Should use 1:2 tradeoff
D |  | -25 dBm/MHz | Some IM3s in passband | Could look at which IM3s are in passband. If NR is on side where IM3 are in passband, must use 1:2 Otherwise, NR could use 1:1

## Slide 10: Example Potential Realization in TS 38.101-3
Section 6.2B.3.1.2 and 6.2B.3.2.1 of TS 38.101-3 specify A-MPR for contiguous and non-contiguous NS_04 (B41/n41)
The current definition, for Type 1 UEs is:
A-MPREN-DC = MAX(A-MPRsingle,E-UTRA, A-MPRsingle,NR, A-MPRIM3, A-MPRACLRoverlap )
A-MPRE-UTRA = MAX( A-MPRsingle,E-UTRA+ MPRsingle,E-UTRA, A-MPREN-DC )
A-MPRNR = MAX( A-MPRsingle,NR, A-MPREN-DC )
This could be changed as follows:
A-MPREN-DC = MAX(A-MPRsingle,E-UTRA, A-MPRsingle,NR, A-MPRIM3, A-MPRACLRoverlap )
A-MPRE-UTRA = MAX( A-MPRsingle,E-UTRA + MPRsingle,E-UTRA, A-MPREN-DC )
ΔA-MPRE-UTRA = (PPowerClass – PE-UTRA_act) – A-MPRIM3
A-MPRNR = MAX( A-MPRsingle,NR, A-MPREN-DC – ΔA-MPRE-UTRA * PTF )
Where:
PE-UTRA_act is the actual power-controlled LTE power to be used, and
PTF (Power Trade Factor) is defined in the tables on the following slides

## Slide 11: Contiguous (Using 2:1 Exchange Rate)
Channel Configuration Case | ΔA-MPRE-UTRA | FC,NR – FC,E-UTRA | PTF (NR dB / LTE dB) | Maximum ¦ΔA-MPRE-UTRA¦1
A | ≥ 0 | N/A | 0.5 | TBD
 | < 0 | N/A | 2.0 | TBD
B | ≥ 0 | > 0 | 2.0 | TBD
 |  | < 0 | 0.5 | TBD
 | < 0 | > 0 | 2.0 | TBD
 |  | < 0 | 0.5 | TBD
NOTE 1: If ¦ΔA-MPRE-UTRA¦ > Maximum and ΔA-MPRE-UTRA ≥ 0, then only up to the Maximum dB of E-UTRA power may be traded. If ¦ΔA-MPRE-UTRA¦ > Maximum and ΔA-MPRE-UTRA < 0, NR transmission may be dropped. |  |  |  | 

## Slide 12: Non-Contiguous (Using 2:1 Exchange Rate)
Channel Configuration Case | FC,NR – FC,E-UTRA | Criteria | ΔA-MPRE-UTRA | PTF (NR dB / LTE dB) | Maximum ¦ΔA-MPRE-UTRA¦1
C | N/A | N/A |  | 0.5 | TBD
 | N/A | N/A |  | 2.0 | TBD
D | > 0 | MAX( SEM-13,high, FIM3,high_block,low ) > Ffilter,high | > 0 | 2.0 | TBD
 |  | MAX( SEM-13,high, FIM3,high_block,low ) ≤ Ffilter,high | > 0 | 0.5 | TBD
 | < 0 | FIM3,low_block,high ≥ Ffilter,low | > 0 | 2.0 | TBD
 |  | FIM3,low_block,high < Ffilter,low | > 0 | 0.5 | TBD
 | > 0 | FIM3,low_block,high ≥ Ffilter,low | < 0 | 2.0 | TBD
 |  | FIM3,low_block,high < Ffilter,low | < 0 | 0.5 | TBD
 | < 0 | MAX( SEM-13,high, FIM3,high_block,low ) ≤ Ffilter,high | < 0 | 2.0 | TBD
 |  | MAX( SEM-13,high, FIM3,high_block,low ) > Ffilter,high | < 0 | 0.5 | TBD
NOTE 1: If ¦ΔA-MPRE-UTRA¦ > Maximum and ΔA-MPRE-UTRA ≥ 0, then only up to the Maximum dB of power may be traded. If ¦ΔA-MPRE-UTRA¦ > Maximum and ΔA-MPRE-UTRA < 0, NR transmission may be dropped. |  |  |  |  | 

## Slide 13: Summary
By using information on the arrangement of LTE and NR channels, it can be determined what trade-off exchange rates can be used for trading LTE and NR power from the baseline equal-backoff definition.
Without this channel arrangement consideration, power must always be traded at the worst case exchange rate.
Significant advantage can be taken when:
Managing NR-side IM3s when LTE power is above equal-backoff level
Managing LTE-side IM3s when LTE power is below equal-backoff level
Approach and Table structure could be easily adapted
If empirical data shows trade-off rate at something other than 2:1
If a range of trade-off rates is appropriate, using worst case from range for each row of tables.