## Slide 1: NR Power Scaling
Sprint
3GPP TSG-RAN WG4 #81 R4-1815878
Spokane, USA, 12 – 16 November 2018

## Slide 2: Comment from offline session in
In an offline session on Pcmax at RAN4 #88bis one company remarked that whenever power scaling is allowed NR power can be reduced by Xscale dB.
When challenged on this, they responded that is what the Way Forward from Gold Coast said.
This ppt will attempt to clear up any misperception on what the intent from Plenary was.

## Slide 3: From the agreed Way Forward in RP-182034
The following conditions should be used when improving the RAN4 Inter-band EN-DC Configured Output Power requirements:
  UE is allowed to drop NR only if the power scaling applied to NR means that the difference between scaled and unscaled NR UL power is more than XdB. In other cases the UE does power scaling of NR UL.
    X dB is RRC configured parameter with 4 fixed values and X is [0, 2, 4 or 6] dB. The UE has to be able to support all these 4 configurable X values.
    This threshold X dB does not limit the UE performance but only defines the UE minimum performance (i.e. UE can perform better than the minimum performance)
Handling of partial overlap needs to be addressed (including possibility to leave this up to the UE implementation)
Handling of multiple NR UL carriers needs to be addressed (including possibility to leave this up to the UE implementation)

## Slide 4: From 15 operators in RP-182120
RAN Plenary to send an LS to RAN4 instructing RAN4 to use R4-1811484 as starting point and find a testable way to ensure that NR is not dropped completely unless NR power would have to be scaled down by more than X dB in order to meet the maximum transmit power limits. X is a parameter to be chosen by the operator and configured for their network. RAN1 to be cc-ed on the LS to RAN4.

## Slide 5: Comments on NR power scaling
X dB is the threshold between when NR power scaling must be applied and when NR dropping is allowed, it is not a scaling step size.
They Way Forward does not say that when there is not enough power for both LTE and NR, NR power may automatically be reduced by X dB
RAN4 may decide on the granularity of scaling, but it should not automatically be assumed to be X dB, especially if X dB only has values of 0 or 6 dB.
The idea was that if there is nearly enough power for NR, NR should be transmitted at a slightly lower than optimal power level.
If NR would only have to be lowered by 0.1 dB to keep emissions below PEN-DC_Total, NR power should not be scaled down by 6 dB. A 6 dB reduction or NR power would be almost as bad as dropping, so there would be no point of scaling.