## Slide 1: WF on SFTD measurement requirements
Ericsson, [MediaTek, Intel, Huawei, HiSilicon, ZTE, Nokia, Nokia-Shanghai Bell, …]
R4-1815912
3GPP RAN WG4 Radio #89
Spokane, US, November 12 – 16, 2018

## Slide 2: Background
NE-DC and NR-NR DC features have been added as Rel-15 late drop by RAN#80
RAN4 has earlier, in LS R4-1808442, asked RAN2 for clarification on some SFTD use cases, and is waiting for feedback
In order to progress in the work on SFTD, companies have reviewed the scenarios, and agreed on how they shall be handled
Justifications for scenarios considered not having to be introduced in Rel-15 are captured in LS R4-1811714 to RAN2
RAN#81 decided that RAN4 work on SFTD for NE-DC and NR-NR DC was to be postponed until Q1 2019

## Slide 3: Agreements from RAN4#88
E-UTRA PCell
SFTD between EUTRA PCell and NR neighbor cell, no PSCell configured
SFTD between EUTRA PCell and NR PSCell
SFTD between EUTRA PCell and NR neighbor cell, with NR PSCell configured
NR PCell NE-DC context:
SFTD between NR PCell and EUTRA neighbor cell, no PSCell configured
SFTD between NR PCell and EUTRA PSCell
SFTD between NR PCell and EUTRA neighbor cell, with EUTRA PSCell configured NR-NR DC context:
SFTD between NR PCell and NR inter-frequency neighbor cell, no PSCell configured
SFTD between NR PCell and NR PSCell
SFTD between NR PCell and NR inter-frequency neighbor cell, with NR PSCell configured
Legend
Already in place
Await RAN2 feedback
Requirement needed in Rel 15
Requirement not needed in Rel 15

## Slide 4: For RAN4#90
Companies are encouraged to provide tentative technical solutions and core requirements for:
  SFTD between NR PCell and EUTRA PSCell (NE-DC context)
  SFTD between NR PCell and NR inter-frequency neighbor cell, no PSCell configured (NR-NR DC context)