## Slide 1: Updated simulation assumptions for Rel-15 MTC WUS
Ericsson
3GPP TSG-RAN WG4 Meeting #89 R4-1816089
Spokane, USA, 12 – 16 November 2018
Agenda Item: 6.5.4.1

## Slide 2: WUS simulation assumptions for Rel-15 MTC (1/2)
Parameter | Value
BS TX antenna configuration | 1 Tx, 2 Tx with transmit diversity Note: Tx diversity scheme will depend on RAN1 agreements
UE Rx antenna configuration | 1 Rx
WUS BW | 2 PRBs
Channel model | EPA 1Hz, ETU 1 Hz, EPA 5 Hz, ETU 30 Hz,
SNR | -6 dB, -12< dB
False alarm rate | 1%
Detection probability | 99%
Combining: | Option 1: No coherent combining over multiple subframes; Option 2: Coherent combining of 2 consecutive WUS subframes
Precoder | precoders alternate every 2 WUS subframes for 2 Tx based WUS transmissions

## Slide 3: WUS simulation assumptions for Rel-15 MTC (2/2)
DRX cycle (s) | Frequency drift [Hz] | Timing drift [us]
0.32 | 65.2 | 4.69006
0.64 | 100.4 | 4.69774
1.28 | 170.8 | 4.72846
2.56 | 311.6 | 4.85134