## Slide 1: PCMAX for Inter-band EN-DC
Sprint, BT
Agenda Item 7.6.4.3.1
3GPP TSG-RAN WG4 #81 R4-1815889
Spokane, USA, 12 – 16 November 2018

## Slide 2: Overview
PCMAX_EN-DC usage
Range between PCMAX_ EN-DC _L(p,q) and PCMAX_ EN-DC _L(p,q)
PCMAX_EN-DC_L for time- aligned LTE and NR
PCMAX_EN-DC_L for non-time-aligned LTE and NR
Measurement period for mixed numerology EN-DC
Observations
Proposals

## Slide 3: PCMAX_EN-DC usage
PCMAX for LTE and PCMAX for NR are crucial for LTE and NR operation because they are used for PHR reporting. They referenced in 36.213 and 38.213 respectively.
For EN-DC, PHR is reported per CC, but not per EN-DC band combination.
Because PHR is reported per CC and not reported per EN-DC band combination, PCMAX_EN-DC is not referenced in 38.213, and thus does not seem to be essential for UE operation.
PCMAX_EN-DC can be useful for UE testing, and so the PCMAX_EN-DC should be defined in such a way that it is useful for UE testing

## Slide 4: Range between PCMAX_EN-DC_L and PCMAX_EN-DC_H
When
  10 log10 [pCMAX_ E-UTRA,c (p) +pCMAX,f,c,NR (q) ] = P_EN-DC_Total
  and pCMAX L_ E-UTRA,c (p) = pCMAX_ E-UTRA,c (p)
  and pCMAX L,f,c,NR (q) = pCMAX,f,c,NR (q)
  then NR power scaling or dropping is not allowed
In this case: PCMAX_ EN-DC _L(p,q) = MIN {10 log10 [pCMAX L _ E-UTRA,c (p) + pCMAX L,f,c,,NR c(q)], PEMAX, EN-DC ,PPowerClass, EN-DC}
Or: PCMAX_ EN-DC _L(p,q) = MIN {PEMAX, EN-DC ,PPowerClass, EN-DC}
So: PCMAX_ EN-DC _L(p,q) = PCMAX_ EN-DC _H(p,q)

## Slide 5: Range between PCMAX_EN-DC_L and PCMAX_EN-DC_H
When
  PEMAX, EN-DC < Min{10 log10 [pCMAX_ E-UTRA,c (p) +pCMAX,f,c,NR (q) ], PPowerClass, EN-DC, pCMAX_ E-UTRA,c (p)}
  PCMAX_ EN-DC _L(p,q) = PEMAX, EN-DC
  And PCMAX_ EN-DC _H(p,q) = PEMAX, EN-DC
So this is another case where:
PCMAX_ EN-DC _L(p,q) = PCMAX_ EN-DC _H(p,q)

## Slide 6: Range between PCMAX_EN-DC_L and PCMAX_EN-DC_H
But if
  10 log10 [pCMAX_ E-UTRA,c (p) +pCMAX,f,c,NR (q) ] is slightly higher than P_EN-DC_Total
  then NR power scaling is allowed
In this case, according to the proposed Pcmax proposal:
PCMAX_ EN-DC _L(p,q) = MIN {10 log10 [pCMAX L _ E-UTRA,c (p) + pCMAX L,f,c,,NR c(q) /X_scale ], PEMAX, EN-DC ,PPowerClass, EN-DC}
Where the maximum scaling is applied to the threshold
Observation 1: The scaling in the PCMAX_EN-DC proposal from Chengdu means that PCMAX_EN-DC_L can be much lower when scaling is needed, then when scaling is not needed

## Slide 7: Numerical example: PCMAX_EN-DC_L when scaling is allowed is less than PCMAX_EN-DC_L when scaling is not allowed
PEN-DC_Total = 23 dBm
When
  PCMAX L_E-UTRA = PCMAX_E-UTRA = 20 dBm
  PCMAX L_NR =PCMAX_NR = 19.9 dBm
  PCMAX_EN-DC_L = 23 dBm
When
  PCMAX L_E-UTRA = PCMAX_E-UTRA = 20 dBm
  PCMAX L_NR =PCMAX_NR = 20 dBm
  (the sum is slightly above 23 dBm
  PCMAX_EN-DC_L = 21 dBm
The purpose of scaling is to keep the output power from exceeding 23 dBm, not to allow it be lowered to 21 dBm
Xscale dB | 6 | linear Xs | 3.981072
ENDC |  | Qualcomm | 
Pmax |  | 23 | 199.5262
Ppowrclass |  | 23 | 199.5262
P_EN-DC_Total |  | 23 | 199.5262
LTE |  |  | 
Popwerclass |  | 23 | 199.5262
Pmax |  | 23 | 199.5262
P_LTE |  | 23 | 199.5262
Pcmax_H |  | 23 | 199.5262
Pcmax_L |  | 20 | 100
Pcmax_E-UTRA |  | 20 | 100
NR |  |  | 
Ppowerclass |  | 23 | 199.5262
Pmax |  | 23 | 199.5262
P_LTE |  | 23 | 199.5262
Pcmax_H |  | 23 | 199.5262
Pcmax_L |  | 19.9 | 97.72372
Pcmax_NR |  | 19.9 | 97.72372
 | Scale | a= | FALSE
 | Drop | b= | FALSE
 |  | If !a | 22.96059
 |  | if a!b | 20.95334
 |  | if ab | 20
 |  | Pcmax_L | 22.96059
Xscale dB | 6 | linear Xs | 3.981072
ENDC |  | Qualcomm | 
Pmax |  | 23 | 199.5262
Ppowrclass |  | 23 | 199.5262
P_EN-DC_Total |  | 23 | 199.5262
LTE |  |  | 
Popwerclass |  | 23 | 199.5262
Pmax |  | 23 | 199.5262
P_LTE |  | 23 | 199.5262
Pcmax_H |  | 23 | 199.5262
Pcmax_L |  | 20 | 100
Pcmax_E-UTRA |  | 20 | 100
NR |  |  | 
Ppowerclass |  | 23 | 199.5262
Pmax |  | 23 | 199.5262
P_LTE |  | 23 | 199.5262
Pcmax_H |  | 23 | 199.5262
Pcmax_L |  | 20 | 100
Pcmax_NR |  | 20 | 100
 | Scale | a= | TRUE
 | Drop | b= | FALSE
 |  | If !a | 23
 |  | if a!b | 20.97323
 |  | if ab | 20
 |  | Pcmax_L | 20.97323

## Slide 8: PCMAX_EN-DC_L with scaling for non-overlapped LTE subframes and NR slots
Scaling only needed when pMCG + pSCG > Min(pPowerclass, pEMAX)
If LTE subframes and NR slots were perfectly aligned, when scaling is needed the combined power should be equal to Min(pPowerclass, pEMAX), otherwise scaling would not have been needed
When scaling is applied:
PCMAX_ EN-DC _L(p,q) should be = MIN {PEMAX, EN-DC ,PPowerClass, EN-DC}
If tolerance is needed, RAN4 should agree on the step size or tolerance for scaling and the resulting impact n PCMAX_ EN-DC _L(p,q) , but it should not arbitrarily apply the maximum possible scaling to the lowest pCMAX L,f,c,,NR c(q) as has been proposed in v12 of the Pcmax CR from Chengdu.
Observation 2: RAN4 may need to establish an NR scaling step size or scaling tolerance
E-UTRA (p)
E-UTRA (p+1)
NR (q)
NR (q+1)

## Slide 9: PCMAX_EN-DC_L with overlapping slots
In offline discussions in Chengdu we were told that because of partial overlap of LTE subrames and NR slots, NR power may need to be scaled or dropped for one LTE subfame, even if it would not have been required for the adjacent LTE subframe. E-UTRA (p) may have PCMAX_E-UTRA,c(p) that is high enough to require scaling in NR(q) even though PCMAX_E-UTRA,c(p+1) may be lower such that NR scaling would not be required.
To account for the partial overlap PCMAX,NR (q) may need to be scaled, even if PCMAX L,E-UTRA (p) would not have been high enough to require scaling :
PCMAX_ EN-DC _L(p,q) = MIN {10 log10 [pCMAX L _ E-UTRA,c (p) + pCMAX L,f,c,NR c(q)/X_scale ], PEMAX, EN-DC ,PPowerClass, EN-DC}
Unfortunately, while this threshold is unreasonably low for non-overlapping slots, it is may not be sufficient to account for all overlap scenarios.
E-UTRA (p)
E-UTRA (p+1)
NR (q)

## Slide 10: PCMAX_EN-DC_L with overlapping slots
At the beginning of NR slot q, the UE should set NR power (PSCG(q)) based both on the PMCG(p) as well as PMCG(p+1) to ensure that PEN-DC_Total = Min(PPOWERCLASS, PEMAX) is never exceeded
The proposed equation for PCMAX_EN-DC doesn’t consider that NR(q) may need to be scaled or dropped either due to PCMAX_L_ E-UTRA,c (p) or PCMAX_L_ E-UTRA,c (p+1)
E-UTRA (p)
E-UTRA (p+1)
NR (q)
P_EN-DC_Total
PMCG(p)
PMCG(p+1)

## Slide 11: PCMAX_EN-DC_L with overlapping slots
If the UE chose PSCG(q) only based on PMCG(p), then PEN-DC_Total may be exceeded during the overlap of E-UTRA subframe p+1 and NR slot q, which is not allowed.
Since this behavior is NOT allowed based on 38.213, the equations for PCMAX_EN-DC_L have to consider both E-UTRA subframes that overlap with an NR slot in determining if the power in NR slot q was scaled or dropped.
E-UTRA (p)
E-UTRA (p+1)
NR (q)
P_EN-DC_Total
PMCG(p)
PMCG(p+1)
PSCG(q)

## Slide 12: Potential problem with partially overlapped LTE subframes and NR slots
The proposed equations for PCMAX_EN-DC_L do not consider the adjacent E-UTRA subfames (p-1) and (p+1) when determining if scaling or dropping is required, only E-UTRA subfame p:
PCMAX_L = MIN { PCMAX_ EN-DC _L (p,q) , PCMAX_ EN-DC _L (p,q+1), … , PCMAX_ EN-DC _L (p,q+n)} where PCMAX_EN-DC_L are the applicable lower limits for each overlapping scheduling unit pairs (p,q) , (p, q+1) , up to (p, q+n) for each applicable Teval duration, where q+n is the last NR UL slot overlapping with LTE subframe p,
Even though NR(q) and NR(q+1) don’t need to be scaled or dropped due to PCMAX_EUTRA(p), they may need to be scaled or dropped due to PCMAX_EUTRA(p-1) or PCMAX_EUTRA(p+1)
Observation 3: When an NR slot overlaps with two E-UTRA subframes, the decision to scale or drop in the NR slot depends on the power in each of the E-UTRA subframes that it overlaps with, not just one.
E-UTRA (p)
E-UTRA (p+1)
NR (q)
NR (q+1)
E-UTRA (p-1)

## Slide 13: Potential problem with partially overlapped LTE subframes and NR slots
E-UTRA MPR/A-MPR (p+1) may be very low (and thus, pCMAX_ E-UTRA,c (p+1) very high) so that the equation for dropping NR: b= 10 log10 [pCMAX_ E-UTRA,c (p+1) +pCMAX,f,c,NR (q) /X_scale] > P_EN-DC_Total is true, and NR dropping is allowed for NR(q), even if NR dropping would not be allowed for NR(q) based on pCMAX_ E-UTRA,c (p).
However, the proposed equation for scaling and dropping considers dropping in E-UTRA subframe p and NR slot q through q+n but not NR dropping in slot q due to E-UTRA subframe p+1 (or p-1).
With the proposed equations for PCMAX_EN-DC measured over the 1 ms E-UTRA subframe, a UE could fail the PCMAX tests for subframe p if it could drop NR in slot q and/or slot q+2 due to E-UTRA subframe p+1 and/or p-1, but not scale or drop for subframe p.
Observation 4: A UE could fail PCMAX testing if it had to drop NR due to LTE power in LTE subfames adjacent to subfame p.
E-UTRA (p)
E-UTRA (p+1)
NR (q)
NR (q+1)
E-UTRA (p-1)

## Slide 14: Potential problem with partially overlapped LTE subframes and NR slots – Numerical example
PCMAX_E-UTRA = PCMAX_E-UTRA_L = 20 dBm in subframe p
PCMAX_E-UTRA = PCMAX_E-UTRA_L = 23 dBm in subframe p-1 and p+1
PCMAX_NR = PCMAX_NR_L = 19.9 dBm
No scaling or dropping required/allowed based on (p,q), (p,q+1)
  a= 10 log10 [pCMAX_ E-UTRA,c (p) +pCMAX,f,c,NR (q) ] > P_EN-DC_Total is FALSE
PCMAX_ EN-DC _L(p,q) = MIN {10 log10 [pCMAX L _ E-UTRA,c (p) + pCMAX L,f,c,,NR c(q)], PEMAX, EN-DC ,PPowerClass, EN-DC}= 22.96 dBm
Actual NR power in slot q and slot q+1 is zero milliwatts because of NR dropping due to power in E-UTRA subframe p-1 and p+1.
Average EN-DC power measured over LTE subfame p is 20 dBm, but PCMAX_EN-DC_L = 22.96 dBm, so the UE would fail.
When an NR slot overlaps with two E-UTRA subfames, the decision to scale or drop in the NR slots depends on both of the LTE subfames that it overlaps with, not just one
E-UTRA (p)
E-UTRA (p+1)
NR (q)
NR (q+1)
E-UTRA (p-1)

## Slide 15: Potential solution for partially overlapped LTE subframes and NR slots
Here is one potential equation for PCMAX_ EN-DC _L(q) (PCMAX_ EN-DC _L during NR slot q) when scaling is allowed:
PCMAX_ EN-DC _L(q) = Min(pPowerclass, pemax) –|pCMAX L _ E-UTRA,c (p), pCMAX L _ E-UTRA,c (p+1)|
E-UTRA (p)
E-UTRA (p+1)
NR (q)
P_EN-DC_Total
PMCG(p)
PMCG(p+1)
PSCG(q)

## Slide 16: Measurement period for PCMAX_EN-DC_L with different LTE and NR numerology
NR allocations and thus A-MPR could be different in each NR slot
With measurements only over the 1 ms E-UTRA subframe duration, unless the allocation of every NR slot were the same it would be impossible to tell if the power was as high as it should have been in each slot. If NR A-MPR in NR slot 3 is much higher than the other slots that overlap with E-UTRA subframe p, then the proposed PCMAX_EN-DC_L would be set based on the NR slot 3, but power measured across all of the NR slots that overlap with E-UTRA subframe p
Since the power is measured over the entire E-UTRA slot p there would be no way to tell if the power was high enough in every interval (p,q)
E-UTRA (p)
NR (3)
NR (2)
NR (1)
NR (4)

## Slide 17: Measurement period for PCMAX_EN-DC_L with different LTE and NR numerology
PCMAX_E-UTRA = PCMAX_E-UTRA_L = 20 dBm in subframe p
PCMAX_NR_L in NR slots 1, 2, and 4 is 19.9 dBm, but actual Tx power during EN-DC operation is 18 dBm (1.9 dB below PCMAX_NR_L )
PCMAX_NR_L in NR slot 3 is 17 dBm due to allocations with high A-MPR, but actual transmit power is 15 dBm (2 dB below PCMAX_NR_L )
The average EN-DC power measured over 1 ms is 21.9 dBm
The UE will pass because PCMAX_N-DC_L based on the lowest slot is 21.76 dBm
Even though NR power is too low by 2 dB in every single slot, the UE would pass when averaged over 1 ms.
Observation 5: 1 ms measurement time can allow UEs to pass Pcmax testing even when they should have failed.
E-UTRA (p)
NR (3) fail
NR (2) fail
NR (1) fail
NR (4) fail
Power measured over 1 ms passes!

## Slide 18: PCMAX_EN-DC_L for non-overlapping NR slots when dropping is allowed
The maximum NR power that could ever be dropped is p_CMAX_NR_H / x_scale (linear)
If reducing NR power to p_CMAX_NR_H / x_scale is still not sufficient to keep the total power below p_en-dc_total, then LTE power would have to be at least p_EN-DC_TOTAL - p_CMAX_NR_H / x_scale (linear)
So, when NR is dropped:
PCMAX_EN-DC_L = 10*log10(10Min(Ppowerclass, Pemax)/10 - p_CMAX_NR_H / x_scale)
Proposal 4: When NR is dropped,
PCMAX_EN-DC_L = 10*log10(10Min(Ppowerclass, Pemax)/10 - p_CMAX_NR_H / x_scale)

## Slide 19: Observations
Observation 1: The scaling in the PCMAX_EN-DC proposal from Chengdu means that PCMAX_EN-DC_L can be much lower when scaling is needed, then when scaling is not needed
Observation 2: RAN4 may need to establish an NR scaling step size or scaling tolerance
Observation 3: When an NR slot overlaps with two E-UTRA subframes, the decision to scale or drop in the NR slot depends on the power in each of the E-UTRA subframes that it overlaps with, not just one.
Observation 4: A UE could fail PCMAX testing if it had to drop NR due to LTE power in LTE subfames adjacent to subfame p.
Observation 5: 1 ms measurement time can allow UEs to pass PCMAX testing even when they should have failed.

## Slide 20: Proposals
Proposal 1: Set TREF and measure power over the NR slot duration rather than the LTE subframe duration
Proposal 2: When scaling is allowed, set PCMAX_ EN-DC _L(q) = Min(pPowerclass, pemax) –|pCMAX L _ E-UTRA,c (p) - pCMAX L _ E-UTRA,c (p+1)| when LTE and NR are not aligned, or PCMAX_ EN-DC _L(q) = Min(pPowerclass, pemax) when LTE and NR are aligned.
Proposal 3: Evaluate the EN-DC power over each NR slot q as follows:
While PCMAX_L (q) is computed as follows:
PCMAX_L (q)= MIN { PCMAX_ EN-DC _L (p,q) , PCMAX_ EN-DC _L (p+1,q)}
where PCMAX_EN-DC_L are the applicable lower limits for each overlapping scheduling unit pairs (p,q) , (p+1, q) for each applicable Teval duration, since at most 2 LTE subframes can overlap with NR subframe q, with potential NR scaling and dropping considered.
Proposal 4: When NR is dropped,
PCMAX_EN-DC_L = 10*log10(10Min(Ppowerclass, Pemax)/10 - p_CMAX_NR_H / x_scale)