## Slide 1: WF on OTA OFF power and transient time for FR2
CATT
R4-1816314

## Slide 2: Background
During RAN4#89 meeting, OTA OFF power and transient time was discussed based on [1-8]. However no consensus was reached.
This paper aims to give a WF on how to handle this issue in future meetings.

## Slide 3: Background
Derivation of EIRP OFF power
The relation between EIRP and TRP in the OFF-period can be expressed as,
EIRPOFF=TRPOFF+DOFF
  The following opotions was discussed for DOFF but no consensus reached.
  Option 1: Declare directivity in OFF state
  Option 2: Agree common assumption for directivity in OFF state
    2a The difference between EIRPON and TRPON
    2b Minimum radiator gain for directivity
  Option 3: Use results from static TX OFF measurement to derive the directivity.
  Option 4: Measure OFF level as TRPOFF and transient period based on EIRP
TE vender’s input for Tx off test is that EIRP with Far Field distance is not feasible at RAN4#89. (Keysight, R&S, Anritsu)

## Slide 4: Way Forward
Based on the inputs and discussion, the following options are proposed for further discussion.
  Option a The difference between EIRPON and TRPON is used for DOFF
  Option b Minimum radiator gain or antenna array gain is used for DOFF
  Option c Measure TRP (gated in the near-fieild)
  Option d Show compliance via OTA sensitivity
TE vendors are encouraged to further contribute on test method and testability aspects in RAN4#90. Specifically,
  The noise of the conducted measurement part and dynamic range of TE.
  Test system budget considering far field distance associated path loss and potential errors due to coming closer than EIRP Far Field criteria.
Test procedures for OFF power and transient period in 38.141-2 are removed in RAN4#89 meeting.
Treat this issue under Rel-15 TEI agenda as an exception in future meetings.

## Slide 5: Reference
[1] R4-1814450 Further discussion on FR2 OTA TDD transient time ZTE
[2] R4-1814753 Discussion on OTA TDD transient time for FR2 CATT
[3] R4-1814753 Discussion on OTA TDD transient time for FR2 CMCC
[4] R4-1814888 FR2 OTA transmit ON/OFF power test system concerns Keysight
[5] R4-1815008 TP to 38.141-2: Corrections to co-location requirements Nokia, Nokia Shanghai Bell
[6] R4-1815031 NR BS FR2 TDD transmitter OFF power and transient period NTT DoCoMo
[7] R4-1815315 On test aspects for FR2 TDD OFF power and transient period Ericsson
[8] R4-1815606 Discuss FR2 TX OFF and ON/OFF transient Huawei