## Slide 1: 3GPP TSG-RAN WG4 Meeting #89 Spokane, Washington, USA, 12 – 16 November 2018
Huawei, …
Way forward on General part of NR BS demodulation performance
R4-1816346

## Slide 2: Background
The following WFs were approved:
  R4-1808022 Way forward on general part for NR BS demodulation requirements, RAN4#87
  R4-1809370 Way forward on general parameters for BS demodulation performance requirements, RAN4#AH1807
  R4-1811726 Way forward on general part of NR BS demodulation performance, RAN4#88
  R4-1813755 Way forward on NR BS demodulation general part, RAN4#88Bis

## Slide 3: Test Applicability -1
Different PUCCH formats
  BS is only required to test the PUCCH format(s) declared to support
PUSCH and declared supported PUCCH format(s) tests with different SCS and CBW combinations
  Test all declared SCS, for each declared SCS, BS is required to test on the highest CBW declared.
    If the largest CBW declared is no in the subset with defined performance requirements, BS will be tested on the nearest lower BW (i.e. reference BW) in the subset, the reference BW will be placed in the middle of the channel BW during the test.

## Slide 4: Test Applicability - 2
Different PRACH formats with requirements defined, i.e. short sequence format A1, A2, A3, B4, C0 and C2 and long sequence format 0:
  BS is tested on all preamble formats declared to support, but just choose one of the supported PRACH SCS per FR for each supported PRACH format(s) with short sequence.

## Slide 5: Addition of New Test
No new test cases will be introduced for this meeting, and new requirements for other declared supported configurations shall be introduced after Nov.

## Slide 6: TP drafting
Use the common sub-clause structure for TS 38.141-2 test cases drafting.
TS 38.104 OTA part and TS 38.141-2, "RX antennas" should be replaced with "demodulation branches".

## Slide 7: Phase Noise model
No Phase noise model for FR2 QPSK
Phase Noise model for FR2 16QAM and 64QAM
  FFS whether PN is modelled in FR2 simulation
    Option 1: Yes, and select one of the two PN model options from the TR.
    Option 2: No, and add a certain amount of margin on top of the impairment results provided by companies. The exact margin to be added is up to company’s implementation.