## Slide 1: WF for NR PUSCH demodulation
R4-1816347
Document for: Approval
3GPP TSG-RAN WG4 RAN#89
Spokane, US, 12th – 16th Nov, 2018
Agenda: 7.13.2.2.1
Nokia, Nokia Shanghai Bell, […]

## Slide 2: Background
The following WFs were approved:
  R4-1808024, WF on NR PUSCH demodulation requirements in Rel-15, RAN4#87
  R4-1809366, WF on NR PUSCH demodulation requirements, RAN4#AH1807
  R4-1811694, WF on NR PUSCH demodulation requirements, RAN4#88
  R4-1813942, WF on NR PUSCH demodulation requirements, RAN4#88bis

## Slide 3: DMRS configuration – Infeasible test cases in CP-OFDM 2Tx
Agreement:
  FR1: remove cases with DMRS 1+0 for 2T2R
  FR2: remove cases with MCS16, 2T2R that cannot achieve 70% TPUT performance

## Slide 4: MCS20 only for 1Tx
Agreement
  Keep the previous agreements of defining requirements for 64QAM with 1Tx only.

## Slide 5: PTRS configuration
Agreements
  Default xOverhead value 0 is agreed to use in the TBS calculation for FR2 cases with PT-RS configured.

## Slide 6: DFT-s-OFDM, SCS/BW combination
One SCS/CBW combination per FR
  Agree to test all 4 agreed CBW/SCS combinations,
CBW for FR2 120kHz SCS
    Change CBW from 100MHz to 50MHz for FR2 120kHz SCS

## Slide 7: Test Parameters, CP-OFDM
Parameter | value | 
 | FR1 | FR2
Transform precoding | Disabled | Disabled
Number of Tx | 1, 2 | 1, 2
Number of Rx | 2, 4, 8 | 2
Number of layers | 1, 2 | 1, 2
Transmission scheme | Identity matrix (TPMI index 0) | Identity matrix (TPMI index 0)
DMRS type | type 1 | type 1
Number of DMRS symbols | 1, 1+1 | 1
symbols length | 14 | 10
start symbol index | 0 | 0
Time domain resource allocation type | type A | type B
Frequency domain resource | Full applicable test bandwidth | Full applicable test bandwidth
MCS index | 2, 16, 20 (20 only for 1Tx) | 2, 16, 20 (20 only for 1Tx)
Carrier frequency (GHz) | 4 | 30
Propagation condition | MCS 2: TDL-B 100ns, 400 Hz MCS 16: TDL-C 300ns, 100 Hz MCS 20: TDL-A 30ns, 10Hz | MCS 2: TDL-A 30ns, 300Hz MCS 16: TDL-A 30ns, 300Hz MCS 20: TDL-A 30ns, 75Hz
SCS and BW | 15kHz: 5MHz, 10MHz, 20MHz; 30kHz: 10MHz, 20MHz, 40MHz, 100MHz 60kHz(FR2): 50MHz, 100MHz; 120kHz: 50MHz, 100MHz, 200MHz | 
PTRS | Not configured | Configured with KPTRS =2, LPTRS =1
Timing offset | 0 | 0
Frequency offset | 0 | 0
Code block group, Frequency hopping, Limited buffer rate matching | Disabled | Disabled
Number of HARQ transmissions | 4 | 4
Testing metric | SNR @70% of maximum throughput | SNR @70% of maximum throughput

## Slide 8: Test Parameters, DFT-s-OFDM
Parameter | value | 
 | FR1 | FR2
Transform precoding | enabled | enabled
Number of Tx | 1 | 1
Number of Rx | 2, 4, 8 | 2
Number of layers | 1 | 1
DMRS type | type 1 | type 1
Number of DMRS symbols | 1+1, 1 | 1
symbols length | 14 | 10
start symbol index | 0 | 0
Time domain resource allocation type | type A | type B
Frequency domain resource | 15kHz: 25 PRB; 30kHz: 24 PRB (middle of test BW) | 60kHz: 30 PRB; 120kHz: 30 PRB (middle of test BW)
MCS index | 2 | 2
Carrier frequency (GHz) | 4 | 30
Propagation condition | MCS 2: TDL-B 100ns, 400 Hz MCS 16: TDL-C 300ns, 100 Hz MCS 20: TDL-A 30ns, 10Hz | MCS 2: TDL-A 30ns, 300Hz MCS 16: TDL-A 30ns, 300Hz MCS 20: TDL-A 30ns, 75Hz
SCS and BW | 15kHz: 5 MHz; 30kHz: 10 MHz | 60kHz: 50; 120kHz: 50
PTRS | Not configured | NRB0=0, NRB1=8, NRB2=NRB3=32, and NRB4=108
Timing offset | 0 | 0
Frequency offset | 0 | 0
Code block group, Frequency hopping, Limited buffer rate matching | Disabled | Disabled
Number of HARQ transmissions | 4 | 4
Testing metric | SNR @70% of maximum throughput | SNR @70% of maximum throughput