## Slide 1: 3GPP TSG-RAN WG4 Meeting #89 Spokane, Washington, USA, 12 – 16 November 2018
Huawei, …
Way forward on NR PUCCH demodulation performance in Rel-15
R4-1816348

## Slide 2: Background
R4-1808025 Way forward on PUCCH demodulation requirements, RAN4#87
R4-1809556 Way forward for NR PUCCH demodulation performance requirements, RAN4#1807
R4-1811727 Way forward for NR PUCCH demodulation performance requirements, RAN4#88
R4-1813943 Way forward on NR PUCCH demodulation requirements, RAN4#88Bis

## Slide 3: Background
Hopping
  Intra-slot frequency hopping: enable
    startingPRB = 0
    secondHopPRB = the largest PRB index – nrofPRBs
  hoppingId = 0

## Slide 4: Time mask impact
Further investigation is needed to check the performance impact due to UE transient period when frequency hopping enabled for 60kHz SCS for FR1 and 120kHz SCS for FR2.
FFS: whether frequency hopping enabled is needed or not for PUCCH performance with 120kHz SCS considering the time mask impact to the PUCCH performances.

## Slide 5: Simulation assumption for format 2
Test metric
  If number of bits <= 11
    DTX to Ack probability <1% and Missed Ack probability < 1%
  If number of bits > 11: BLER < 1%

## Slide 6: Initial Simulation Assumptions
Parameters |  | PUCCH Format 0 | PUCCH Format 1 | PUCCH Format 2 | PUCCH Format 3 | PUCCH Format 4 | 
BandWidth/SCS |  | FR1: 10MHz/15kHz; 40MHz/30kHz; FR2: 100MHz/60kHz; 100MHz/120kHz |  |  |  |  | 
Antenna |  | 1T2R, 1T4R and 1T8R for FR1; 1T2R for FR2 |  |  |  |  | 
Propagation condition |  | FR1: : TDLC300-100; FR2: TDLA30-300 |  |  |  |  | 
Carrier frequency (GHz) |  | FR1: 4GHz; FR2: 30GHz |  |  |  |  | 
(#Bits, #Symbols, #PRBs) |  | (1, 1, 1) (1, 2, 1) | (2, 14,1) | (4, 1, 4) (22, 2, 9) | (16, 14, 1) (16, 4, 3) |  | (22, 14, 1)
DMRS pattern |  |  |  |  | FR1: Without additional DMRS for all cases With additional DMRS for cases with the number of OFDM symbols more than 9 FR2: Without additional DMRS |  | 
Modulaiton |  |  |  | QPSK | QPSK |  | QPSK
initialCyclicShift |  | 0 | 0 |  |  |  | 
StartingSymbolIndex |  | 13 for 1 symbol; 12 for 2 symbols; | 0 | 13 for 1 symbol; 12 for 2 symbols; | 0 |  | 0
Index of orthogonal sequence (time-domain-OCC) |  |  | 0 |  |  |  | 
occ-Length |  |  |  |  |  |  | n2
occ-Index |  |  |  |  |  |  | n0
Test metric | DTX to Ack probability <1% | √ | √ | √ for bits <=11 | × |  | ×
 | Missed Ack probability < 1% | √ | √ | √ | × |  | ×
 | NACK2ACK < 0.1% | × | √ | × | × |  | ×
 | BLER < 1% | × | × | √ for bits >11 | √ |  | √