## Slide 1: 3GPP TSG-RAN WG4 Meeting #89 Spokane, Washington, USA, 12 – 16 November, 2018
Huawei, HiSilicon, …
Way forward on 8Rx demodulation and CSI tests
R4-1816383

## Slide 2: Applicability rule - Control and Data Channel
For 8Rx capable UEs without any 2Rx supported RF but with 4Rx supported RF bands:
  For all test cases specified in 8.2 to 8.8 for control channel with 2Rx
    UE is tested on any of the 4Rx supported RF bands, where the SNR requirements specified with 2Rx should be tightened by 1.5dB
  All single carrier tests specified in 8.2 to 8.8 with 2Rx for PDSCH are tested on
    Any of the 4Rx supported RF bands by duplicating the fading channel from each Tx antenna and add independent noise for each Rx antenna as 2x2 or 4x2
    SNR requirement specified with 2Rx should be tightened by 1.5dB

## Slide 3: PDSCH demodulation performance tests
Introduce 8Rx demodulation test(s)
  TM9
  Rank 8
  16QAM
  EPA5
  Duplex mode
    TDD

## Slide 4: CA test
Simulation is needed for the largest bandwidth 20MHz+20MHz for CA combinations

## Slide 5: SDR test -1
64QAM
  Rank: 8
  Tx EVM: 6%
  MCS 24
256QAM
  Rank: 8
  Tx EVM: 3%
  MCS21

## Slide 6: SDR test -2
Test applicability rule for SDR test with 2/4 Rx:

## Slide 7: CQI test
CQI reporting definition under AWGN
  TM9 rank 4