## Slide 1: Way forward on NR UE PDSCH demodulation requirements and General aspects
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #89
Spokane, USA, 12 – 16 November 2018 Agenda Item: 7.13.1.2
R4-1816388

## Slide 2: EN-DC performance requirements
Issue 1: Handling of simultaneous Tx/Rx for EN-DC
  EN-DC test parameters
      Transmissions on the LTE and NR carriers are synchronous (i.e. aligned on subframe boundaries)
      TDD-TDD EN-DC LTE configuration
        Use LTE TDD DL-UL configuration 2
        LTE frame is shifted by 2 SF’s to the right with respect to the start of NR frame

## Slide 3: EN-DC performance requirements
Issue 2: Handing of FR1 EN-DC test cases of NR TDD DL-UL configurations not aligned with LTE
  FR1 EN-DC test cases with NR TDD DL-UL configurations not aligned with LTE can be tested on the corresponding EN-DC BCs where UE supports simultaneous Tx/Rx

## Slide 4: EN-DC performance requirements
Issue 3-1 : EN-DC including FR2 carrier requirements (both SDR and normal test cases)
  Normal demodulation requirements: no requirements for FR1 NR/LTE carriers for Rel-15 EN-DC test cases including FR2 carrier.
  SDR requirements: Define requirements for FR1 NR/LTE carriers of Rel-15 EN-DC SDR test cases which including FR2 carrier. Only FR2 performance is tested in Rel-15.

## Slide 5: Requirements Applicability
Issue 1-1 : Applicability rules for SA and NSA of normal test cases
  For UE’s that support both NSA and SA: Normal UE demodulation requirements are verified using SA requirements only
Issue 1-2 : Applicability rules for SA and NSA of SDR Test cases
  For UE’s that supports both NSA and SA: SDR requirements tested for both SA and NSA

## Slide 6: Requirements Applicability
Issue 2: applicability rules for 2Rx and 4Rx
  For UE’s that support 4RX on at least one band, the normal UE performance requirements are verified using 4RX tests and 2RX tests can be skipped.

## Slide 7: PDSCH
Issue 1: Additional soft buffer test for PDSCH mapping type A
  Previous agreement
    Requirement with 70% test point and 8 HARQ process for FDD and 16 HARQ process for TDD: (FFS whether needed or not)
      Option 1: No tests
      Option 2 (simulation purpose)
        MCS #19 and rank 2 for FR1, FDD and TDD (7D1S2U) for both 2Rx and 4Rx
        MCS #13 and rank 2 (2Rx) for TDD (DDDSU) FR2
      Other options not excluded
      Interested companies are encourage to bring more analysis with simulation results to further decide the necessity of introducing such test cases in next RAN4 meeting.
  Proposal:
    Option 1: No Test (Intel, QC)
    Option 2: Have test cases for normal test cases meanwhile for SDR test using 8 HARQ for TDD and 4 for FDD (NTT DoCoMo, Huawei)

## Slide 8: PDSCH
Issue 2: LTE-NR co-existence test case (duration length)
  Previous agreements:
    PDSCH Type A
    Start symbol (S): 3
    Duration (L): [9 or 11]
      Note: Use 11 if RAN1 agreement on changes of additional DMRS position for Type A is confirmed
    Number of additional DMRS: 1
    Duplex mode: FDD only
    FRC: MCS4 Rank 1 for 2Rx and 4 Rx
    Overhead for TBS determination: 18
  Proposals
    Option 1: Introduce both test cases for duration 9 and 11. (E///, Intel, QC, AT&T)
    Option 2: Introduce test cases for time duration 9. Further discuss additional requirements for symbol duration 11

## Slide 9: PDSCH
Issue 3: Dynamic TDD DL-UL configuration test
  Option 1: Use dynamic UL/DL determination for some existing PDSCH demodulation test case(s).
  Option 2: Do not define test

## Slide 10: PDSCH
Issue 4: CSI-RS for UE RX beam refinement
  Configure CSI-RS for UE Rx Beam refinement purpose during test, whether UE using this or not for Rx Beam refinement pending on UE capability and implementation.
  NZP CSI-RS configuration for BM:
    1 port
    2 resources
    Periodicity 20 ms
    Offset 0
    Repetition ON
    Subcarrier index: 0
    OFDM symbol:
      Resource 1: 8, Resource 2: 9, (note: no collision with SSB or CSIRS for CSI acquisition)
    Density [3]
    No CDM
Notes: Offline for CSI-RS parameters configurations

## Slide 11: PDSCH
Issue 5: SNR requirements derivation
  Plan for deriving performance requirements (SNR points)
    Define tentative SNR requirements for the agreed test cases as much as possible
    Updating TPs including SNR requirements for test cases with []
    The agreed SNR values still can be updated if more results collected from companies in future meeting or technical issues identified
    Keep requirements TBD for FR2 64QAM cases , decide the SNR values with more results from companies in RAN4#90 , IM results submitted from companies should take PN impact into account.
  SNR = average of IM results among companies +extra margin
  For test cases which the span among companies’ results within [2dB], using the same extra margin values and the test cases with larger span further checking the details of simulation assumption and extra margin cases by cases
  Default margin values:
    0.5dB for QPSK, 16QAM and 0.8 dB for 64QAM and 25QAM

## Slide 12: PDSCH
Issue 6: New test cases for follow PMI for TDD configuration of DDDSU for FR2.
  Introduce one additional PMI test case based on DDDSU for FR2 120kHz
  Do not introduce follow PMI PDSCH demodulation test cases