## Slide 1: WF on SDR requirement
NTT DOCOMO
3GPP TSG-RAN WG4 Meeting RAN4#89 R4-1816389
Spokane,USA, 12 -16 Nov, 2018

## Slide 2: Number of HARQ process
Previous agreements
  FFS: 8/4 processes for TDD/FDD soft combining verification test with 16/8 process for TDD/FDD
Proposal:
  Option 1：If normal PDSCH demodulation requirement with 16 (TDD)/8 (FDD) HARQ processes targeting for higher Rank/MCS are introduced, the number of HARQ process for SDR test is 8 (TDD) / 4 (FDD)； Otherwise, 16 (TDD) / 8 (FDD) processes
  Option 2: 8 for TDD and 4 for FDD
Notes: O

## Slide 3: TDD pattern for FR2 120kHz
Previous agreements:
  NR TDD configuration for FR2 120kHz
    Alt.1: DDDSU
    Alt.2: DDSU
Proposal
  DDDSU

## Slide 4: PDSCH scheduling for TDD
Proposal
  Skip scheduling PDSCH in special slots
Notes: Intel: simulation based on full DL slots

## Slide 5: MCS levels and tables 1/3
Previous agreement
  MCS/TBS determination
    Adopt the methodology in Section 2.1 of R4-1812165
  Companies are encouraged to provide simulation results with the following two MCS conditions
    The highest MCS based on UE capability without any restriction of testable SNR
    The highest MCS achieved within testable SNR range in Rel.15
Proposal
  Define SDR test cases for the following two MCS levels
    : The higher MCS according to UE capability calculated by Sec. 2.1 of R4-1812165
    : The highest practical MCS considering feasible SNR levels
  Conduct SDR test by
  Adopt look up table in the next slide for FR1 SDR test
  Note: keep as TBD in this meeting, companies are encouraged to bring evaluation to decide the values .
  Keep with [].
Notes: What’s the method for patricidal MCS? Pending on UE implementation ?
More time to check the values in tables. (QC, Ericsson)

## Slide 6: MCS levels and tables 2/3
UE capability index |  |  |  |  | 
1 | 1 | 8 | 1 | 26 [27] | 26 [27]
2 | 1 | 8 | 0.8 | [21] | 
3 | 1 | 8 | 0.75 | [20] | 
4 | 1 | 8 | 0.4 | [11] | 
5 | 1 | 6 | 1 | 27[28] | 27[28]
6 | 1 | 6 | 0.8 | [23] | 
7 | 1 | 6 | 0.75 | [22] | 
8 | 1 | 6 | 0.4 | [14] | 
9 | 1 | 4 | 1 | [16] | [16]
10 | 1 | 4 | 0.8 | [16] | 
11 | 1 | 4 | 0.75 | [16] | 
12 | 1 | 4 | 0.4 | [10] | 
13 | 1 | 2 | 1 | [9] | [9]
14 | 1 | 2 | 0.8 | [9] | 
15 | 1 | 2 | 0.75 | [9] | 
16 | 1 | 2 | 0.4 | [4] | 
17 | 2 | 8 | 1 | 27[28] | [26]
18 | 2 | 8 | 0.8 | [21] | 
19 | 2 | 8 | 0.75 | [20] | 
20 | 2 | 8 | 0.4 | [11] | 
21 | 2 | 6 | 1 | 27[28] | 27[28]
22 | 2 | 6 | 0.8 | [23] | 
23 | 2 | 6 | 0.75 | [22] | 
24 | 2 | 6 | 0.4 | [14] | 
25 | 2 | 4 | 1 | [16] | [16]
26 | 2 | 4 | 0.8 | [16] | 
27 | 2 | 4 | 0.75 | [16] | 
28 | 2 | 4 | 0.4 | [10] | 
29 | 2 | 2 | 1 | [9] | [9]
30 | 2 | 2 | 0.8 | [9] | 
31 | 2 | 2 | 0.75 | [9] | 
32 | 2 | 2 | 0.4 | [4] | 
UE capability index |  |  |  |  | 
33 | 4 | 8 | 1 | [27] | [26]
34 | 4 | 8 | 0.8 | [22] | 
35 | 4 | 8 | 0.75 | [21] | 
36 | 4 | 8 | 0.4 | [12] | 
37 | 4 | 6 | 1 | [28] | [28]
38 | 4 | 6 | 0.8 | [24] | 
39 | 4 | 6 | 0.75 | [23] | 
40 | 4 | 6 | 0.4 | [14] | 
41 | 4 | 4 | 1 | [16] | [16]
42 | 4 | 4 | 0.8 | [16] | 
43 | 4 | 4 | 0.75 | [16] | 
44 | 4 | 4 | 0.4 | [11] | 
45 | 4 | 2 | 1 | [9] | [9]
46 | 4 | 2 | 0.8 | [9] | 
47 | 4 | 2 | 0.75 | [9] | 
48 | 4 | 2 | 0.4 | [5] | 
Note: The highest MCS for each modulation order
QPSK: #9 (Table 5.1.3.1-1 in TS38.214)
16QAM: #16 (Table 5.1.3.1-1 in TS38.214)
64QAM: #28 (Table 5.1.3.1-1 in TS38.214)
256QAM: #27 (Table 5.1.3.1-2 in TS38.214)
Notes: How to derive low bound one?
Keep MCS_pratical TBD at current stage.

## Slide 7: MCS levels and tables 3/3
Proposal (Cont.)
  Adopt the following procedure for FR2 SDR test cases: (baseline)
    Use general procedure to select CA bandwidth for testing
    Derive for each CC based on UE capability by the previous slide (j is CC index)
    Identify testable SNR value for particular test configuration based on test equipment characteristics
    Use “SNR to MCS+Rank” table to find for each CC (Detail of “SNR to MCS+Rank” table is FFS)
    Conduct SDR test with for each CC
  Other options not excluded