## Slide 1: Way forward on NR PDCCH demodulation requirements
Ericsson
3GPP TSG-RAN WG4 Meeting #89
Spokane, US, 12 – 16 Nov, 2018
R4-1816390

## Slide 2: AL=16 with 4Rx on tc14 and tc15
Agreements made from offline
  For FR1 15 kHz (case 14): further evaluate under TDL-A with MIMO correlation ULA medium A for AL=16 under 4Rx, decide in next RAN4 meeting for whether introducing test cases with AL 16 under 4Rx.
  For FR1 30 kHz (case 15a): Introducing test cases AL 16 with 4Rx
    TDL-C with ULA medium A(baseline)
    TDL_A with ULA medium A
    Decided above two options based on evolution results

## Slide 3: Bundle size for 4Rx on tc6 and tc7
Option 1: REG bundle size =2, CORESET BW = 102
Option 2: REG bundle size =6, CORESET BW = 90
Further check the details simulation assumption and results among companies and decide in next meeting.

## Slide 4: SNR requirements derivation
Plan for deriving performance requirements (SNR points)
  Define tentative SNR requirements for the agreed test cases as much as possible
  Update TPs including SNR requirements for test cases with []
  The agreed SNR values still can be updated if more results collected from companies in future meeting or technical issues identified
SNR = average of IM results among companies +extra margin [0.5dB]
For test cases where the span among companies’ results is within [2.5dB], capture the SNR requirement with [] as above in the TP
For test cases with larger span than [2.5dB], further check the details of simulation assumption and further discuss extra margin on a case by case basis, leave TBD for the SNR requirement in the TP

## Slide 5: Summary of simulation assumption – (1/2)
Test No. | SCS(KHz) | Format | CORESET RB | Payload | CORESET time duration | AL | CCE-to-REG Mapping | REG bundle size | CORESET-interleaver-size | Propagation condition | Antenna configuration with 2Rx | Antenna configuration with 4Rx
1 | 15 | 1_0 | 24 | 39 | 2 | 2 | Non-interleaved | 6 | NA | TDL-A, 30ns, 10Hz | 1x2 Low | 1x4 Low
2 | 15 | 1_0 | 24 | 39 | 2 | 4 | Non-interleaved | 6 | NA | TDL-C, 300ns, 100Hz | 2x2 Low | 2x4 Low
3 | 15 | 1_1 | 24 | 50 | 2 | 2 | Non-interleaved | 6 | NA | TDL-C, 300ns, 100Hz | 1x2 Low | 1x4 Low
4 | 15 | 1_1 | 48 | 50 | 2 | 4 | Non-interleaved | 6 | NA | TDL-A, 30ns, 10Hz | 1x2 Low | 1x4 Low
5 | 15 | 1_1 | 48 | 50 | 2 | 8 | Non-interleaved | 6 | NA | TDL-C, 300ns, 100Hz | 2x2 Low | 2x4 Low
6a | 30 | 1_0 | 102 | 41 | 1 | 2 | Interleaved | 2 | 3 | TDL-A, 30ns, 10Hz | 1x2 Low | 1x4 Low
6b | 30 | 1_0 | 90 | 41 | 1 | 2 | Interleaved | 6 | 3 | TDL-A, 30ns, 10Hz | NA | 1x4 Low
7a | 30 | 1_1 | 102 | 52 | 1 | 4 | Interleaved | 2 | 3 | TDL-C, 300ns, 100Hz | 1x2 Low | 1x4 Low
7b | 30 | 1_1 | 90 | 52 | 1 | 4 | Interleaved | 6 | 3 | TDL-C, 300ns, 100Hz | NA | 1x4 Low
8 | 30 | 1_1 | 90 | 52 | 1 | 8 | Interleaved | 6 | 3 | TDL-C, 300ns, 100Hz | 2x2 Low | 2x4 Low
9 | 120 | 1_0 | 60 | 40 | 1 | 2 | Interleaved | 2 | 3 | TDL-A, 30ns, 75Hz | 1x2 Low | NA
10 | 120 | 1_1 | 60 | 51 | 1 | 4 | Interleaved | 6 | 2 | TDL-A, 30ns, 300Hz | 1x2 Low | NA
11 | 120 | 1_1 | 60 | 51 | 1 | 8 | Interleaved | 2 | 3 | TDL-A, 30ns, 75Hz | 2x2 Low | NA

## Slide 6: Summary of simulation assumption – (2/2)
Test No. | SCS(KHz) | Format | CORESET RB | Payload | CORESET time duration | AL | CCE-to-REG Mapping | REG bundle size | CORESET-interleaver-size | Propagation condition | Antenna configuration with 2Rx | Antenna configuration with 4Rx
12 | 15 | 1_0 | 48 | 39 | 1 | 4 | Non-interleaved | 6 | NA | TDL-A, 30ns, 10Hz | 1x2 Low | 1x4 Low
13 | 15 | 1_1 | 48 | 50 | 1 | 8 for 2Rx and 4 for 4Rx | Non-interleaved | 6 | NA | TDL-A, 30ns, 10Hz | 2x2 Low | 2x4 Low
14 | 15 | 1_0 | 48 | 39 | 2 | 16 | Non-interleaved | 6 | NA | [TDL-A, 30ns, 10Hz] | 1x2 Low | 1x4 Medium A
15a | 30 | 1_0 | 48 | 41 | 2 | 16 | Non-interleaved | 6 | NA | [TDL-C, 300ns, 100Hz] as baseline | 1x2 Low | 1x4 Medium A
15b | 30 | 1_0 | 48 | 41 | 2 | 16 | Non-interleaved | 6 | NA | [TDL-A, 30ns, 10Hz] as optional only for 4Rx | NA | 1x4 Medium A
16 | 120 | 1_0 | 60 | 40 | 2 | 16 | Interleaved | 2 | 3 | [TDL-A, 30ns, 75Hz] | 2x2 Low | NA

## Slide 7: Alignment results summary
Description | Ericsson | QC | Intel | Samsung | Huawei | CATT | CMCC | MTK | STD | SPAN | AVE
Test 1 2Rx | 5,4 | 7,1 | 6,0 |  | 5,9 | 6,8 |  | 6,7 | 0,6 | 1,7 | 6,3
Test 1 4Rx | -0,8 | 1,1 | 0,5 |  | -1,0 | 0,8 |  | 0,6 | 0,9 | 2,1 | 0,2
Test 2 2Rx | 0,4 | 0,0 | -0,9 |  | -2,0 | 0,1 |  | 0,4 | 0,9 | 2,4 | -0,3
Test 2 4Rx | -3,4 | -4,2 | -4,6 |  | -6,0 | -4,3 |  | -4,2 | 0,9 | 2,6 | -4,4
Test 3 2Rx | 5,5 | 7,4 | 5,8 |  | 5,1 |  |  | 6,6 | 0,9 | 2,3 | 6,1
Test 3 4Rx | -0,4 | 1,1 | 0,6 |  | -0,5 |  |  | 1,2 | 0,8 | 1,7 | 0,4
Test 4 2Rx | 2,6 | 3,9 | 3,6 |  | 3,2 |  |  | 4,8 | 0,8 | 2,2 | 3,6
Test 4 4Rx | -3,0 | -0,9 | -1,6 |  | -3,0 |  |  | -0,9 | 1,1 | 2,1 | -1,9
Test 5 2Rx | -3,3 | -3,3 | -4,0 |  | -5,1 | -3,2 |  | -3,1 | 0,8 | 2,0 | -3,7
Test 5 4Rx | -6,6 | -6,7 | -7,1 |  | -8,5 | -6,5 |  | -6,4 | 0,8 | 2,1 | -7,0
Test 6 2Rx | 3,7 | 5,3 | 5,3 |  | 4,2 |  | 5,0 | 5,5 | 0,7 | 1,8 | 4,8
Test 6 4Rx Option 1 | -1,2 | 1,3 | 4,1 |  | -0,7 |  | 0,2 | 1,2 | 1,9 | 5,3 | 0,8
Test 6 4Rx Option 2 | -1,7 | 0,4 | -0,7 |  | -1,4 |  | -1,4 | 1,0 | 1,1 | 2,7 | -0,6
Test 7 2Rx | 0,0 | 2,1 | 1,6 |  | -0,3 |  | -0,2 | 1,8 | 1,1 | 2,4 | 0,8
Test 7 4Rx Option 1 | -4,0 | -1,3 | 2,0 |  | -4,0 |  | -4,1 | -1,8 | 2,4 | 6,1 | -2,2
Test 7 4Rx Option 2 | -4,7 | -1,8 | -3,8 |  | -4,7 |  | -4,0 | -2,2 | 1,2 | 2,9 | -3,5
Test 8 2Rx | -3,9 | -2,1 | -3,7 |  | -4,9 | -3,0 | -3,9 | -2,0 | 1,1 | 2,9 | -3,4
Test 8 4Rx | -7,5 | -5,5 | -6,9 |  | -8,1 | -5,8 | -7,2 | -5,4 | 1,1 | 2,8 | -6,6
Test 9 | 2,6 | 5,1 | 4,3 |  | 2,6 |  |  | 4,8 | 1,2 | 2,5 | 3,9
Test 10 | -0,6 | 2,2 | -0,1 |  | -0,5 |  |  | 2,0 | 1,4 | 2,8 | 0,6
Test 11 | -3,7 | -1,7 | -2,2 |  | -4,0 |  |  | -1,5 | 1,2 | 2,5 | -2,6
Test 12 2Rx | 2,1 | 2,2 | 2,4 |  | 1,9 |  | 3,3 | 4,1 | 0,8 | 2,2 | 2,7
Test 12 4Rx | -3,1 | -2,0 | -2,5 |  | -3,9 |  | -2,8 | -0,8 | 1,1 | 3,2 | -2,5
Test 13 2Rx AL 8 | -2,7 | -2,5 | -2,5 |  | -3,7 | -2,5 | -1,7 | -0,3 | 1,1 | 3,4 | -2,3
Test 13 4Rx AL 4 | -4,3 | -3,2 | -3,3 |  | -5,2 | -3,5 | -3,0 | -1,6 | 1,1 | 3,6 | -3,4
Test 14 2Rx | -4,8 | -3,5 | -3,9 |  | -3,7 |  | -4,3 | -2,1 | 0,9 | 2,7 | -3,7
Test 14 4Rx (for information) | -5,9 |  | -7,8 |  | -8,7 |  | -7,5 | -6,8 | 1,1 | 2,8 | -7,3
Test 15 2Rx | -7,0 | -5,1 | -6,7 |  | -7,1 |  | -7,6 | -5,4 | 1,0 | 2,5 | -6,5
Test 15 4Rx (for information) | -8,3 |  | -9,4 |  | -10,3 |  | -9,2 | -7,7 | 1,0 | 2,6 | -9,0
Test 15 4Rx(Med-A) |  | -5,0 | -5,3 |  | -6,7 |  |  |  |  | 1,7 | 
Test 16 | -5,9 | -5,8 | -5,1 |  |  |  |  | -4,9 | 0,5 | 1,0 | -5,4
Note: Based on alignment results, only test cases marked green with impairments results will be specified with square brackets. The marked yellow test cases will be specified as TBD. And the mark red test cases will not be specified in the TP and require further evaluations.

## Slide 8: Impairment results summary
Note: Based on alignment results, only test cases marked green with impairments results will be specified with square brackets in the TP
Description | Ericsson | QC | Intel | Samsung | Huawei | CATT | CMCC | MTK | xx | STD | SPAN | AVE | AVE+margin(0.5dB)
Test 1 2Rx | 7,6 | 8,6 | 7,5 |  | 6,5 | 8,3 |  | 7,7 |  | 0,7 | 2,1 | 7,7 | 8,2
Test 1 4Rx | 0,7 | 2,6 | 2,0 |  | 0,5 | 2,3 |  | 1,6 |  | 0,9 | 2,1 | 1,6 | 2,1
Test 2 2Rx | 2,0 | 1,5 | 0,6 |  | -0,5 | 1,6 |  | 1,4 |  | 0,9 | 2,5 | 1,1 | 1,6
Test 2 4Rx | -1,6 | -2,2 | -3,1 |  | -4,5 | -2,8 |  | -3,2 |  | 1,0 | 2,9 | -2,9 | 
Test 3 2Rx | 7,4 | 8,9 | 7,3 |  | 6,6 |  |  | 7,6 |  | 0,8 | 2,3 | 7,6 | 8,1
Test 3 4Rx | 1,4 | 2,6 | 2,1 |  | 1,0 |  |  | 2,2 |  | 0,7 | 1,6 | 1,8 | 2,3
Test 4 2Rx | 4,9 | 5,4 | 5,1 |  | 4,7 |  |  | 5,8 |  | 0,4 | 1,1 | 5,2 | 5,7
Test 4 4Rx | -1,6 | 0,6 | -0,1 |  | -1,5 |  |  | 0,1 |  | 1,0 | 2,2 | -0,5 | 0,0
Test 5 2Rx | -1,7 | -1,3 | -2,5 |  | -3,6 | -1,7 |  | -2,1 |  | 0,8 | 2,4 | -2,1 | -1,6
Test 5 4Rx | -4,8 | -4,7 | -5,6 |  | -7,0 | -5,0 |  | -5,4 |  | 0,8 | 2,3 | -5,4 | -4,9
Test 6 2Rx | 7,2 | 6,8 | 6,8 |  | 5,7 |  | 6,0 | 6,5 |  | 0,6 | 1,5 | 6,5 | 7,0
Test 6 4Rx Option 1 | 5,7 | 2,8 | 5,6 |  | 0,8 |  | 1,2 | 2,2 |  | 2,1 | 4,9 | 3,0 | 
Test 6 4Rx Option 2 | 0,3 | 1,9 | 0,8 |  | 0,2 |  | -0,4 | 2,0 |  | 1,0 | 2,4 | 0,8 | 
Test 7 2Rx | 4,4 | 3,6 | 3,1 |  | 1,2 |  | 0,8 | 2,8 |  | 1,4 | 3,6 | 2,7 | 3,2
Test 7 4Rx Option 1 | 4,5 | 0,7 | 3,5 |  | -2,5 |  | -3,1 | -0,8 |  | 3,1 | 7,6 | 0,4 | 
Test 7 4Rx Option 2 | -2,2 | 0,2 | -2,3 |  | -3,2 |  | -3,0 | -1,2 |  | 1,3 | 3,4 | -2,0 | 
Test 8 2Rx | -2,2 | 0,0 | -2,2 |  | -3,4 | -1,5 | -2,9 | -1,0 |  | 1,1 | 3,4 | -1,9 | 
Test 8 4Rx | -5,2 | -3,5 | -5,4 |  | -6,6 | -4,3 | -6,2 | -4,4 |  | 1,1 | 3,1 | -5,1 | 
Test 9 | 6,1 | 6,6 | 5,8 |  | 4,1 |  |  | 5,8 |  | 0,9 | 2,5 | 5,7 | 6,2
Test 10 | 1,5 | 3,7 | 1,4 |  | 1,0 |  |  | 3,0 |  | 1,2 | 2,7 | 2,1 | 
Test 11 | -0,5 | 0,3 | -0,7 |  | -2,5 |  |  | -0,5 |  | 1,0 | 2,8 | -0,8 | -0,3
Test 12 2Rx | 4,2 | 3,7 | 3,9 |  | 3,4 |  | 4,3 | 5,1 |  | 0,6 | 1,7 | 4,1 | 4,6
Test 12 4Rx | -1,2 | 0,0 | -1,0 |  | -2,4 |  | -1,8 | 0,3 |  | 1,0 | 2,7 | -1,0 | 
Test 13 2Rx AL 8 | -1,0 | -0,5 | -1,0 |  | -2,2 | -1,0 | -0,7 | 0,7 |  | 0,9 | 2,9 | -0,8 | 
Test 13 4Rx AL 4 | -2,1 | -1,2 | -1,8 |  | -3,7 | -2,0 | -2,0 | -0,6 |  | 0,9 | 3,1 | -1,9 | 
Test 14 2Rx | -2,9 | -1,5 | -2,4 |  | -2,2 |  | -3,3 | -1,1 |  | 0,8 | 2,2 | -2,2 | 
Test 14 4Rx | -4,1 |  | -6,3 |  | -7,2 |  | -6,5 | -5,8 |  | 1,2 | 3,1 | -6,0 | 
Test 15 2Rx | -5,0 | -3,1 | -5,2 |  | -5,6 |  | -6,6 | -4,4 |  | 1,2 | 3,5 | -5,0 | -4,5
Test 15 4Rx | -6,5 | -3,0 | -7,9 |  | -8,8 |  | -8,2 | -6,7 |  | 2,1 | 5,8 | -6,9 | 
Test 16 | -3,8 | -3,8 | -3,6 |  | -5,2 |  |  | -3,9 |  | 0,6 | 1,6 | -4,1 | -3,6

## Slide 9: Information on payload size for Format 1_1
For all test cases with Format 1_1 companies would like to double check the payload size to make sure it’s configurable and consistent.
Keep the payload size in [] in FRC in Annex for the test cases above in the TP for this meeting.
Companies will provide updated numbers of payload size with detailed assumptions after the meeting, in order to align the simulation assumptions for next meeting.
Requirements and results can be revisied in next meeting based on simulation results based on companies.