## Slide 1: Way forward on the idle mode reporting
Ericsson
3GPP TSG-RAN WG4 Meeting # 89
Spokane, WA, USA, November 12-16, 2018
Agenda: 7.12.2
R4-1816414

## Slide 2: Background
The following parameters are used by the UE to verify whether the UE meets cell selection criterion S as described in section 5.2.3.2 of TS 38.304:
  Qrxlevmin: Minimum required RX level in the cell (dBm).
  Qqualmin: Minimum required quality level in the cell (dB).
The values of the above parameters are signaled by the network to the UE in idle state.
RAN2 needs to specify the ranges of Qrxlevmin and Qqualmin, which are currently tentative (See Annex A).
In RRC connected state the SS-RSRP and SS-RSRQ ranges are defined:
  SS-RSRP: from -44 dBm down to -156 dBm
  SS-RSRQ: from 20 dB down to -43 dB

## Slide 3: Way Forward on Qrxlevmin and Qqualmin
Recommended ranges for Qrxlevmin:
  Qrxlevmin range should be similar to SS-RSRP.
  SS-RSRP and current LTE RSRP ranges are similar: between -44 dBm to -156 dBm.
    In LTE, RSRP below -140 dBm (down to -156 dBm) was introduced to support enhanced coverage.
  The recommended Qrxlevmin range is as follows:
    Minimum Qrxlevmin = -140 dBm
    Maximum Qrxlevmin = -44 dBm
Recommended ranges for Qqualmin:
  Compared to LTE RSRQ, the NR SS-RSRQ can be quite low due to different types of SS-RSSI measurement schemes in NR.
    Therefore at least the lowest value of Qqualmin should be the same as lowest SS-RSRQ in RRC connected state.
    However the upper value of Qqualmin can be larger than the largest SS-RSRQ because Qqualmin is the minimum quality level.
  The recommended Qqualmin range is as follows:
    Minimum Qqualmin = -43 dB
    Maximum Qqualmin = -12 dB

## Slide 4: Annex A: Qqualmin and Qrxlevmin in Section 6.3.2 of TS 38.331
– Q-QualMin
The IE Q-QualMin is used to indicate for cell selection/ re-selection the required minimum received RSRQ level in the (NR) cell. Corresponds to parameter Qqualmin in TS 38.304 [4]. Actual value Qqualmin = field value [dB].
Q-QualMin information element
Q-QualMin ::= INTEGER (-34..-3) -- FFS range
– Q-RxLevMin
The IE Q-RxLevMin is used to indicate for cell selection/ re-selection the required minimum received RSRP level in the (NR) cell. Corresponds to parameter Qrxlevmin in TS 38.304 [4]. Actual value Qrxlevmin = field value * 2 [dBm].
Q-RxLevMin information element
Q-RxLevMin ::= INTEGER (-70..-22) -- FFS range