## Slide 1: Way forward on NR UE PDSCH demodulation requirements and General aspects
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #89
Spokane, USA, 12 – 16 November 2018 Agenda Item: 7.13.1.2
R4-1816488

## Slide 2: EN-DC performance requirements
Issue 1: Handling of simultaneous Tx/Rx for EN-DC
  Proposal: EN-DC test parameters
      Transmissions on the LTE and NR carriers are synchronous (i.e. aligned on subframe boundaries)
      TDD-TDD EN-DC LTE configuration
        Use LTE TDD DL-UL configuration 2
        LTE frame is shifted by 2 SF’s to the right with respect to the start of NR frame

## Slide 3: EN-DC performance requirements
Issue 2: Handing of FR1 EN-DC test cases of NR TDD DL-UL configurations not aligned with LTE
  Proposal: FR1 EN-DC test cases with NR TDD DL-UL configurations not aligned with LTE can be tested on the corresponding EN-DC BCs where UE supports simultaneous Tx/Rx

## Slide 4: EN-DC performance requirements
Issue 3-1 : EN-DC including FR2 carrier requirements (both SDR and normal test cases)
  Proposal:
    Normal demodulation requirements:
      No requirements for FR1 NR/LTE carriers for Rel-15 EN-DC test cases including FR2 carrier.
    SDR requirements:
      Define requirements for FR1 NR/LTE carriers of Rel-15 EN-DC SDR test cases which including FR2 carrier.
      Only FR2 performance is tested in Rel-15.

## Slide 5: Requirements Applicability
Issue 1-1 : Applicability rules for UEs with SA and NSA support
  Proposal: For UE’s that support both NSA and SA:
    Normal UE demodulation requirements are verified using SA requirements only
    SDR requirements are tested for both SA and NSA

## Slide 6: Requirements Applicability
Issue 2: Applicability rules for 2Rx and 4Rx
  Proposal: For UE’s that support 4RX on at least one band, the normal UE performance requirements are verified using 4RX tests and 2RX tests can be skipped.

## Slide 7: PDSCH
Issue 1: Additional soft buffer test for PDSCH mapping type A
  Previous agreement
    Requirement with 70% test point and 8 HARQ process for FDD and 16 HARQ process for TDD: (FFS whether needed or not)
      Option 1: No tests
      Option 2 (simulation purpose)
        MCS #19 and rank 2 for FR1, FDD and TDD (7D1S2U) for both 2Rx and 4Rx
        MCS #13 and rank 2 (2Rx) for TDD (DDDSU) FR2
      Other options not excluded
      Interested companies are encourage to bring more analysis with simulation results to further decide the necessity of introducing such test cases in next RAN4 meeting.
  Proposal:
    FFS whether to introduce additional requirement with 70% test point with 8 HARQ process for FDD and 16 HARQ process for TDD
      Option 1: No Test since soft buffer test has been defined (Intel, QC)
      Option 2: Introduce PDSCH demodulation tests with 70% test point with 8 HARQ processes for FDD and 16 HARQ processes for TDD

## Slide 8: PDSCH
Issue 2: LTE-NR co-existence test case (duration length)
  Previous agreements:
    PDSCH Type A
    Start symbol (S): 3
    Duration (L): [9 or 11]
      Note: Use 11 if RAN1 agreement on changes of additional DMRS position for Type A is confirmed
    Number of additional DMRS: 1
    Duplex mode: FDD only
    FRC: MCS4 Rank 1 for 2Rx and 4 Rx
    Overhead for TBS determination: 18
  Proposals
    Introduce test cases for 9 and 11 symbols PDSCH duration
      In RAN4 89, specify requirements for 9 symbols test. In RAN4 90, specify additional requirements for 11 symbols PDSCH duration.

## Slide 9: PDSCH
Issue 3: Dynamic TDD DL-UL configuration test
  Previous agreements:
    Dynamic UL/DL determination is a mandatory feature for Rel-15.
    Forward Compatibility: If no test is defined to test this feature now, network operators will have a risk of breaking some existing NR UEs if they try to configure dynamic TDD configuration now or in any future NR release.
    To avoid any extra workload, it can be tested for some existing TDD test case(s) as below:
      Configure all slots as flexible in RRC configuration or do not configure TDD UL-DL configuration through RRC.
      Send DL or UL DCI to indicate D, S and U slot to configure the same TDD UL-DL config as agreed for those test case(s).
    The above methodology does not impact simulation results or RMCs but it verifies that UE supports DCI based slot configuration.
    Way forward
      Option 1: Use dynamic UL/DL determination for some existing PDSCH demodulation test case(s). [QC, Ericsson, NTT Docomo, AT&T, China Mobile, Intel]
      Option 2: Do not define test ( it’s a functionality test, not in UE demodulation performance scope) (Huawei, MTK)
  Proposal:
    Way forward
      Option 1: Use dynamic UL/DL determination for some existing PDSCH demodulation test case(s).
      Option 2: Do not define test
    Next steps
      Further make downselection in RAN4 #90

## Slide 10: PDSCH
Issue 4: CSI-RS for UE RX beam refinement
  Proposal
    Configure CSI-RS for UE Rx Beam refinement purpose during test, whether UE using this or not for Rx Beam refinement pending on UE capability and implementation.
    NZP CSI-RS configuration for BM:
      1 port
      2 resources
      Periodicity 20 ms
      Offset 0
      Repetition ON
      Subcarrier index: 0
      OFDM symbol:
        Resource 1: 8, Resource 2: 9, (note: no collision with SSB or CSIRS for CSI acquisition)
      Density [3]
      No CDM
    Further discuss how to capture the beam refinement procedure in the test case definition

## Slide 11: PDSCH
Issue 5: SNR requirements derivation
  Plan for deriving performance requirements (SNR points)
    Define tentative SNR requirements for the agreed test cases as much as possible
    Update TPs including SNR requirements for test cases with []
    The agreed SNR values still can be updated if more results collected from companies in future meeting or technical issues identified
    Keep requirements TBD for FR2 64QAM cases , decide the SNR values with more results from companies in RAN4#90 , IM results submitted from companies should take PN impact into account.
  SNR = average of IM results among companies +extra margin
  For test cases where the span among companies’ results is within [2.5dB], use the same extra margin values.
    Extra margin values: 0.5dB for QPSK, 16QAM and 0.8 dB for 64QAM and 25QAM
  For test cases with larger span further check the details of simulation assumption and further discuss extra margin on a case by case basis

## Slide 12: PDSCH
Issue 6: New test cases for follow PMI for TDD configuration of DDDSU for FR2.
  Proposal:
    Introduce one additional PMI reporting test case based on DDDSU for FR2 120kHz
    Do not introduce follow PMI PDSCH demodulation test cases

## Slide 13: PDSCH
Other open issues
  Proposal:
    PDSCH scheduling for TDD tests with Mapping type B
      Do not schedule PDSCH Type B in special slot (i.e. confirm RAN4 89 simulation assumptions)
    VRB-to-PRB interleaving
      All requirements are defined under assumption of no VRB-to-PRB interleaving in Rel-15
    Further discuss in RAN4 #90
      TCI state and QCL configuration parameters for PDSCH requirement
      TRS configuration for FR2
        Option 1: Do not change TRS configuration
        Option 2: 20ms with 1 slot duration and OFDM symbol indexes 5, 9
        Option 3: 40ms with 1 slot duration
        Other options are not precluded
        TRS configuration change can be applicable for one of test cases. Exact test cases is FFS.
        FFS whether to introduce configuration for normal demodulation or SDR test cases

## Slide 14: For Information: Dynamic TDD UL/DL Configuration
It can be configured for any of the existing TDD test cases by changing the way TDD UL/DL configuration is communicated to the UE.
As an example, DDDSU (S = 10D:2G:2U) can be configured as follows, assuming 2 symbol PDCCH:
  Do not configure semi-static TDD configuration through RRC.
  Follow the below table for scheduling:
Slot Index | DCI Format | Grant Allocation
mod(slot_idx,5) = 0,1,2 | 1-0 | Symbol 2-13
mod(slot_idx,5) = 3 | 1-0 | Symbol 2-9
mod(slot_idx,5) = 3 | 0-0 | Symbol 12-13 in current slot and symbol 0-13 in next slot