## Slide 1: Way forward on NR PBCH demodulation requirements
CMCC
3GPP TSG-RAN WG4 Meeting #89 R4-1816391
Spokane, WA, USA, 12th – 16th Nov 2018
Agenda: 7.13.1.3.2

## Slide 2: Background
Agreed way forward in RAN4#88bis:
  R4-1814240 Way forward on NR PBCH demodulation requirements

## Slide 3: Way forward
Issue 1: Necessity of 4Rx PBCH test cases
  Option 1: introducing 4Rx PBCH test cases
  Option 2: not introducing 4Rx PBCH test cases
Proposal:
  Further discuss whether to introduce 4Rx PBCH test cases after collecting results from more companies in next meeting
  If 4Rx PBCH requirements is introduced,
    whether to apply 4Rx PBCH requirements is up to UE declaration
    Note the PBCH demodulation requirements do not need to be tested in RAN5 as same as LTE PBCH demodulation requirements. (i.e. no conformance requirements)

## Slide 4: Way forward
Issue 2: UE assumption on DMRS SSB index acquisition for PBCH demodulation
  Option 1: Derive requirements assuming without knowledge of SSB index
  Option 2: Derive two kinds of requirements with and without knowledge of SSB index
Proposal:
  Introduce PBCH requirements assuming without knowledge of SSB index.
    PBCH requirements is derived with the combination of SSB index detection probability and MIB decoding probability
  Whether to introduce requirements with knowledge of SSB index will be further discussed after collecting results from more companies in next meeting

## Slide 5: Way forward
Companies are encouraged to provide simulation results and impairment results in next meeting.
Define SNR requirements based on average of impairment plus extra margin for agreed test cases in next meeting. For extra margin value,
  If the span is <= 2dB, margin is 0dB
  If the span is > 2dB, the margin can be discussed case by case.

## Slide 6: Simulation assumptions
Parameters | Unit | Value
Cell ID |  | 0
CP length |  | Normal
Number of SS/PBCH blocks within an SS burst set periodicity |  | 1
SS/PBCH block index |  | 0
SS burst periodicity | ms | 20
MIB size | bits | 24
PBCH payload size (including 24 bits CRC and 8 bits of SS/PBCH location information) | bits | 56
Receiver assumption |  | LMMSE
Table 1: common parameters
For PBCH demodulation requirements
  The simulation assumptions in Table 1 are subject to common setup
  The simulation assumptions in Table 2 are subject to simulation alignment

## Slide 7: Simulation assumption
Parameters | Test 1 | Test 2 | Test 3 | Test 4
Frequency Range | FR1 | FR1 | FR2 | FR2
Channel Bandwidth | 10MHz | 40MHz | 100MHz | 100MHz
SS/PBCH SCS | 15kHz | 30kHz | 120kHz | 240kHz
SS Block pattern (Note 1) | Case A | Case B Case C | Case D | Case E
Antenna Configuration | 1x2 1x4 | 1x2 1x4 | 1x2 | 1x2
Propagation channel (Note 2) | TDLC300-100 | TDLA30-10 | TDLA30-300 | TDLA30-75
Assumption on DMRS SSB index acquisition | a: SS/PBCH block index is known b: SS/PBCH block index is not known |  |  | 
Table 2: Test cases for PBCH demodulation
Note 1: Depending on the operating band. Refers to TS38.101-1 Table 5.4.3.3-1 for which band uses which pattern
Note 2: Use PDP specified in TS38.901