## Slide 1: Way forward on NR UE CSI requirements
Samsung
3GPP TSG-RAN WG4 Meeting RAN4#89 R4-1816491
Spokane, US, 12-16 Nov, 2018

## Slide 2: Previous agreed test cases list (Background information)
Static CQI test cases
  Test 1: FR1 FDD 10MHz &15kHz , 2*2, 2*4
  Test 2: FR1 TDD 40MHz&30kHz, 2*2, 2*4
  Test 3: FR2 100MHz& 120kHz, 2*2
Wideband fading CQI test cases
  Test 1: FR1 FDD 10MHz &15kHz , 2*2, 2*4
  Test 2: FR1 TDD 40MHz&30kHz, 2*2, 2*4
  Test 3: FR2 100MHz& 120kHz, 2*2
Wideband PMI test cases
  Test 1: FR1 FDD 10MHz &15kHz , 8*2, 8*4
  Test 2: FR1 TDD 40MHz&30kHz, 8*2, 8*4
  Test 3: FR2 100MHz& 120kHz, 2*2
  Test 4: FR1 FDD 10MHz &15kHz , 4*2, 4*4
  Test 5: FR1 TDD 40MHz&30kHz, 4*2, 4*4
RI test
  Test 1: FR1 FDD 10MHz&15kHz, 2*2, 2*4, 4*4
  Test 2: FR1 TDD 40MHz&30kHz, 2*2, 2*4, 4*4
  Test 3: FR2 100MHz&120kHz, 2*2
Sub-band CQI test cases
  Test 1: FR1 FDD 10MHz &15kHz
  Test 2: FR1 TDD 40MHz&30kHz

## Slide 3: Test Set-up (1/2)
CSI-RS resource/CSI reporting interval and slot offset for aperiodic CSI reporting
  FR1 FDD 15 kHz: 5 slots as CSI reporting interval, slot offset as 1
  FR1 TDD 30kHz: 10 slots as CSI reporting interval, slot offset as 1
  FR2 TDD 120kHz: 8 slots as CSI reporting interval, slot offset as 1
CSI-RS resource periodicity and slot offset for FR2 120kHz CSI test cases
  8 slots as periodicity and slot offset as 1
CSI reporting type for FR2 fading CQI, RI test cases
  Using aperiodic CSI reporting for FR2 fading CQI test cases and RI test
Minimum CSI processing delay for FR2 test cases
  Reduced Doppler shift value for FR2 CSI test cases, candidate values for further evaluation [35]Hz
  Minimum CSI delay by separate UL slots for ACK/NACK and CSI:
    [ACK/NACK feedback in UL Slot 3 with 8 slots interval]
    [CSI feedback in UL slot 7 with 8 slots interval]
    [Minimum CSI delay: 11 slots]
D
U
S
D
D
U
S
D
D
U
S
D
D
U
S
D
D
U
S
D
0
X
X
1
0
X
X
1
6
X
X
7
4
X
X
5
2
X
X
3
UL SF for CSI feedback
CSI-RS SF
First scheduled PDSCH SF
Minimum CSI delay: 11 slots
HARQ process ID
UL SF for ACK/NACK feedback
K1 = 10
K1 = 9
K1 = 6
K1 = 5

## Slide 4: Test Set-up (2/2)
Minimum CSI delay for periodic CSI test cases in FR1
  FR1 FDD: 8ms
  FR1 TDD 30kHz : 19 slots (9.5 ms)
For FR1 TDD fading CSI (fading CQI, sub-band CQI, RI, and PMI test cases),revise Doppler spread/shift from 10Hz to 5Hz
CDM (as same as PDSCH test cases DMRS configurations) will be used for CSI test cases with rank2 transmission
Minimum CSI delay assumption for additional FR2 following PMI test cases (120kHz DDDSU)
  [CSI-RS interval and offset : 5/1
  ACK/NACK feedback in UL part of slot 3 per 5 slots interval
  CSI feedback in UL Slot 4 per 5 slots interval
  Minimum CSI delay: 14 slots
  HARQ process number :8
  Other parameters reusing agreed test configurations of existing FR2 TDD PMI test cases with TDD DL-UL DDSU]

## Slide 5: Static CQI test cases
Test Metric:
  The reported CQI value shall be in the range of ±1 of the reported median more than 90% of the time.
  If the PDSCH BLER using the transport format indicated by median CQI is less than or equal to 0.1, the BLER using the transport format indicated by the (median CQI + 1) shall be greater than 0.1. If the PDSCH BLER using the transport format indicated by the median CQI is greater than 0.1, the BLER using transport format indicated by (median CQI – 1) shall be less than or equal to 0.1.
Test SNR points: (baseline)
  FR1 2Rx FDD:[8/9]dB, [14/15]dB
  FR1 4Rx FDD :[5/6]dB, [11/12]dB
  FR1 2Rx TDD:[8/9]dB, [14/15]dB
  FR1 4Rx TDD :[5/6]dB, [11/12]dB
  FR2 2Rx:[8/9]dB, [14/15]dB
  Other options not excluded
  Include these SNR points into 38.101-4 with [], the SNR points were introduced based on current results from companies; these requirements can be revised based on more results from companies.

## Slide 6: Wideband fading CQI test cases
Test metric:
  a) a CQI index not in the set {median CQI -1, median CQI, median CQI +1} shall be reported at least a % of the time;
  b) the ratio of the throughput obtained when transmitting the transport format indicated by each reported wideband CQI index and that obtained when transmitting a fixed transport format configured according to the wideband CQI median shall be ≥ g ;
  c) when transmitting the transport format indicated by each reported wideband CQI index, the average BLER for the indicated transport formats shall be greater or equal to TBD.
Test SNR points and test requirements for FR1 FDD:
Test SNR points and test requirements for FR1 TDD:
  Candidate SNR points: [6/7]dB], [12/13] dB for 2Rx; [3/4]dB], [9/10] dB for 4Rx
Test SNR points and test requirements for FR2 TDD:
  Candidate SNR points: [6/7]dB], [12/13] dB for 2Rx;
Including these values into 38.101-4 with [] for FR1 FDD , the requirements were introduced based on current results from companies; these requirements can be revised based on more results from companies.
  companies are encouraged to bring more evaluation to further confirm above SNR points and requirements after Dec.
  For FR1 TDD and FR2 fading CQI requirements, Decide test points and test requirements in RAN4#90 based on companies’ results
FR1 FDD 2*2 |  |  |  | FR1 FDD 2*4 |  |  | 
Test SNR points | BLER requirements | CQI distribution requirements | Through ration requirements | Test SNR points | BLER requirements | CQI distribution requirements | Through ration requirements
[6/7]dB], [12/13] dB | [0.02] | [20%] | [1.05] | TBD | TBD | TBD | TBD

## Slide 7: Sub-band CQI Test cases
Number of Tx
  Option 1： 1Tx
  Option 2： 2Tx (baseline)
Companies are encouraged to bring results among 0~20 dB with 2dB step size:
  Relative throughput ratio between following CQI on selected sub-band and median wideband CQI on a random selected sub-band with full size
  BLER with following CQI on selected sub-band
  The percentile of reported sub-band differential CQI offset level equals to 0 for each sub-band with full size
Decide test points and test requirements in RAN4#90 based on companies’ results

## Slide 8: PMI test cases
Test metric: Relative Throughput ratio between following PMI and random PMI at SNR point corresponding to X% TP with follow PMI.
    X= 90
Test requirements
  FR1 FDD:
    8T2R, 8T4R: TBD
    4T2R,4T4R: [1.4][1.3]
    Other options not excluded
  FR1 TDD:
    8T2R, 8T4R: TBD
    4T2R,4T4R: [1.4][1.3]
  FR2 TDD:
    2T2R: TBD
MCS and Rank for FR2 2Tx PMI test case:
  MCS 13 and Rank1
Beam steering approach applied for 4Tx and 8Tx PMI test cases, the methodology can be refer to TS36.101 B.2.3A.4, update speed as k =1 for 15kHz and k=0.5 for 30kHz and The step of phase variation as per rand per ms
Including these values into 38.101-4 with [] for FR1 FDD and FR1 TDD , the requirements were introduced based on current results from companies; these requirements can be revised based on more results from companies.
  Decide test points and test requirements in RAN4#90 based on companies’ results
MIMO correlation for FR2 2Tx PMI test case:
  Option 1: ULA Low
  Option 2: ULA medium

## Slide 9: RI test cases
Test metric:
  a) The ratio of the throughput obtained when transmitting based on UE reported RI and that obtained when transmitting with fixed rank 1 shall be ≥ g1;
  b) The ratio of the throughput obtained when transmitting based on UE reported RI and that obtained when transmitting with fixed rank 2 shall be ≥ g2;
Test requirements:
  FR1 FDD 2Rx : (Baseline))
    Other options not excluded
  FR1 FDD 4Rx:
    TBD
  FR1 TDD 2Rx : TBD
  FR1 TDD 4Rx:
    TBD
  FR2 TDD 2Rx:
    TBD
  Including these values into 38.101-4 with [] for FR1 FDD and FR1 TDD 2Rx test cases, companies are encouraged to bring more evaluation to further confirm above SNR points and requirements after Dec.
  For FR1 FDD 4Rx, FR1 TDD 4Rx and FR2 TDD 2Rx, Decide test points and test requirements in RAN4#90 based on companies’ results
Test Number | Test 1 (2X2) ULA Low |  | Test 2 (2X2) ULA Low |  | Test 3 (2X2) ULA High for FR1 | 
 | SNR | Gamma 2 | SNR | Gamma 1 | SNR | Gamma 1
 | [0 dB] | [1.0] | TBD | TBD | TBD | TBD