## Slide 1: WF for test case SNR derivation procedure
R4-1816594
Document for: Approval
3GPP TSG-RAN WG4 RAN#89
Spokane, US, 12th – 16th Nov, 2018
Agenda: 7.13.2.1
Nokia, Nokia Shanghai Bell, […]

## Slide 2: Background
We need to agree upon a large quantity of SNR values based on a large quantity of simulation results for the test requirements in 38.104 and 38.141-1/2.
After email discussion and adhoc discussion a selection procedure proposal was captured.
  See R4-1816345.
Some open issues with the procedure have been identified and their resolution has led to the refined selection procedure captured in the following.

## Slide 3: Background
According to Table 4.1.2.4-1 in 38.141-1 and Table 4.1.2.4-1 in 38.141-2, the following MU will be added for both conducted and radiated conformance test requirements in FR1.
The MU for FR2 is still TBD.
Subclause | Maximum Test System Uncertainty
8 PUSCH, PUCCH, PRACH with [single antenna port] and fading channel | ± [0.6] dB
8 PRACH with [single antenna port] and AWGN | ± [0.3] dB
8 PUSCH with [two antenna port] and fading channel | ± [0.8] dB

## Slide 4: Refined Selection Procedure
Procedure to derive the performance requirements:
  Only inputs that consist of a pair of ideal and impaired results can be taken into account.
  If the ideal span <= [2dB]:
    The AVERAGE impairment results can be used for the performance requirement with [] in the TPs;
  Else if the ideal span is larger than [2dB]:
    The results farthest from the AVERAGE value is taken out for the AVERAGE and SPAN re-calculation until the ideal span is <=2dB but still with at least 3 companies’ results available:
      The ultimate AVERAGE impairment results with corresponding ideal span <=2dB can be used for performance requirement with [] in the TPs.
    Otherwise put TBD for the related performance requirements.
  [If the span of the impairment results after removal the outliers (if any) are larger than [3dB], then the procedure cannot be applied, related performance requirement remain TBD.](*)
  The agreed SNR values during this meeting remains in [] and can be updated if more or updated results are collected from companies in future meeting or technical issues are identified.
(*) Remark: In RAN4 #89 results, this rule was checked but did not trigger.