## Slide 1: WF on handling of ETC requirement in FR2
NTT DOCOMO, INC.
R4-1816629

## Slide 2: Background
Related WF approved in RAN4#88bis [1]
  Companies are encouraged to propose a list of RF requirements which need be tested due to expected different performance in extreme temperature conditions
  RAN4 decides which UE RF requirements are allowed to be verified only under normal temperature condition and inform RAN5 on RAN4’s decision.
In this meeting, there are proposals for further clarification as below:
  For core requirement perspective [2]
  For test perspective [3,4,5,6]
Concerns
  Regulation related issue
  Performance degradation due to extreme temperature condition
  Feasibility of testing equipments
Agreement in RAN4#89:
  At least EIS and EIRP spherical coverage and TRP requirements are not tested under ETC.

## Slide 3: Way forward
Core requirement perspective
  The values of the requirements specified in TS 38.101-2 should be kept on both NC and ETC.
Testing perspective
  To address the performance degradation issue and feasibility of testing equipment issue due to extreme temperature condition, some requirements on ETC can be verified by being tested on only NC instead of tested on ETC.
    Frequency error are tested on both NC and ETC.
    MPR, ALCR, EIS Spherical, EIRP spherical coverage and TRP requirements are not tested under ETC
    Companies are encourage to submit technical contribution if the certain requirements are required to be tested on ETC due to extreme temperature condition.

## Slide 4: Reference
[1] R4-1814173, “WF on FR2 Temperature Conditions for UE RF Requirements Verification”, MediaTek Inc., RAN4#88bis, Chengdu, China , October 8-12, 2018
[2] R4-1815055, “Extreme condition requirement for FR2”, NTT DOCOMO, INC., RAN4#89, Spokane, Washington, November 12-16, 2018
[3] R4-1816046, “On applicability of EC on FR2 requriements”, Qualcomm Incorporated, RAN4#89, Spokane, Washington, November 12-16, 2018
[4] R4-1814841, “On FR2 Temperature Testing”, Keysight Technologies UK Ltd, RAN4#89, Spokane, Washington, November 12-16, 2018.
[5] R4-1814891 Temperature condition for EIRP verification, MediaTek Inc., RAN4#89, Spokane, Washington, November 12-16, 2018.
[6] R4-1814960, ”Discussion on UE RF requirement verification with extreme conditions in FR2”, OPPO, RAN4#89, Spokane, Washington, November 12-16, 2018.