## Slide 1: Updated WF on 2 Rx vehicle UE: Link budget simulation assumptions
SAMSUNG, LG Electronics, Volkswagens AG
3GPP TSG-RAN WG4 #89 Meeting
Spokane, Washington, U.S., 12th – 16th Nov., 2018 Agenda Item: 10.3.2
R4-1816647
(Revision of R4-1814143,
R4-1814775)

## Slide 2: Offline Discussion Results (RAN 4 #88bis) 1. Coverage analysis and Link budget simulation assumptions

## Slide 3: Agreement 1: WF on Parameter for Link Budget Evaluation
 |  | 4Rx HHUE (Outdoor browsing) | 4Rx HHUE (Passenger Holding browsing) | 4Rx HHUE (Dash board) | 2Rx VUE
Antenna Configuration |  | 4Rx/2Tx | 4Rx/2Tx | 4Rx/2Tx | 2Rx/2Tx
BS Antanna Gain1 [dBi] |  | 18 | 18 | 18 | 18
UE Antenna Gain | Antenna system gain per element 2,5 [dBi] | -7.5 | -7.5 | -4.5 | -3
 | Penetration Loss3 [dB] | 0 | 9 | 9 | 0
 | Total [dB] | -9.5 -7.5 | -18.5 -16.5 | -15.5 -13.5 | -3
Fading Margin [dB] |  | [9] | [9] | [9] | [9]
Interference Margin [dB] |  | 3 | [3] [ 0.5] | [3] [0.5] | 3
DL | BS Tx Power [dBm] | 46 | 46 | 46 | 46
 | UE REFSENS4 [dBm] | -87.4 | -87.4 | -87.4 | -84.7
Note 1. E/// proposed during AH. Note 2. Antenna system gain per element = (ant. efficiency + directivity) + cable/Body Loss Note 3. O2I car penetration loss is based on TR38.901 7.4.3.2 Note 4. 4 Rx REFSENS = 2 Rx REFSENS (TS38.101-1 Table 7.3.2-1) + ΔRIB,4R (TS38.101-1 Table 7.3.2-2) Note 5: To be confirmed by feedback from 5GAA on definition of the term ‘baseline’ for vehicle antenna performance |  |  |  |  | 

## Slide 4: 5GAA response to 3GPP LS R4-1814315
LS RP-181522 provides average antenna gain values of typical antenna implementations in series cars to be taken as the baseline assumption in the study in 3GPP RAN4. The origin of these antenna gain values are passive antenna measurements and include cable losses.
Elevation range of 0-30° (measured from ground to sky, equal to theta=60-90° of measurement / simulation systems) is relevant for vehicular mobile communication.
5GAA recommends 3GPP RAN4 to exceptionally take the automotive methodology to characterise vehicular antennas into account and not to expect similar methods and metrics as of handheld UEs to be applied.

## Slide 5: Agreement 2: Conclusion on parameters for Link Budget Evaluation
In RAN 4 #88bis, -3dBi is initially used for vehicle UE antenna gain (as provided by 5GAA LS). Conclusion of RAN 4 study is subject to:
Provision of antenna system gain per element by means of TRP* measurements (with no stringent time budget, if possible RAN #82, per note 2) by OEMs in 3GPP or 5GAA
TRP is used to infer gain of the system, although receiver link budgets are discussed
New: Antenna gain values provided by 5GAA (elevation from 0 ° to 40 °) is used.
In note 2: Detailed values for n7/n41 are based on follows:
HH-UE : https://www.gsma.com/newsroom/wp-content/uploads/TS-24-v3-01.pdf
Vehicle UE : 5GAA LS (R4-1811528)

## Slide 6: Offline Discussion Results (13-Nov-2018) 2. Conclusion on Methods to distinguish vehicular UE

## Slide 7: Agreement 3: Conclusion on Methods to distinguish vehicular UE
Conclusion 1: “Declare and differentiate 2 RX Vehicle UE through 3GPP compliance testing via GCF/other certification organizations.
  3GPP do not need to consider UE outside 3GPP compliance.
Conclusion 2: For Vehicle UE, network based authorization is required. The actual implementation of authorization method does not impact 3GPP decision on 2 RX exception.
  A possible solution to implement conclusion 2 is based on SPID value in 36.300/38.300 (Annex I), targeting rel-15 and beyond, to be captured in TR 38.826.
  Other authorization proposals in RAN plenary is not precluded.
  RAN 4 recommends RAN to consider other authorization proposals without additional RAN signaling.
Conclusion 3: RAN 4 agree on existing RRC signaling for # of MIMO layers to differentiate 2 RX UE from 4 RX UE
Conclusion 4: Definition of Vehicular mounted UE in TS 38.101
Final Conclusion: 2 RX Vehicular UE can be distinguished based on conclusion 1+2+3+4, to be captured in TR 38.826

## Slide 8
Conclusion 4: Definition of Vehicular UE in TS 38.101
Huawei: Vehicle mounted UE: A UE mounted in a vehicle with external antennas, with the average effective antenna gain including the total loss of all components after the chipset unit antenna connector and the gain of the external antenna no less than -3dBi.
Samsung: A UE mounted in a vehicle with external antennas that have better than 0 dBi effective gain value, compared to handheld UE
VW: Vehicular UE: A UE embedded in a vehicle. A vehicular UE with no integrated antennas for eMBB purposes.
VDF: Vehicular UE: A UE embedded in a vehicle with no integrated antennas for eMBB service with baseline antenna gain -3dBi