## Slide 1: WF on 2Rx exception for NR vehicle UE
SAMSUNG, LG Electronics, Volkswagen AG
3GPP TSG-RAN WG4 #89 Meeting
Spokane, Washington, U.S., 12th – 16th Nov., 2018 Agenda Item: 10.3.2
R4-1816650

## Slide 2: 1. Conclusion on Coverage analysis and Link budget simulation assumptions

## Slide 3: Agreement 1: Table 1. Parameter for Link Budget Evaluation
 |  | 4Rx HHUE (Outdoor browsing) | 4Rx HHUE (Passenger Holding browsing) | 4Rx HHUE (Dash board) | 2Rx VUE
Antenna Configuration |  | 4Rx/2Tx | 4Rx/2Tx | 4Rx/2Tx | 2Rx/2Tx
BS Antanna Gain1 [dBi] |  | 18 | 18 | 18 | 18
UE Antenna Gain | Antenna system gain per element 2 [dBi] | -7.5 | -7.5 | -4.5 | -3
 | Penetration Loss3 [dB] | 0 | 9 | 9 | 0
 | Total [dB] | -9.5 -7.5 | -18.5 -16.5 | -15.5 -13.5 | -3
Fading Margin [dB] |  | 9 | 9 | 9 | 9
Interference Margin [dB] |  | 3 | [3] 0.5 | [3] 0.5 | 3
DL | BS Tx Power [dBm] | 46 | 46 | 46 | 46
 | UE REFSENS4 [dBm] | -87.4 | -87.4 | -87.4 | -84.7
Note 1. E/// proposed during AH. Note 2. Antenna system gain per element = (ant. efficiency + directivity) + cable/Body Loss Note 3. O2I car penetration loss is based on TR38.901 7.4.3.2 Note 4. 4 Rx REFSENS = 2 Rx REFSENS (TS38.101-1 Table 7.3.2-1) + ΔRIB,4R (TS38.101-1 Table 7.3.2-2) |  |  |  |  | 
In note 2: Detailed values for n7/n41 are based on follows:
HH-UE : https://www.gsma.com/newsroom/wp-content/uploads/TS-24-v3-01.pdf
Vehicle UE : 5GAA LS (R4-1811528)

## Slide 4: 5GAA response to 3GPP LS R4-1814315
LS RP-181522 provides average antenna gain values of typical antenna implementations in series cars to be taken as the baseline assumption in the study in 3GPP RAN4. The origin of these antenna gain values are passive antenna measurements and include cable losses.
Elevation range of 0-30° (measured from ground to sky, equal to theta=60-90° of measurement / simulation systems) is relevant for vehicular mobile communication.
5GAA recommends 3GPP RAN4 to exceptionally take the automotive methodology to characterise vehicular antennas into account and not to expect similar methods and metrics as of handheld UEs to be applied.

## Slide 5: Agreement 2: Conclusion on parameters for Link Budget Evaluation
TRP measurements for vehicular antennas are not available in automotive industry (R4-1816254)
-3dBi antenna gain value provided by 5GAA (R4-1811528) is used for concluding coverage analysis
Details about antenna gain in elevation angle 0° to 40° (5GAA: R4-1816254, car OEM in 3GPP: R4-1816654) is used for concluding coverage analysis.

## Slide 6: Final Conclusion on Coverage analysis
Based on meeting minutes in R4-1816649
Conclusion 1:
Based on MCL from link budget results, we can see following:
The coverage with 2 Rx vehicular UE is comparable with 4 Rx hand-held UE based on the agreed parameters for link budget analysis [R4-1814775].

## Slide 7: 2. Conclusion on Methods to distinguish vehicular UE

## Slide 8: Agreement 3: Conclusion on Methods to distinguish vehicular UE
Conclusion 2.1: “Declare and differentiate 2 RX Vehicle UE through 3GPP compliance testing via GCF/other certification organizations.
  3GPP do not need to consider UE outside 3GPP compliance.
Conclusion 2.2: For Vehicle UE, network based identification is required for authorization purposes. The actual implementation of network based identification method does not impact 3GPP decision on 2 RX exception.
  A possible solution to implement conclusion 2.2 is based on SPID value in 36.300/38.300 (Annex I), targeting rel-15 and beyond, to be captured in TR 38.826.
  Other network based identification proposals in 3GPP are not precluded.
  RAN 4 recommends RAN to consider other network based identification proposals without additional RAN signaling.
Conclusion 2.3: RAN 4 agree on existing RRC signaling for # of MIMO layers to differentiate 2 RX UE from 4 RX UE
Conclusion 2.4: Definition of Vehicular mounted UE in TS 38.101-1 for FR1
Conclusion 3:
2 RX Vehicular UE can be distinguished based on conclusion 2.1+ 2.2+ 2.3 +2.4, to be captured in TR 38.826

## Slide 9
Section 3 in TS 38.101-1
Vehicular UE: A UE which is integrated in a vehicle with externally radiating antennas for NR operating bands.
Note: Integrated UE does not refer to other UE form factors placed inside the vehicle.
Section 7 in TS 38.101-1 (Draft CR to TS 38.101-1, R4-1814767):
Note 1: Four Rx antenna ports shall be the baseline for this operating band. The exception is allowed for vehicular UE in this operating band, for which the requirements with two Rx antenna ports can be applied. 2Rx vehicular UE typically has better antenna system gain than other UE (eg: Section 5 and 6 in [TR 38.826])
Agreement 4: definitions and notes in TS 38.101-1