## Slide 1: WF on channel spacing for intra-band contiguous CA
Intel
3GPP TSG-RAN4 Meeting #89
Spokane, USA, 12 - 16 November 2018
R4-1816665

## Slide 2: Background
In (R4-1814597) raised the concern that in the current RAN4 spec there is ambiguity on whether or not channel spacing remains unchanged during SCS reconfiguration.

## Slide 3: Channel Spacing intra-band contiguous CA (1)
Channel spacing should remain fixed when SCS changes. The ARFCN should not dynamically change with the SCS signaled by scs-SpecificCarrierList IE defined in TS 38.331.
Propose to capture in TS38.101-1, 38.101-2 with the following text:
  “where BWChannel(1) and BWChannel(2) are the channel bandwidths of the two respective NR component carriers according to Table 5.3.2-1 with values in MHz. and the GBChannel(i) is the minimum guard band defined in sub-clause 5.3.3, while µ1 and µ2 are the subcarrier spacing configurations of the component carriers as defined in TS 38.211. The channel spacing for intra-band contiguous carrier aggregation can be adjusted to any multiple of least common multiple of channel raster and sub-carrier spacing less than the nominal channel spacing to optimize performance in a particular deployment scenario and will not dynamically change with the SCS.”

## Slide 4: Channel Spacing intra-band contiguous CA (2)
Propose to capture in TS38.104 with the following text:
  “where BWChannel(1) and BWChannel(2) are the channel bandwidths of the two respective NR component carriers according to Table 5.3.2-1 with values in MHz. and the GBChannel(i) is the minimum guard band defined in sub-clause 5.3.3, while µ1 and µ2 are the subcarrier spacing configurations of the component carriers as defined in TS 38.211. The channel spacing for intra-band contiguous carrier aggregation can be adjusted to any multiple of least common multiple of channel raster and sub-carrier spacing less than the nominal channel spacing to optimize performance in a particular deployment scenario and shall not dynamically change with the SCS.”