## Slide 1: WF on known cell condition for handover FR2
R4-1816672
Document for: Approval
3GPP TSG-RAN WG4 RAN#89
Spokane, US, 12th – 16th Nov, 2018
Agenda: 7.11.5.2
Nokia, Nokia Shanghai Bell, Ericsson, […]

## Slide 2: Background
For handover with FR1 target cell, known cell condition for FR1 cell has been defined to be:
  In the interruption requirement a cell is known if it has been meeting the relevant cell identification requirement during the last 5 seconds otherwise it is unknown. Relevant cell identification requirements are described in Clause 9.2.5 for intra-frequency handover and Clause 9.3.1 for inter-frequency handover.
For Scell activation, SCell in FR1 is known if it has been meeting the following conditions:
  - During the period equal to max([5] measCycleSCell, [5] DRX cycles) for FR1 before the reception of the SCell activation command:
  - the UE has sent a valid measurement report for the SCell being activated and
  - the SSB measured remains detectable according to the cell identification conditions specified in section 9.2 and 9.3.
  - the SSB measured during the period equal to max([5] measCycleSCell, [5] DRX cycles) also remains detectable during the SCell activation delay according to the cell identification conditions specified in section 9.2 and 9.3.

## Slide 3: Background
For PScell activation, PSCell is known if it has been meeting the following conditions:
  During the last 5 seconds before the reception of the NR PSCell configuration command:
    the UE has sent a valid measurement report for the NR PSCell being configured and
    One of the SSBs measured from the NR PSCell being configured remains detectable according to the cell identification conditions specified in section 9.3 of TS 38.133 [50],
  One of the SSBs measured from NR PSCell being configured also remains detectable during the NR PSCell configuration delay according to the cell identification conditions specified in section 9.3 of TS 38.133 [50].

## Slide 4: Way forward
For RAN4#90 meeting, RAN4 intends to find a known cell condition for FR2 target cell, which takes into account scenarios in which the UE is able to use prior information from measurement results on suitable TX and/or RX beam to use initially for the target cell.