## Slide 1: WF on RRC and MAC based BWP switching
R4-1816689
Document for: Approval
3GPP TSG-RAN WG4 RAN#89
Spokane, US, 12th – 16th Nov, 2018
Agenda: 7.11.7.5
Nokia, Nokia Shanghai Bell, Mediatek Inc. […]

## Slide 2: Background
RRC-based BWP switch is a mandatory feature for 6-1 capability UE in Rel-15, but before RAN4#89 meeting, RAN4 has not defined delay or interruption requirements for RRC-based BWP switch because of lacking RAN2 agreements.
In 3GPP TSG-RAN WG2 Meeting #104, RAN2 has sent an LS to RAN4 in R4-1816420 concerning RRC- and MAC-based BWP switch. The contents of the LS are repeated below:

## Slide 3: Total RRC-based BWP switch delay
Total RRC-based BWP switch delay from slot n which is the last slot containing RRC reconfiguration command to the slot n+TBD where UE can send RRC reconfiguration complete is shown in Figure 1.
Figure1: Total RRC-based BWP switch delay
Total BWP switch delay equals TRRC_delay + TBWPswitchDelayRRC
  RRC processing delay TRRC_delay will be defined by RAN2.
  BWP switch delay TBWPswitchDelayRRC will be defined by RAN4. See next slide.
The UL grant uncertainty for transmitting RRCReconfigurationComplete due to TA and TA_offset during RRC based BWP switching is FFS
RRC processing delay
BWP switch delay RRC
RRC Reconfiguration Complete
RRC Reconfiguration Command

## Slide 4: BWP switch delay for RRC-based BWP switch
For RRC-based BWP switch, the BWP switch delay TBWPswitchDelayRRC is defined for the following two cases:
    Case 1: BWP switch to another existing BWP configuration
    No change to any of the existing configured BWPs
    Case 2: BWP switch to a new BWP configured by the same RRC re-configuration signaling
    New BWP configurations are added and activated with different parameters to current active BWP through RRC reconfiguration
The BWP switch delay for Cases 1 and 2 is FFS.

## Slide 5: For further study
RRC-based BWP switch
  FFS whether to define core interruption requirements
MAC-based BWP switch
  FFS whether to define core delay requirements
  FFS whether to define core interruption requirements