## Slide 1: WF on test methods for FR2 RRM testing
Qualcomm Incorporated, AT&T, Docomo, Verizon, Telstra, Keysight, Anritsu, Rohde & Schwarz
3GPP TSG-RAN WG4 Meeting RAN4#89 R4-1816742
Spokane, US, 12-16 Nov, 2018

## Slide 2: Test method for Scenario #1 (Agreement from NR Test Methods SI ad-hoc meeting notes)
SCENARIO #1: 1 AOA WITH SIGNAL COMING FROM THE UE RX BEAM PEAK DIRECTION
  From test methodology perspective support Scenario#1 with Type 1 RRM test cases ( UE uses “Fine” RX beams)
    Mode 1: TE emulates target SNR conditions
      Use Noc level of -155dBm/Hz for PC3 UE in n260
      Note: the feasible SNR will be provided by TE vendors and included in TR 38.810
    Mode 2: TE emulates desired signal only without artificial noise
  From test methodology perspective support Scenario#1 with Type 2 RRM test cases ( UE uses “Rough” RX beams)
    Mode 1: TE emulates target SNR conditions
      Noc = Noc1 + Y dB
        Noc1 is the Noc level for the case of Scenario 1 and Type 1 RRM test cases
        Y = [7] dB for PC3 UE (using fine beam peak direction during the test, see slide 4)
    Mode 2: TE emulates desired signal only without artificial noise

## Slide 3: Test method for Scenario #2 (Agreement from NR Test Methods SI ad-hoc meeting notes)
SCENARIO #2: 1 AOA WITH SIGNAL COMING FROM THE NON UE RX BEAM PEAK DIRECTION
  From test methodology perspective support Scenario#2 with Type 1 RRM test cases ( UE uses “Fine” RX beams)
    Mode 1: TE emulates target SNR conditions
      Noc = Noc1 + X dB
        Noc1 is the Noc level for the case of Scenario 1 and Type 1 RRM test cases
        X derived based on EIS spherical coverage requirement (i.e. difference between the peak EIS and [50]%-tile EIS)
    Mode 2: TE emulates desired signal only without artificial noise
  From test methodology perspective support Scenario #2 with Type 2 RRM test cases ( UE uses “Rough” RX beams)
    Tested directions:
        Option 2A: Any single direction which is covered by 50% percentile EIS spherical coverage of the DUT
    Mode 1: TE emulates target SNR conditions
      Noc = Noc1 + X + Z dB
        Noc1 is the Noc level for the case of Scenario 1 and Type 1 RRM test cases
        X derived based on EIS spherical coverage requirement (i.e. difference between the peak EIS and [50]%-tile EIS)
        Z is [8] (Use [8] dB intermediate value. Further refine the values in RAN4 #90 (as a part of maintenance). Any values can be considered based on companies’ simulation results (see slide 4).
    Mode 2: TE emulates desired signal only without artificial noise

## Slide 4: Antenna gain difference between the rough and fine beams for Noc derivation
Antenna gain difference between the rough and fine beams for Noc derivation for RRM test methods for PC3 UE
  Gain difference in the RX beam peak direction (scenario #1): Y=[7] dB (Applied for slide 2)
  Peak antenna gain difference: [5] dB (Applicability is FFS)
  Minimum absolute gain of rough beams over the best 50% of the sphere in which spherical EIS is met relative to the gain of 50%-tile CDF of fine beams antenna gains:
    Use Z=[8] dB intermediate value (Applied for slide 3)
    Further refine the values in RAN4 #90 (as a part of maintenance). Any values can be considered based on companies’ simulation results.
    Companies are encouraged to bring simulation results to compare fine/rough antenna gain difference over the best 50% of the sphere in which spherical EIS is met. Simulation assumptions:
      Reuse RF room assumptions for PC3 UE spherical coverage analysis (R4-1801202 slides 5 & 8)
        Results are provided at least for the case of 1 panel and 4x1 array. If this case does not meet spherical EIS requirements, companies shall provide results for other cases where UE meets spherical EIS requirements.
      UE RX codebooks:
        Fine beam codebook: Implementation specific
        Rough beam codebook: At least results for 1 beam codebook are provided

## Slide 5: Test method for Scenario 3(2AoAs)
SCENARIO #3: 2 AOAS
  From test methodology perspective support Scenario#3 with the following method for tests with two UE RX fine beams or two rough beams cases.
  Mode 1:
    Test directions:
      Both signals come from the non RX beam peak directions
      The angle between two probes should match the relative probe spacing of 30, 60, 90, 120, 150 and UE is in the directions in which the UE RRM test cases can be performed.
      Both directions which are covered by [50%] percentile EIS spherical coverage of the DUT
    Noc level:
      Fix the identical noise level for two active probes, then control the desired signal level to reach target SNR or SINR at reference point.
      The noise level is the same as that for 1AoA with non-peak beam direction in Scenario 2 based on the UE beam type (fine/rough).

## Slide 6: Test method for Scenario 3(2AoAs)
SCENARIO #3: 2 AOAS (cont.)
  Mode 1:
    SINR control:
      Case 1: TDM transmissions from 2 probes
        Each probe transmits both signal and artificial noise in TDM manner
        SNR would be the same as the value in 1AoA case with non-peak beam direction in Scenario 2 based on the UE beam type(fine/rough).
      Case 2: Simultaneous transmissions from 2 probes
        The lower bound of maximum feasible SINR
          Use maximum gain difference between the 2 directions when signals and artificial noise are received on the same UE Rx beam to determine SINR
            The antenna gain difference for dual directions on the same UE RX beam (decided by D defined in slide 8 and 9G1 and G2 in slide 7) will be further discussed in the RRM room as a part of performance requirements definition
          Lower bound of SINR can be derived based on the Equations in slide 7.
        The upper bound of maximum feasible SINR
          Consider the ideal rejection from the direction of interfering probe.
          Upper bound of SINR is the SNR transmitted from signal probe.

## Slide 7: Test method for Scenario 3(2AoAs)
SCENARIO #3: 2 AOAS (cont.)
  Mode 2:
    Support methodology for RRM tests without any artificial noise and with signal levels derived based on the defined side conditions for 2AOAs scenario.
      Case 1: TDM transmission for 2 probes
        Each probe only transmits signal without artificial noise
        SNR can be derived as the ratio of the desired signal power level and UE noise level
      Case 2: Simultaneous transmission for 2 probes
        The lower bound of maximum feasible SINR
          Use maximum gain difference between the 2 directions when signals are received on the same UE Rx beam to determine SINR
            The antenna gain difference for dual directions on the same UE RX beam (decided by D defined in slide 8, and 9G1 and G2) will be further discussed in the RRM room as a part of performance requirements definition
          Lower bound of SINR can be derived based on the Equations in slide 8.
        The upper bound of maximum feasible SINR
          Consider the ideal rejection from the direction of interfering probe.
          Upper bound of SINR is the SNR transmitted from signal probe.

## Slide 8: Test method for Scenario 3(2AoAs): SINR Equation for Mode 1 case 2
Signal probe: P1; Interference probe: P2
Since would be at least 6dB higher than Noise floor, then we can have the following equation to derive the SINR1
, where D=G2/G1 is the antenna difference for dual directions.
Simultaneous transmission

## Slide 9: Test method for Scenario 3(2AoAs): SINR Equation for Mode 2 case 2
Signal probe: P1; Interference probe: P2
Assume > Noc level, and Noc level would be at least 6dB higher than Noise floor, then we can have the following equation to derive the SINR1
, where D=G2/G1 is the antenna difference for dual directions.
Simultaneous transmission

## Slide 10: Noc level for multi-band devices and CA case
Noc levels in the WF are derived for the case of single carrier and single band device. The Noc levels shall be further adjusted for multi-band devices and CA case to take into account corresponding EIS relaxations defined in TS 38.101-2.

## Slide 11: Appendix
 | Fine/Rough beam | SNR1 (dB) | SNR2 (dB) | D (dB) | SINR1 (dB)
n257 | Fine | 13 | -6 | 8 | 3.5
 | Rough | 8 | -6 | 8 | -1.5
Example for lower bound of maximum feasible SINR control for Mode 1 case 2