## Slide 1: WF on NR MIMO OTA
CAICT, Spirent, Keysight
3GPP TSG-RAN WG4 Meeting #90 R4-1901383
Athens, GR, 25th Feb – 1st March, 2019
Agenda item: 10.2.1
Document for: Approval

## Slide 2: BS antenna pattern
BS antenna pattern assumption:
  Use example pattern in TR38.901 Table 7.3-1 for both FR1 and FR2, e.g. 3dB = 65, SLAv = 30dB, GE,max =8 dBi;
  2 transmitting beams for FR1
      Two strongest beams
  1 transmitting beam for FR2- strongest beam to strongest cluster
  For FR1：A code book of 60 fixed beams is constructed to a grid of five elevation angles from –20 to +20 with 10 steps and 12 azimuth angles from –80 to +80 with ~15 steps
  For FR2：A code book of 128 fixed beams is constructed to a grid of eight elevation angles from –25 to +25 with ~7.1 step size and 16 azimuth angles from –60 to +60 with 8 step size

## Slide 3: Channel model simulation
  CDL-A and CDL-C are selected for both FR1 and FR2 for simulation assumption
  3.5 GHz and 28GHz is set as center frequency (fc) in TR38.901 for FR1 and FR2 channel model scaling, respectively.
    Study the impact to FR1 range
  FR1 RMS delay spread: UMi with 100ns, Uma with 365ns
  FR2 RMS delay spread: UMi with 60ns, InO with 30 ns

## Slide 4: Channel model scaling procedure
  Follow the procedure in TR38.901 on how to scale the channel model to map the Scenarios
    Option 1: Scaling per TR38.901
    Option 2: Rotate AoDs/ZoDs and scale to CDL-A and CDL-C using the methods in 38.901 (section 7.7.5.1) to make them fit the median values in 38.901 Table 7.5-6 for the accepted scenarios
  Channel model simplification is needed, how to simplify is FFS

## Slide 5: NEXT actions
CE vendors are encouraged to provide the channel models with and without BS filtering and simplification.
Estimation of number of probes based on the provided channel model is encouraged.
RAN4#90bis meeting will make decision on the channel model from Option 1 or Option 2 in slide 4.