## Slide 1: WF on MPR/AMPR issue for intra-band ENDC for B41/n41
Huawei, CMCC, [Skyworks]
3GPP TSG-RAN WG4 #90 Meeting
Athens, Greece, 25th Feb. – 01st March, 2019
R4-1902190

## Slide 2: Background
Current AMPR requirements for intra-band contiguous and non-contiguous ENDC B41/n41 only considers additional RF requirements (e.g. ASEM, ASE) under NS_04
There is no MPR/AMPR requirements which comply with general RF requirements (e.g. SEM, SE)
This WF only considers MPR/AMPR requirements complied with general RF requirements.

## Slide 3: Way forward
For both intra-band contiguous and non-contiguous ENDC scenario in any band, define generic MPR requirement without consideration of filter deriving from B41/n41 ENDC AMPR requirment for NS_04
Define new NS and A-MPR requirement for band specific requirment or optimized MPR requirment with the consideration of filter.
MPR/A-MPR requirements are captured in Rel-15 specification.

## Slide 4: Background: Deriving Back-off from current NS_04 A-MPR
For contiguous
  In NS_04 case we have AMPR for IM3 cases:
    -13dBm/MHz OOB region
    -25dBm/MHz OOB region
  In general case
    -13dBm/MHz SEM region is subject IMD3
    -25dBm/MHz SEM region is subject IMD5
    -30dBm/MHz in spurious emission is subject to IMD5
For non-contiguous
  In NS_04 case we have AMPR for IM3 cases:
    -13dBm/MHz OOB region
    -25dBm/MHz OOB region
  In general case
    -13dBm/MHz SEM region is subject IMD3
    -25dBm/MHz SEM region is subject IMD3
    -30dBm/MHz in spurious emission is subject to IMD3

## Slide 5: Way forward
NS_04 -13dBm/MHz AMPR equation can be used for contiguous ENDC back-off
For non-contiguous where -30dBm/MHz is IMD3 reuse NS_04 -25dBm/MHz AMPR + 3dB
Above requirements can be used for both PC3+PC3=PC3 and PC2+PC2=PC2 cases
AMPR/MPR based on this is introduced in the specification in brackets to allow refinement in upcoming meetings