## Slide 1
WF on FBW
NEC
R4-1902244
3GPP TSG-RAN WG4 Meeting #90 Athens, Greece, 25th Feb – 1st Mar, 2019
Agenda item: 6.9.2.1

## Slide 2
Background
In RAN4 #90, FBW was discussed based on [1].
  Corresponding draft CRs were submitted in [2] and [3].
After the 1st round on-line discussin, chairman provided the note that says;
  Companies are encouraged to discuss the following aspects:
  - In Rel-15, for band n77, BS vendors are allowed to declare up to 3 EIRP values
  - For other bands (including new bands), FFS on more than 3 declarations in Rel-16 and beyond.

## Slide 3
Discussion
Discussion to support up to 3 declaration
  It is allowed to declare up to 2 EIRP values for the band with FBW of more than 6%, why further declaration is not allowed for the sub-band with FBW of more than 6%?
  Contribution of antenna directivity was not considered to define the accuracy requirements. There is little room to allow additional contributions in ±2.2 dB accuracy
    → Compromized that the number of declarations is up to 3 in Rel-15
    → Up to 3 declarations are applied only to n77 in Rel-15
Discussion to disagree up to 3 declaration
  The antenna aperture sets the directivity but it is not the only factor in the radiated EIRP so it is not clear that the EIRP will increase in the simple way only looking at the antenna aperture indicates.
  Data sheet of antenna product was shown which shows less gain variance than calculated by directivity due to fixed aperture
  → 2 declarations is sufficient

## Slide 4
Way Forward
  Companies are encouraged to study the actual antenna gain variation caused by frequency difference
  Consider revising TR 38.817-02

## Slide 5
References
[1] R4-1900743, Discussion on FBW, NEC
[2] R4-1900744, Draft CR to TS 38.104: Radiated transmit power requirement with wideband operation (9.2), NEC
[3] R4-1900745, Draft CR to TS38.141-2: Radiated transmit power requirement with wideband operation (6.2), NEC

## Slide 6
Appendix
EIRP accuracy requirement (BS type 1-H, 1-O, normal condition)
  ±2.2 dB was agreed based on the assumption
    [dB]
    where:
    - is the maximum conducted output power error at the transceiver unit output.
    - is the variation in main beam EIRP due to beamforming errors caused by phase error at the transceiver unit output.
    - is the variation due to the error in the passive elements, the RDN, the antenna array gain errors, mismatch errors and insertion losses variations.
BS output power requirement (BS type 1-H, normal condition)
  ±2.0 dB
OTA output power requirement (BS type 1-O, normal condition)
  ±2.0 dB