## Slide 1: WF on FR2 Transient Period
R4-1902286
3GPP TSG-RAN WG4 Meeting # 90
Athens, Greece, 25th February – 1st March 2019

## Slide 2: Background
During RAN4#90 meeting, OTA TxOFF power and transient time was discussed based on [1-9]. References included comments but no suggested measurement methodology
One proposal was to determine if there was sufficient sensitivity to measure to a limit of -36dBm/MHz + 27dB (estimated Txon antenna gain, mentioned in R4-1900463)

## Slide 3: Txoff Link Budget Analysis w/ 27dB Txoff Relaxation (example)
DUT
Tx emission
TRP limit:
-36 dBm / MHz
Txoff gain
27dB
OTA loss
68dB @ 28 GHz
71dB @ 40 GHz
10dB gain
Cable Loss (4m cables)
10 dB @ 28GHz
12 dB @ 40GHz
Avg noise level
-162dBm + 60dB = -102 dBm @ 28GHz
-156dBm + 60dB = -96 dBm @ 40GHz
0 dB Input atten
Low Noise Path
Noise Floor Extension
RMS detector
1 MHz RBW
)2
Chamber
Broadband IF Clipping level
P1dB= ~ -30dBm//MHz
in 1 MHz RBW
Tx EIRP levels:
+50 to +75 dBm / 100 MHz
Txon Power out of OMT
- 8 to +17 dBm/100 MHz @ 28 GHz
-11 to +14 dBm/100 MHz @ 40 GHz
Assumptions: CATR (~4.5mx3mx3m)
~1m Quiet Zone
~ 2m focal length
Receiver
OMT
Switch/Cable Loss
2 dB @ 28GHz
4 dB @ 40GHz
System Avg
noise level at OMT
-90 dBm @ 28GHz
-80 dBm @ 40GHz
Txoff emission
at OMT
-67 dBm/MHz @ 28GHz
-70 dBm/MHz @ 40GHz
Broadband IF Clipping level
P1dB= ~ -20dBm//MHz
~ -16dBm/MHz
Reference plane
V
H
Gate trigger
to receiver

## Slide 4: Measurement budget - summary
Using the assumption in the previous slide
  The TX OFF level at the analyzer input is -86dBm/1MHz @ 40GHz
  The analyzer sensitivity is -96dBm/MHz @ 40GHz
  The TX OFF level at the analyzer input is -79dBm/1MHz @ 28GHz
  The analyzer sensitivity is -102dBm/MHz @ 28GHz
Under these conditions there is sufficient margin to measure the TX OFF level.

## Slide 5: Agreements
If it assumed that the OFF antenna gain is equal to the ON antenna gain (27dBi in this example) then the link budget for measuring Txoff power (with +27dBi antenna gain) demonstrates sufficient system sensitivity for the CATR-based system with <= 2m focal length and direct far-field measurement systems with measurement distances <= 2m.
Assuming OFF antenna gain is equal to ON antenna gain is accepted to be ‘best case’ however as TX transient can only be measured under this assumption RAN4 agrees that this assumption will be used to estimate an EIRP level conformance level from the TRP core specification level for the purpose of the transient test.
Agreements
  Measuring TX OFF power level with assumption OFF ant gain = ON antenna gain (= full array gain) is feasible
  The conformance EIRP OFF level for the transient test will be Core TRP level plus the ON antenna directivity.

## Slide 6: Way Forward
More work needed to study the test system specifically:
  verify measurement receiver/spectrum analyzer will be out of compression during Txoff period when using TM 1.1 test signal.
  Transient period measurement still needs to be developed.
  MU table needs to be developed.
CR’s prepared next meeting
  to capture the background in the TR
  To capture the test requirement and test procedure in the conformance specification

## Slide 7: References
[1] R4-1900234 Further discussion and test result on FR2 OTA TDD transient time
[2] R4-1900463 Discussion on EIRP OFF power for measuring FR2 transient period
[3] R4-1900492 Further discussion on FR2 transient period measurement
[4] R4-1900493 Comments on WF (R4-186577) concerning options for measuring FR2 OTA Txoff power and Txon/off transient.
[5] R4-1900741 Discussion on OTA OFF power and transient period requirements for BS type 2-O
[6] R4-1901543 Discuss FR2 TX OFF and ON/OFF transient
[7] R4-1901544 Draft CR to TS 38.141-2 update TX OFF measurement procedure.
[8] R4-1901545 CR to TR 38.817-02 - capture FR2 TX ON/OFF transient background
[9] R4-1901549 Discuss FR2 TX OFF MU