## Slide 1: Way forward on NR PBCH demodulation requirements
CMCC
3GPP TSG-RAN WG4 Meeting #90 R4-1902405
Athens, GR, 25th Feb – 1st March, 2019

## Slide 2: Background
Agreed way forward in RAN4#88bis:
  R4-1814240 Way forward on NR PBCH demodulation requirements
Agreed way forward in RAN4#90
  R4-1816490 Way forward on NR PBCH demodulation requirements

## Slide 3: Way forward
Issue 1: Necessity of 4Rx PBCH test cases
  Option 1: introducing 4Rx PBCH test cases
    If 4Rx PBCH requirements is introduced,
      whether to apply 4Rx PBCH requirements is up to UE declaration
      Note the PBCH demodulation requirements do not need to be tested in RAN5 as same as LTE PBCH demodulation requirements. (i.e. no conformance requirements)
  Option 2: not introducing 4Rx PBCH test cases
Proposal:
  Introduce PBCH requirements with and without knowledge of SSB index (Option 2)
    whether to apply 4Rx PBCH requirements is up to UE declaration
    Note the PBCH demodulation requirements do not need to be tested in RAN5 as same as LTE PBCH demodulation requirements. (i.e. no conformance requirements)

## Slide 4: Way forward
Issue 2: UE assumption on DMRS SSB index acquisition for PBCH demodulation
  Option 1: Derive requirements assuming without knowledge of SSB index
  Option 2: Derive two kinds of requirements with and without knowledge of SSB index
Proposal:
  Introduce PBCH requirements assuming with and without knowledge of SSB index. (Option 2)
    PBCH requirements is derived with the combination of SSB index detection probability and MIB decoding probability

## Slide 5: Way forward
Deriving SNR requirements
  Define tentative SNR requirements for agreed test cases with []
  The agreed SNR values still can be updated if more results collected from companies in future meeting
  SNR=average of IM results among companies + extra margin(if needed)
  For test cases where the span among companies’ results is within 2.5 dB , margin is 0.5dB
  For test cases where the span is larger than 2.5dB, the margin can be discussed case by case.

## Slide 6: Alignment results summary
Note: Based on alignment results, test cases marked green with impairments results will be specified with square brackets. Test cases marked yellow will be specified as TBD and companies will further check the results in next meeting.

## Slide 7: Impairment results summary
Note: Based on alignment results, test cases marked green with impairments results will be specified with square brackets. Test cases marked yellow will be specified as TBD and companies will further check the results in next meeting.

## Slide 8: Simulation assumptions
Parameters | Unit | Value
Cell ID |  | 0
CP length |  | Normal
Number of SS/PBCH blocks within an SS burst set periodicity |  | 1
SS/PBCH block index |  | 0
SS burst periodicity | ms | 20
MIB size | bits | 24
PBCH payload size (including 24 bits CRC and 8 bits of SS/PBCH location information) | bits | 56
Receiver assumption |  | LMMSE
Table 1: common parameters
For PBCH demodulation requirements
  The simulation assumptions in Table 1 are subject to common setup
  The simulation assumptions in Table 2 are subject to simulation alignment

## Slide 9: Simulation assumption
Parameters | Test 1 | Test 2 | Test 3 | Test 4
Frequency Range | FR1 | FR1 | FR2 | FR2
Channel Bandwidth | 10MHz | 40MHz | 100MHz | 100MHz
SS/PBCH SCS | 15kHz | 30kHz | 120kHz | 240kHz
SS Block pattern (Note 1) | Case A | Case B Case C | Case D | Case E
Antenna Configuration | 1x2 1x4 | 1x2 1x4 | 1x2 | 1x2
Propagation channel (Note 2) | TDLC300-100 | TDLA30-10 | TDLA30-300 | TDLA30-75
Assumption on DMRS SSB index acquisition | a: SS/PBCH block index is known b: SS/PBCH block index is not known |  |  | 
Table 2: Test cases for PBCH demodulation
Note 1: Depending on the operating band. Refers to TS38.101-1 Table 5.4.3.3-1 for which band uses which pattern
Note 2: Use PDP specified in TS38.901