## Slide 1: WF on NR-U BS RF requirements
Nokia, Nokia Shanghai Bell
R4-1902505
3GPP TSG-RAN WG4 Meeting #90
Athens, Greece, 25th February – 1st March 2019

## Slide 2: Background
During RAN4#90 meeting the following contributions were discussed on NR-U BS RF requirements:
R4-1900664, BS requirements on wideband carrier operation for NR-U, Huawei, HiSilicon
R4-1901333, Discussion on BS RF requirements for NR-U, Nokia, Nokia Shanghai Bell
This document summarizes the way forward on NR-U BS RF requirements.
NR-U wideband carrier operation is not covered in this WF.

## Slide 3: Way forward (1/2)
1. NR FR1 BS RF core specification requirements in TS 38.104 can be used as a baseline for NR-U BS RF requirement.
2. Following NR FR1 transmitter requirements could be reused by NR-U:
  BS output power,
  RE power control dynamic range,
  Transmitter transient period,
  Frequency error, Modulation quality,
  Time alignment error,
  Transmitter spurious emission,
  Transmitter intermodulation.
3. 35dB ACLR requirements can be reused for NR-U single carrier <=20MHz and CA.
4. LAA Operating band unwanted emission mask can be reused by NR-U single carrier <=20Mhz and CA.
5. For NR-U for channel bandwidths above 20 MHz OBUE masks should be considered.

## Slide 4: Way forward (2/2)
6. Following NR FR1 receiver requirements can be reused for 5GHz NR-U:
  In-band blocking,
  Out-of-band blocking,
  Receiver spurious emission,
  Receiver general intermodulation.
7. There will be no narrowband blocking and narrowband intermodulation requirement for NR-U.
8. For NR-U the need for new reference measurement channels (FRCs) should be considered.
9. For NR unlicensed band(s) above 6 GHz, extension of BS Tx and RX requirements from below 6 GHz shall be verified.