## Slide 1: Way forward on HST enhancement for RRM
Huawei, HiSilicon
3GPP TSG-RAN4 Meeting #90
Athens, Greece, 25 Feb – 1 Mar, 2019
R4-1902520
Document for: Approval

## Slide 2: Background: objectives in new WID: Further performance enhancement for LTE in high speed scenario (RP-181482)
The core part of this WI include
Extend the RRM/demodulation enhancement to CA in release 14 HST scenario [RAN4/RAN2]
  At least, extend Rel-14 RRM/demodulation enhancement to CA case
The following new scenario are considered for non-CA case [RAN4]
  The target speed is 500km/h
  SFN scenario defined in TS36.101 and TR36.878 with bidirectional coverage for tunnel and open space
  SFN scenario defined in TS36.878 with unidirectional coverage for tunnel and open space
    More discussion on how to specify the general unidirectional antenna pattern
  In addition to SFN scenarios, other deployment scenarios are not precluded
Evaluate the downlink and uplink demodulation performance under the above scenarios, using the existing LTE CRS/DMRS, and study possible enhancements of the downlink and uplink demodulation under those scenarios, aiming to provide inputs to RAN2 if needed [RAN4]
  New or modified physical layer reference signals shall not be considered
  Change for PRACH shall not be considered
  The maximum Doppler shift supported by the LTE CRS/DMRS transmission schemes is to be determined by RAN4
  If RAN4 identifies the necessity for enhancements, define relevant signaling support [RAN4/RAN2]
Investigate the RRM measurement performance in the high speed scenario [RAN4]
  If RAN4 identifies the necessity for enhancements, define relevant signaling support [RAN4/RAN2]
Investigate the robustness for RLM in the high speed scenario [RAN4]
  If RAN4 identifies the necessity for enhancements, define relevant signaling support [RAN4/RAN2]

## Slide 3: Way Forward on RRM requirements
Enhanced intra-frequency cell identification and measurement period are defined for SCC
  Using the existing highSpeedEnhancedMeasFlag or introducing new IE is FFS
  How to define the UE capability for enhanced intrafrequency cell identification and measurement period for SCC is FFS
  Note: it is expected to send LS to RAN2 in next meeting (RAN4#90bis)
RAN4 RRM shall focus on the following requirement impacts for HST feature:
  Cell reselection requirements in idle mode
  Measurement requirements in connected mode (single carrier)
    DRX
    Non-DRX
  Measurement requirements of SCC with both active Scells and deactivated SCells
  RLM
  Measurement accuracy
  FFS: UE Tx timing, i.e., Tq

## Slide 4: Way Forward on RRM requirements
High speed CA scenarios
  CA scenario 1 is a typical deployment in high speed scenario
  Whether scenario 4/5 are implemented needs operator input
  Note: CA scenarios are listed in R4-1901531
For high speed scenarios, ISD requires operator input for typical setting/range
Scenario | Description
1 | F1 and F2 cells are co-located and overlaid, providing nearly the same coverage. Both layers provide sufficient coverage and mobility can be supported on both layers. Likely scenario is when F1 and F2 are of the same band, e.g., 2 GHz, 800 MHz, etc. It is expected that aggregation is possible between overlaid F1 and F2 cells.
2 | F1 and F2 cells are co-located and overlaid, but F2 has smaller coverage due to larger path loss. Only F1 provides sufficient coverage and F2 is used to improve throughput. Mobility is performed based on F1 coverage. Likely scenario when F1 and F2 are of different bands, e.g., F1 = {800 MHz, 2 GHz} and F2 = {3.5 GHz}, etc. It is expected that aggregation is possible between overlaid F1 and F2 cells.
3 | F1 and F2 cells are co-located but F2 antennas are directed to the cell boundaries of F1 so that cell edge throughput is increased. F1 provides sufficient coverage but F2 potentially has holes, e.g., due to larger path loss. Mobility is based on F1 coverage. Likely scenario is when F1 and F2 are of different bands, e.g., F1 = {800 MHz, 2 GHz} and F2 = {3.5 GHz}, etc. It is expected that F1 and F2 cells of the same eNB can be aggregated where coverage overlaps.
4 | F1 provides macro coverage and on F2 Remote Radio Heads (RRHs) are used to improve throughput at hot spots. Mobility is performed based on F1 coverage. Likely scenarios are both when F1 and F2 are DL non-contiguous carrier on the same band, e.g., 1.7 GHz, etc. and F1 and F2 are of different bands, e.g., F1 = {800 MHz, 2 GHz} and F2 = {3.5 GHz}, etc. It is expected that F2 RRHs cells can be aggregated with the underlying F1 macro cells.
5 | Similar to scenario #2, but frequency selective repeaters are deployed so that coverage is extended for one of the carrier frequencies. It is expected that F1 and F2 cells of the same eNB can be aggregated where coverage overlaps.