## Slide 1: Way forward on open issue for FR2 RRM testing
Qualcomm Incorporated, […]
3GPP TSG-RAN WG4 #90 Meeting
Athens, Greece, 25th Feb. – 01st March, 2019
Document for : Approval
R4-1902525

## Slide 2: Background
In RAN4#89 meeting, the following agreements on test methods for FR2 RRM testing were made in [1].
During RAN4#90 meeting the following issues were discussed on FR2 RRM testing [2-10]:
  Antenna gain difference between fine and rough beam for 1AoA
  Antenna gain difference for dual directions within 1 beam for 2AoA
  Noc setup and SNR/SINR range
  Test setup
This document summarizes the way forward on FR2 RRM testing.

## Slide 3: Antenna gain difference for 1AoA
The following assumptions on antenna gain difference can be used for 1AoA RRM testing:
  For peak beam direction
    Antenna gain difference for PC3 Y=7dB
      Y is the antenna gain difference between the fine and rough beams in the RX beam peak direction. (Y is not band dependent)
  For non-peak beam direction
    Antenna gain difference for PC3 Z will be further studied in the RAN4#90bis meeting.
      Z is the antenna gain difference between “fine” and “rough” RX beams within 50% percentile EIS directions (Z is not band dependent).
      Companies are encouraged to provide analysis on this, and define Z at RAN4#90bis meeting.
    Further evaluate how panel selection may impact the Z value, e.g., how to share 24 samples for FR2 measurement for PC3 UE
  Further evaluate the antenna gain difference between the rough and fine beams (Y and Z values) for the UE PC 1, 2 and 4.

## Slide 4: Antenna gain difference for 2AoA
Further study antenna gain difference for dual directions within 1 beam for 2AoA
  Companies are encouraged to bring analysis on antenna gain difference for PC3 UE fine/rough beams and assess the gain difference dependency on relative probe spacing.
The following assumptions on antenna gain difference can be used for 2AoA RRM testing:
  PC3 UE with fine beams
    The maximum gain difference D for dual directions within 1 fine beam can be derived by the following options:
    Option 1: D=X
      X is the difference between the peak EIS and [50]%-tile EIS (X is band dependent)
    Option 2: D=0dB
  PC3 UE with rough beams
    The maximum gain difference D for dual directions within 1 rough beam can be derived by the following options:
    Option 1: D=X+Z-Y
      X is the difference between the peak EIS and [50]%-tile EIS (X is band dependent), Y and Z are defined in the page 3 (Y and Z are not band dependent).
    Option 2: D=0dB

## Slide 5: Noc setup for multi-band device
For PC3 multi-band devices, the Noc power level shall increase by multi-band relaxation defined in TS 38.101-2 Table 6.2.1.3-4.
  AoA fromTest cases with peak beam direction:
    NocMB = NocSingle + ΣMBP
  AoA fromTest cases with non-peak beam direction:
    NocMB = NocSingle + ΣMBS
  NocSingle is derived by assuming UE supports single band.

## Slide 6: Test setup
For 2AoA cases,
  TDM transmission approach for 2 probes is allowedused.
  For 2AoA cases, simultaneous transmission approach for 2 probes will be further studied.
The antenna gain difference defined in this WF can be used to derive the FR2 RRM side condition.

## Slide 7: Reference
[1] R4-1816742 “WF on test methods for FR2 RRM testing”, Qualcomm Incorporated, AT&T, Docomo, Verizon, Telstra, Keysight, Anritsu, Rohde & Schwarz, RAN4 #89, November 2018
[2] R4-1900123 “Remaining details of NR FR2 RRM test methods”, Intel
[3] R4-1900504 “On RRM AoA Selections”, Keysight
[4] R4-1900595 “Wide Beams and Narrow Beams in FR2”, Qualcomm Incorporated
[5] R4-1900752, “Noc level definition and SNR range for 1AoA RRM testing”, Qualcomm Incorporated
[6] R4-1900753, “Noc level definition and SINR range for 2AoA RRM testing”, Qualcomm Incorporated
[7] R4-1901654, “NR FR2 2AoA RRM test method” Intel
[8] R4-1900522, “Gain difference between rough and fine Rx beams in FR2 RRM testing”, MediaTek
[9] R4-1900967, “Further details of OTA setup for NR RRM”, Ericsson
[10] R4-1900080, “UE parameters for FR2 UE RRM test cases in 38.133”, ANRITSU