## Slide 1: Way Forward on TCI State Switching Requirements
Intel Corporation
3GPP TSG-RAN WG4 Meeting #90bis R4-1902938
Xi’an, China, 8 - 12 April, 2019

## Slide 2: Background
In RAN4#90 the following agreements were made:
  TCI state switching for RRM requirements shall be considered for:
    TCI state switching for PDSCH based on DCI within the active TCI state set within the RRC configured TCI state set
    TCI state switching for PDCCH based on MAC CE within the RRC configured TCI state set
  RRC based TCI state switching is FFS
  Whether Known/ Unknown condition is needed or not shall be FFS.

## Slide 3: Way Forward
Proposal #1: Known TCI state is applicable only for UE supporting Power Class 1. For UE supporting Power class 2/3/4 only unknown TCI state is applicable.
Proposal #2: Define target TCI state as known if the UE has reported the L1-RSRP for it within [80] ms for UE supporting Power class 1
Proposal #3: The delay for MAC CE based TCI state switch for PDCCH starts from the slot with PDSCH carrying the activation command to the slot when PDCCH can be received based on new TCI state
Proposal #4: The switching delay for MAC-CE based TCI state shall include time for time/frequency offset acquisition
Proposal #5: The delay for MAC CE based TCI switch for PDCCH to a known TCI state is defined as TTCI-Switch, MAC-CE, known = THARQ + TACQ-TO-FO + 3ms
Proposal #6: Define time for Rx beam acquisition as TACQ-RxBeam = N*max(TCSI-RS,Rep-ON , n) , where N=8 if maxNumberRxBeam not indicated by UE; N=ceil(maxNumberRxBeam/#CSI-RS resources in Set) if maxNumberRxBeam is indicated by UE
Proposal #7: The delay for MAC CE based TCI switch for PDCCH to an unknown TCI state is defined as TTCI-Switch, MAC-CE, unknown = THARQ + max(TACQ-RxBeam , TACQ-TO-FO ) + 3ms
Proposal #8: DCI based TCI state/ beam switch delay for PDSCH starts from the end of last symbol of PDCCH to beginning of the first symbol of PDSCH
Proposal #9: The delay for DCI based TCI switch for PDCCH to a known TCI state is defined as TTCI-Switch, DCI, knownTCI, knownTOFO = UE Capability for timeDurationForQCL for case when TO/FO acquisition time is not needed and as TTCI-Switch, DCI, knownTCI, unknownTOFO = TACQ-TO-FO + UE Capability for timeDurationForQCL when additional time for when TO/FO acquisition is needed
Proposal #10: For DCI based TCI state switch to unknown TCI state – Option 1: No delay requirements are defined (or) Option 2: The delay is defined as TTCI-Switch, DCI, unknownTCI, knownTOFO = TACQ-RxBeam + UE Capability for timeDurationForQCL for the case when TO/FO acquisition time is not needed and as TTCI-Switch, DCI, unknownTCI, unknownTOFO = max(TACQ-RxBeam , TACQ-TO-FO )+ UE Capability for timeDurationForQCL when additional time for when TO/FO acquisition is needed
Proposal #11: For RRC based TCI state switch, no delay requirements are introduced