## Slide 1: Way Forward on AoA for FR2 RRM Testing
Qualcomm Incorporated, KDDI, Verizon
R4-1904064
3GPP TSG-RAN WG4 RAN4#90 Bis
Xi’an, China, April 8th – 12th, 2019

## Slide 2: Background
Following setups are candidates for FR2 RRM testing:
  Setup #1: Single AoA setup with signal arriving in the peak direction of Rx antenna beam
  Setup #2: Single AoA setup with signal arriving not in the peak direction of Rx antenna beam
  Setup #3: Dual AoA setup
The choice of angle of arrival is straightforward for Setup#1 but is still under discussion for Setup #2 and Setup #3
RRM requirements apply over all directions(any angle of arrival) that fall within the top 50%-ile of spherical EIS
It is important to test that UEs meet the requirements over multiple directions

## Slide 3: Choice of AoA for Setup#2
The AoA should be chosen randomly from the applicable directions(top 50%-ile of spherical EIS)
The AoA should be changed for each test run
The minimum angular distance between test runs should be 20 degrees

## Slide 4: Choice of AoA for Setup#3
The AoA pair should be chosen randomly from the applicable directions(top 50%-ile of spherical EIS)
The pair of AoAs should be changed for each test run. The TE should pick the AoA and UE position such that all candidate AoA pairs from the set of applicable pairs for the respective power class are used and different UE positions are tested
  Set of applicable AoA pairs for PC3: 30°, 60°, 90°, 120° and 150°
  Detailed algorithm can be left to RAN5, see next slide for a possible algorithm

## Slide 5: Example for how to choose the AoA and UE position for Setup #3
1. Find a position with AoA 30 degrees, position the UE, execute 1 run
2. Find a position with AoA 60 degrees, position the UE, execute 1 run
…
5. Find a position with AoA 150 degrees, position the UE, execute 1 run
6. go back to Step 1.
If no position can be found then TE skips to the next steps until test is finalized or there are no position/AoA pairs available and TE goes back to the position used in the first run.