## Slide 1: 3GPP TSG-RAN WG4 Meeting #90bis Xi’an, China, 8th – 12th April, 2019
Ericsson
Way forward on Rel-16 NB-IoT RRM enhancement
R4-1904581

## Slide 2: Group WUS
RAN4 shall wait for further RAN1 progress on release 16 WUS design work to decide whether release 15 WUS requirements are reusable.
  Based on current design, it likely possible to apply Rel-15 legacy WUS requirements on Rel-16 group WUS.

## Slide 3: Preconfigured UL resource
RAN4 shall define requirements for following options to validate TA:
  Serving cell change
  Time alignment timer (TAT)
  serving cell RSRP change
PUR transmissions/resources should be not allowed during the time (T0) UE is out of synchronization in IDLE mode (e.g. between PTWs).
  Value of T0 is FFS
PUR transmissions are allowed only when maximum serving cell change is less than RSRP and received TA is less than TAmax.
  Values of RSRP and TAmax are FFS

## Slide 4: Multicarrier operation
For the MSG3-based DL channel quality reporting for non-anchor carrier, RAN4 reuses the framework of anchor carrier DL channel quality reporting specified in Rel-14.
RAN4 waits for the RAN1 decision on the reported values for CQI-NPDCCH-Short-NB used for non-anchor channel quality reporting.
Serving cell non-anchor carrier measurements are feasible under following scenarios:
  the relaxed cell monitoring criterion is met,
  transmit power difference of the signals/channels between anchor- and non-anchor carriers is known,
  UE is not configured with any positioning measurements.