## Slide 1: WF for requirement SNR derivation procedure
R4-1904713
Document for: Approval
3GPP TSG-RAN WG4 RAN#90Bis
Xi’an, China, 8th – 12th April, 2019
Agenda: 6.12.2.1
Nokia, Nokia Shanghai Bell, ZTE, Ericsson, […]

## Slide 2: Background
This WF captures the finalization of the agreements made in:
  R4-1816594, WF for test case SNR derivation procedure, RAN4#89.
We take into account the details added in:
  R4-1903278, Further discussion on deriving performance requirements, RAN4#90b.
We take into account the discussion and agreements in:
  R4-1904712, Ad Hoc minutes for NR BS demodulation, RAN4#90b.
  Which also prompted the creation of this WF:
      Nokia will apply for a new WF to capture the updated procedure for the derivation of the minimum performance requirements.

## Slide 3: Updated Selection and Derivation Procedure
Procedure to derive the performance requirements:
  – Only inputs that consist of a pair of ideal and impaired results can be taken into account.
  – If the ideal span <= [2]dB:
    • The AVERAGE impairment results can be used for the performance requirement with [] in the draftCRs/CRs;
  – Else if the ideal span is larger than [2]dB:
    • The results farthest from the AVERAGE value is taken out for the AVERAGE and SPAN re-calculation until the ideal span is <=2dB but still with at least 3 companies’ results available:
      – The ultimate AVERAGE impairment results with corresponding ideal span <=2dB can be used for performance requirement with [] in the draftCRs/CRs.
    • Otherwise put TBD for the related performance requirements.
  – If the span of the impairment results after removal the outliers (if any) are larger than 4dB, then the procedure cannot be applied, related performance requirement remain TBD.

## Slide 4: Procedure Flow Diagram