## Slide 1: Way forward on NR UE PDSCH demodulation requirements and General aspects
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #90bis
Xi’an, China, 8 April – 12 April 2018 Agenda Item: 6.12.1.2
R4-1904754

## Slide 2: TDD requirements
      Issue 1: TDD UL/DL configuration {DDDSUU}+{DDDD} for FR1 requirements
  Previous agreement:
    Option 1: No introduce test case(s) for TDD DL/UL configuration: {DDDSUU}+{DDDD} under 30kHz in Rel-15
    Option 2: Introduce one additional test case for {DDDSUU}+{DDDD} for PDSCH demodulation
  Proposal:
    Modify the following tests: 5.2.2.2.1, 2-2 and 5.2.3.2.1, 2-2 (20 MHz/30 kHz, 64QAM, Rank 2)

## Slide 3: TDD requirements
      Issue 2: TDD requirements for second priority TDD patterns
  NO more TDD UL-DL patterns will be introduced in Rel-15 except below patterns.
  Proposal:
    Introduce one test case for the following UL-DL patterns:
      FR1:
        FFS for Case 1: DDSU, S=10D:2G:2U
        FFS for Case 2: DSSU, S1=10D:2G:2U, S2=12D:2G
        FFS for Case 3: DSUU, S = 12D:2G
      FR2:
        FFS for Case 1: DSUU, S=12D:2G
    Baseline settings for agreed test cases if any:
      FR1: Section 5.2.2.2.1, test 1-1 and Section 5.2.3.2.1, test 1-1
      FR2: Section 7.2.2.2.1, test 1-1
  Companies are encourage to bring both alignment and impairment results for agreed test cases if any in RAN4#91 meeting.
Notes: Huawei: we already have timelines and agreements for scope Rel-15.
Intel: I have concern for timeline? What’s the plan?
NTT DoCoMo: SU not work, so we would like to replace SU using this DSUU.

## Slide 4: PDSCH requirements
      Issue 1: HST requirements
  Channel model:
    Use single tap channel model with the following parameters for Rel-15
    HST-SFN will not introduced in Rel-15.
  Simulation assumptions:
    Antenna assumptions: 1Tx with 2Rx and 4Rx (static channel matrix)
    Channel bandwidth and SCS:
      FDD: 10 MHz, SCS 15 kHz
      TDD: 40 MHz, SCS 30 kHz (7D1S2U, S = 6D:4S:4U)
    PDSCH mapping: Type A, Start symbol 2, Duration 12
    DMRS configuration: Type 1, Single symbol, 2 additional DMRS
    TRS configuration: 10ms, 2 slots, offset 1
    FRC: 16QAM Rank 1 (MCS 13)
    Baseline receiver assumption to define requirements: TRS based on tracking
      Note: No restrictions on actual UE implementation
Parameter | 
Ds | 300 m
Dmin | 2 m
v | 300 km/h
fd | 750 Hz for 15 kHz SCS test and 1000 Hz for 30 kHz SCS test

## Slide 5: PDSCH requirements
      Issue 2: Dynamic TDD DL-UL configuration test
  Previous agreement:
    Use dynamic UL/DL determination for some existing PDSCH demodulation test case(s)-both FR1 and FR2
      Change one existing test case for FR1
      Change one existing test case for FR2
  Proposal:
    Use dynamic TDD UL/DL determination for Test 1-1 for FR1 TDD (Sections 5.2.2.2.1 and 5.2.3.2.1) and Test 1-1 for FR2 TDD (Section 7.2.2.2.1)

## Slide 6: PDSCH requirements
      Issue 3: TRS configuration for FR2
  Previous agreement
    Option 1: No change: Use 2 slots TRS configuration for Rel-15 Normal and SDR requirements (Intel, QC)
    Option 2: Replace FR2 Test 1-1 with TRS configuration: 20ms with 1 slot and OFDM symbol 6, 10 (NTT DoCoMo)
      Option 2a: 2 additional DMRS
      Option 2b: 1 additional DMRS
    Bring evaluation results for option 2 and decide among above two options in next meeting
  Proposal:
    Use 2 slots TRS with periodicity 20ms and symbols allocation {3, 7}
    Modify TRS configuration for the following tests:
      Section 7.2.2.2.1, Test 1-1, TRS offset: 80, 81 slots
      Section 7.2.2.2.1, Test 1-2, TRS offset: 82, 83 slots

## Slide 7: PDSCH requirements
      Issue 4: PTRS power ratio configurations
  epre-Ratio = 0
      Issue 5: Parameters of PDCCH for PDSCH and CSI test cases
  Add additional PDCCH parameters:
    PDCCH interleaving = Non-interleaved
      Issue 6: Update of BWP configuration for PDSCH and SDR tests
  Revise “First PRB” by “RB offset”
  Introduce parameters related to SCS-SpecificCarrier: offsetToCarrier and subcarrierSpacing

## Slide 8: PDSCH requirements
      Issue 7: NR PDSCH mapping for LTE-NR coexistence tests for slots overlapped with LTE PSS/SSS/PBCH
  Option 1: No NR PDSCH mapping in slots overlapped with LTE PSS/SSS/PBCH (Ericsson, Intel, QC, Huawei)
  Option 2: using rate matching for LTE PSS/SSS/PBCH
      Issue 8: Requirements applicability for mandatory with capability features
  Option 1: Define applicability for all mandatory with capability features