## Slide 1: Way Forward on AoA for FR2 RRM Testing for PC3
Qualcomm Incorporated, KDDI, Verizon, Vodafone, T-Mobile USA, Samsung, NTT Docomo
R4-1904770
3GPP TSG-RAN WG4 RAN4#90 Bis
Xi’an, China, April 8th – 12th, 2019

## Slide 2: Background
Following setups are candidates for FR2 RRM testing:
  Setup #1: Single AoA setup with signal arriving in the peak direction of Rx antenna beam
  Setup #2: Single AoA setup with signal arriving not in the peak direction of Rx antenna beam
  Setup #3: Dual AoA setup
The choice of angle of arrival is straightforward for Setup#1 but is still under discussion for Setup #2 and Setup #3
RRM requirements apply over all directions (any angle of arrival) that fall within the specified %-ile of spherical EIS
It is important to test that UEs meet the requirements over multiple directions

## Slide 3: Choice of AoA for Setup#2
Setup#2 will be further split in Setup#2a and Setup#2b
Setup#2a:
  The AoA should be chosen randomly from the applicable directions (top specified %-ile of spherical EIS)
  The AoA is fixed between test iterations
Setup#2b:
  The AoA should be chosen randomly from the applicable directions (top specified %-ile of spherical EIS)
  The AoA shall be changed for each test iteration
  The details on how to change the AoA will be decided by RAN5

## Slide 4: Choice of AoA for Setup#3
The AoA pair should be chosen randomly from the applicable directions(both directions have to be within the top specified %-ile of spherical EIS)
  The TE should pick the AoAs such that the relative AoA offset is from the set of applicable AoA offsets for the respective power class
    Set of applicable AoA offsets for PC3: 30°, 60°, 90°, 120° and 150°
The relative AoA offset should be changed for each test iteration
  Details on how to change the relative AOA offset will be decided by RAN5