## Slide 1: Way forward on BS demodulation requirement for HST enhancement
3GPP TSG-RAN WG4 Meeting #90bis
Xi'an, China, 8th – 12th April 2019
Agenda item: 7.15.5 BS Demodulation [LTE_high_speed_enh2-Perf]
Document for: Approval
R4-1904793
NTT DOCOMO, INC., …

## Slide 2: Background
In RAN#80, the new WI on further performance enhancement in high speed scenario was approved [1].
In RAN4 #90, the work plan [2] and WF on BS demodulation [3] were approved.
In RAN4 #90bis, BS performance requirements for high speed were discussed based on contributions [4-6]

## Slide 3: WF on PUSCH for HST
The following deployment scenario are considered:
  Open space
    Bi-directional (1st priority)
    Uni-directional
  Tunnel for multi-antennas
    Bi-directional (1st priority)
    Uni-directional
BS-Railway track distance (Dmin) and Initial distance of the train from BS (Ds/2):
  Same as existing HST scenario 1 for open space and 3 for tunnel
  Other options are not precluded

## Slide 4: WF on PUSCH for HST for evaluation (not for requirement)
Deployment scenarios and related parameters (e.g., Ds, Dmin, fd) will be decided based on evaluation results. The following parameters should be considered in the evaluation.
The requirements will be specified based on the outcome of simulation.
Parameter | Value |  |  | 
 | Open space |  | Tunnel for multi-antennas | 
 | Bi-directional (1st priority) | Uni-directional | Bi-directional (1st priority) | Uni-directional
Ds | 1000 m |  | 300 m | 
Dmin | 50 m |  | 2 m | 
v | 500 km/h |  | 500 km/h (Other options are not precluded) | 
fd | 2200Hz 1945Hz (1st priority for initial simulation) 1750Hz 1600Hz Any values in between acceptable are not precluded |  |  | 

## Slide 5: WF on PUSCH for HST for evaluation (not for requirement)
Initial simulation assumption for just information
Parameters | Unit | Values
Bandwidth | MHz | 10
MCS for PUSCH |  | QPSK 1/2 16QAM 3/4
Propagation condition and correlation matrix |  | Reference to the previous slide
Antenna configuration |  | 1x2
Reference receiver |  | MRC
Noise estimation |  | Practical
Time and frequency track |  | Practical

## Slide 6: WF on PUSCH for UL timing adjustment
PUSCH requirements for UL timing adjustment considering 500km/h UE velocity
  Option 1: Introduce the following moving propagation scenario
  Option 2: Not introduce new moving propagation scenario
Companies are encourage to provide the performance impact compared to the existing moving propagation scenario
Parameter | Proposed scenario [3] | Existing moving propagation scenario for HST (Reference)
Channel model | Stationary UE: AWGN Moving UE: AWGN | Stationary UE: AWGN Moving UE: AWGN
UE speed | 500 km/h | 350 km/h
CP length | Normal | Normal
A | 10 ms | 10 ms
Dw | [0.18] s-1 | 0.13 s-1

## Slide 7: WF on PUSCH and PUCCH for multipath fading
PUSCH for multipath fading
  Option 1: Introduce the requirements with higher Doppler spread above 600Hz
  Option 2: Not introduce new requirements
PUCCH for multipath fading
  Option 1: Introduce the requirements with higher Doppler spread above 300Hz
  Option 2: Not introduce new requirements
Companies are encouraged to provide the practical deployment with multipath fading scenario considering high velocity about 500km/h.

## Slide 8: WF on PRACH restricted set B
After defining maximum Doppler shift, the necessity of a new test case for PRACH restricted set B would be discussed.

## Slide 9: Reference
[1] RP-181482, “New Work Item on Further performance enhancement for LTE in high speed scenario”, SoftBank, RAN#80
[2] R4-1900804, “Work plan for LTE high speed in Rel.16”, NTT DOCOMO, INC., Huawei, HiSilicon, RAN4#90
[3] R4-1902522, “Way Forward on BS demodulation scenarios and requirements for HST”, Ericsson, NTT Docomo, RAN4#90
[4] R4-1903574, “BS demodulation for LTE high speed in Rel.16”, NTT DOCOMO, INC., RAN4#90bis
[5] R4-1903632, “BS performance requirements for HST at 500 km/hr”, Ericsson, RAN4#90bis
[6] R4-1903369, “View on BS performance requirements for high speed scenario in LTE Rel- 16” Samsung, RAN4#90bis
[7] R4-1904380, “On Maximum Doppler shift in uplink for Rel-16 HST at 500 km/h”, Nokia, Nokia Shanghai Bell, RAN4#90bis
[8] R4-1904382, “On Rel-16 HST scenarios for BS demodulation“, Nokia, Nokia Shanghai Bell, RAN4#90bis