## Slide 1: WF on Noc, Es power setting
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #90bis
Xi’an, China, 8 April – 12 April 2018 Agenda Item: 6.12.1.2
R4-1904794

## Slide 2: Issue #1: Per band or fixed values Noc and Es value
Previous agreement
  Use a per-band Noc and Es power level
Current options
  Option 1: per band
  Option 2: generic values (worst values)
    Noc level = [-136] dBm/Hz
      Band 12, 15 MHz, 30 kHz: PnoiseRF = -152 dBm/Hz
      Noc = -152 + 16 = -136 dBm/Hz
    Es level = [-117] dBm/Hz
      Band 12, 15 MHz, 30 kHz: Es = -152 + 35 = -117 dBm/Hz
Proposal
  Send LS to RAN5 to clarify what is the difference between option 1 and option 2 from RAN5 point of view (i.e. check if it is possible or not to have band agnostic conformance tests for Option 1)

## Slide 3: Issue #2: Noc and Es calculation
      Noc calculation
  Previous agreement for Noc calculation
    Noc (dBm/Hz) = PNoiseRF (dBm/Hz) + X dB
    X value
      Option 1: X = [16 ]dB
  Proposal:
    X = 16 dB
      Es calculation
  Previous agreement for Noc calculation
    Noc (dBm/Hz) = PNoiseRF (dBm/Hz) + X dB
    X value
      Option 1: X = [35 ]dB
  Proposal:
    X = 35 dB

## Slide 4: Issue #3: PnoiseRF calculation
General equation
  PnoiseRF (dBm/Hz) = REFSENS – 10*log(BW) + Diversity Gain – SNRREFSENS
    BW: should followed the assumption used in REFSENS requirements to maintain PSD of noise floor, BW = NRBs*SCS*12
    Using 2Rx REFSENS levels to generate noise floor with assumption 3dB diversity gain for both 2Rx and 4Rx test cases
    Same Noc values per Rx port applied for 2Rx and 4Rx
Handing of tests for UE supporting CA
  Option 1: Applying ΔRIB relaxation depending on scenario
  Option 2: No need to consider this impact
  Option 3: Apply fixed relaxation value [1] dB for all scenarios
Handling of CA tests
  Option 1: Use individual values for each CC
  Option 2: Select the maximum values applied for all CC

## Slide 5: Issue #4: SNR upper bound in FR2
RAN4 does not put any limit on the upper SNR into the specification, It is up to each test system implementation whether a test case can be performed or not.
Define methodology for testable baseband SNR range in TR 38.810 for scenarios without external noise sources