## Slide 1: WF on analysis of V2X RRM requirement
CATT, LG Electronics
3GPP TSG-RAN WG4 #90bis R4-1904828
Xi’an, China, 8th Apr – 12th Apr, 2019

## Slide 2: Background
5G V2X WID(RP-190766)
  The objective of this work item is to specify radio solutions that are necessary for NR to support advanced V2X services (except the remote driving use case which was studied in TR 38.824) based on the study outcome captured in TR 38.885.
    Sidelink synchronization mechanism as per the study outcome [RAN1, RAN2]
      Procedures selecting synchronization reference
      S-SSB and procedures to transmit and receive it, including when GNSS and gNB/eNB are unavailable
      Use of RS for sidelink synchronization if specification impact is identified
TR38.885
  SL synchronization sources are GNSS, gNB, eNB, NR UE, each associated with a synchronization priority
Based on 5G V2X WID, GNSS, gNB, eNB and NR UE are defined as SL synchronization sources.

## Slide 3: Background
Agreement in RF session (R4-1905211)
  3.3 Time Error in LS
    gNB based TE at FR2 : follow specified Timing Error in TS38.133
    GNSS based TE:
      Option1:Time error is 12*64Tc for 15kHz. Other cases are FFS.
      Option2:Time error is 12*64Tc for all SCS.
  Agreement:
    GNSS based synch source: option1 is acceptable as starting point, subject to change during RAN4 WI phase based on further analysis

## Slide 4: WF on analysis of V2X RRM requirement for RAN4#91
RAN4 starts to study V2X UE sidelink transmit timing requirement for different synchronization reference source, e.g. GNSS, gNB/eNB and Sync Ref UE
  RAN4 is subject to follow RAN1/2’s decision for synchronization reference source during the discussion in future meeting
Other RRM requirements is not precluded if identified.