## Slide 1: WF for BS TAE and MRTD specification for NR Rel-15
Ericsson
3GPP TSG-RAN4 Meeting #90bis
Xian, China, 8-12 April 2019
R4-1904851

## Slide 2: BS TAE
Decouple the BS TAE discussions for FR1 and FR2.
Consider the following:
  BS TAE for FR1 Intra-band non-contiguous CA to be [3]us
    ZTE, HW, Samsung, CATT: 3us
    Ericsson, Intel, MediaTek, Nokia, Qualcomm: 260ns
  BS TAE for FR2 Intra-band non-contiguous CA to be [3]us
    ZTE, HW: 3us
    Nokia, Ericsson, MediaTek, Intel, Samsung: 260ns
    Qualcomm: 130ns

## Slide 3: MRTD specification for intra-band NC CA
Define the MRTD specification as follows in Section 7.6.4, TS 38.133:
Frequency Range | Maximum receive timing difference (µs)
FR1 | [3/0.26]
FR2 | [3/0.26/0.13]
Table 7.6.4-1: Maximum receive timing difference requirement for intra-band non-contiguous NR carrier aggregation

## Slide 4: MRTD specification for intra-band synchronous EN-DC
Define the MRTD specification as follows in Section 7.6.3, TS 38.133:
Sub-carrier spacing in E-UTRA PCell (kHz) | DL Sub-carrier spacing in PSCell (kHz) Note1 | Maximum receive timing difference (µs)
15 | 15 | 3, [0.26]2
15 | 30 | 3
15 | 60 | 3
NOTE 1: DL Sub-carrier spacing is min{SCSSS, SCSDATA}. NOTE 2: This is applicable for UEs that is only capable of handling a single UL timing for E-UTRA and NR cell (ul-TimingAlignmentEUTRA-NR). |  | 
Table 7.6.3-1 Maximum receive timing difference requirement for intra-band synchronous EN-DC