## Slide 1: Way forward on NR demodulation scope for Rel-16
China Telecom,…
3GPP TSG-RAN WG4 Meeting #91
Reno, Nevada, US, May 13 - 17, 2019
Agenda: 6.12
R4-1905335

## Slide 2: WF (1/3)
PDSCH demodulation requirements for the following scenarios
  Additional TDD configurations based on operator request, including {DDSU} with S=10D:2G:2U for FR1 and {DSUU} with S=12D:2G for FR2
  with 2 TCI states
  Missing set of channel bandwidth and subcarrier spacing in Rel-15 if any
  Additional channel model, including TDL-D and TDL-E
  PDSCH requirements with the presence of co-channel intra-cell inter-user interference
    MMSE receiver can be considered as reference receiver

## Slide 3: WF (2/3)
Interference-aware receivers for FR1
  BS side:
    PUSCH requirements with enhanced receivers for handling co-channel inter-cell interference
      LMMSE-IRC or interference pre-whitening can be considered as reference receiver
    Study whether to introduce PUSCH requirements with enhanced receivers for handling co-channel intra-cell inter-stream/user interference
      For intra-cell inter-user interference handling, hard-IC (hard L-CWIC) and hybrid-IC (mixing hard-IC and soft-IC) receivers as defined in NOMA TR 38.812 can be considered as reference receiver
  UE side:
    PDSCH requirements with enhanced receivers for handling co-channel inter-cell interference
      LMMSE-IRC or interference pre-whitening can be considered as reference receiver
    Study whether to introduce PDSCH requirements with enhanced receivers for handling co-channel intra-cell intra-stream interference for SU-MIMO
      Up to 4 transmission layers for SU-MIMO are to be considered, and parallel - soft IC can be considered as reference receiver
    Study whether to introduce PDSCH requirements with enhanced receivers for handling co-channel intra-cell inter-user interference for MU-MIMO

## Slide 4: WF (3/3)
CA and DC requirements:
  UE side: PDSCH normal demodulation requirements and CA/DC specific requirements, including soft buffer management, power imbalance.
PDSCH and CSI requirements with the number of Tx ports larger than 8 and upper to 32
Release independent aspect for the demodulation requirements for UE side

## Slide 5
Thanks!